## Slide 1: Ph.D. Thesis Defense: Matching Theory Framework for 5G Wireless Communications
Yunan Gu
Advisor: Zhu Han
University of Houston
Electrical and Computer Engineering Department
Date: 11/29/2016

## Slide 2: Outline
University of Houston
Introduction
  Matching theory basics
Wireless-Oriented Matching Applications:
  Dynamic stability in LTE-Unlicensed
  Content sharing in LTE V2X communications
  Device-to-device (D2D) communications
  Facebook content caching
  Fog Computing
  Wireless network virtualization
  Mobile crowd sensing
Future Works
  Dynamic stability in LTE V2X communications
  Stable multiple activity matching in HetNets
Conclusion
  Motivations

## Slide 3: 5G features
University of Houston
Cited from “5G Use Cases and Requirements,” a white paper from Nokia.
5G features:
  Higher data rates
  Reduced end-to-end latency
  Higher energy efficiency
  Better network coverage
  Enhanced security
  Ultra reliability
  and so on…

## Slide 4: 5G key technologies
University of Houston
New paradigms:
  Device-to-device (D2D) communication
  Network virtualization
  LTE-Unlicensed
  Small cell (SC) deployment
  Cloud-based radio access network (C-RAN)
  Massive multiple-input multiple-output (MIMO)
  Internet of Things
  And so on…
Cited from: http://www.eurescom.eu/news-and-events/eurescommessage/eurescom-message-1-2014/3gpp-system-standards-heading-into-the-5g-era.html

## Slide 5: 5G resource allocation
University of Houston
Challenges:
  Exponential data increase
  Node/cell heterogeneous characteristics
  Rich communication content
  Various QoS requirements
  Mobility management
Centralized solution:
  Global information
  Significant overhead
  High computation complexity
  High service latency
Cited from: http://5gmobile.fel.cvut.cz/activities/
Shift from centralized mechanism to self-organized distributive solutions.

## Slide 6: Distributive solutions
University of Houston
Game theory:
  Study of mathematical models of conflict and cooperation between intelligent rational decision-makers
  Knowledge of other players’ actions
  Specific utility function
Matching theory:
  Mathematical framework attempting to describe the formation of mutually beneficial relationships over time
  Players make local decisions
  Preference lists replace specific utilities

## Slide 7: Outline
University of Houston
Introduction
  Motivations
Wireless-Oriented Matching Applications:
  Dynamic stability in LTE-Unlicensed
  Content sharing in LTE V2X communications
  Device-to-device (D2D) communications
  Facebook content caching
  Fog Computing
  Wireless network virtualization
  Mobile crowd sensing
Future Works
  Dynamic stability in LTE V2X communications
  Stable multiple activity matching in HetNets
Conclusion
  Matching theory basics

## Slide 8
University of Houston
Everyone finds a date!
Unstable marriage!
How to design algorithm to prevent unstable results?

## Slide 9
University of Houston
Alvin E. Roth and Lloyd S. Shapley shared the 2012 Nobel Prize in Economic Science.
Shapley, designed theoretical constructs and algorithms to study and compare different matching methods.
Roth, built on his work, using experimental economics and market design to solve real-world problems.
Alvin Elliot Roth (born December 18, 1951) is the Craig and Susan McCaw professor of economics at Stanford University and the Gund professor of economics and business administration emeritus at Harvard University.
Lloyd Stowell Shapley (born June 2, 1923) is a distinguished American mathematician and economist. He is a professor Emeritus at UCLA, affiliated with departments of Mathematics and Economics.

## Slide 10: Definitions
University of Houston
Basic elements (Stable Marriage (SM)):
  Agents: A set of men, and a set of women;
  Preference list: A sorted list of men/women based on her/his preferences;
  Blocking pair (BP) (m,w):
    m is unassigned or prefers w to his current partner;
    w is unassigned or prefers m to her current partner;
  Stable matching: A matching admit no BPs.
  Gale-Shapley (GS) algorithm: find a stable matching in SM

## Slide 11
Adam
Heiki
Bob
Fran
Geeta
Carl
Irina
David
Geeta, Heiki, Irina, Fran
Irina, Fran, Heiki, Geeta
Geeta, Fran, Heiki, Irina
Irina, Heiki, Geeta, Fran
Carl > Adam
David > Bob
We reach a stable marriage!

## Slide 12: Conventional classification 1
University of Houston
One-to-one matching:
  Stable roommate (SR);
  Stable marriage (SM);
Many-to-one matching:
  House allocation (HA)
  College admission (CA)
Many-to-many matching:
  Worker-Firm (WF)
  Assign paper to reviewer

## Slide 13: Conventional classification 2
University of Houston
Bipartite matching problem with two-sided preferences.
  Assign junior doctors to hospitals
  Assign purples to schools
Bipartite matching problem with one-sided preferences.
  Campus housing allocation
  DVD rental markets
Non-bipartite matching problem with preferences.
  Form pairs of agents for chess tournaments
  Create partnership in P2P network
  Kidney exchange market

## Slide 14: Matching in wireless resource allocations
University of Houston
Matching modeling:
  Users, resources: agents/players
  System requirements: preference lists
  System objectives: stability, maximum weight, Pareto optimality…
Stability notion:
  Robustness to deviations that can benefit both the resource owners and the users in the wireless resource allocations
Advantages:
  Suitable models for specific issues
  Preference lists to satisfy various system requirements
  Stability guaranteed
  Semi-distributive implementations and close-optimal results

## Slide 15: Wireless-oriented classification
University of Houston

## Slide 16: Information exchange in matching
University of Houston
Initialize:
preference lists (PLs) set up
Propose:
Each user proposes to its most favorite resource; and delete it from its PL;
Check:
If all users’ PLs are empty?
Accept/reject:
Each resource keeps the most favorite user(s) w.r.t. its PL and quota from the proposals; and reject the rest;
Check:
If all users are matched?
Terminate:
A stable matching between users and resources.
No
Yes
Yes
No
Preference list set up:
  Users/resources collect information locally
  Interference, propagation gain, transmission rate, monetary offer…
  Channel sensing, communication...
Proposing:
  Communication signals with proposal overhead
  Update preference lists and partner lists
Accepting/rejecting:
  Make decisions and send communication signals with reject/accept overhead
  Update partner lists
Detection of blocking pair or other operations:
  Require the PLs of both type of users
  Centralized agents (eNBs or Wi-Fi Aps)
Semi-distributive implementation

## Slide 17: Outline
University of Houston
Introduction
  Motivations
  Matching theory basics
Wireless-Oriented Matching Applications:
  Content sharing in LTE V2X communications
  Device-to-device (D2D) communications
  Facebook content caching
  Fog Computing
  Wireless network virtualization
  Mobile crowd sensing
Future Works
  Dynamic stability in LTE V2X communications
  Stable multiple activity matching in HetNets
Conclusion
  Dynamic stability in LTE-Unlicensed

## Slide 18: LTE-Unlicensed
Features to protect Wi-Fi neighbors
Thanks to LTE Advanced anchor in licensed spectrum with robust mobility
Coexistence with Wi-Fi
Enhanced user experience
aggregation
5 GHz
700MHz to 3.8GHz
Carrier
LTE in Licensed Spectrum
LTE in Unlicensed Spectrum
Co-channel interference:
Unlicensed transmission: CSMA/CA
Licensed transmission: QoS
Fair coexistence?
University of Houston

## Slide 19: LTE-Unlicensed system model
University of Houston
One-to-one:
  Cellular users (CUs) , unlicensed users (UUs)
Many-to-one:
  UUs, unlicensed bands
Coexistence issues:
  interference from co-channel UUs to CUs
  interference from co-channel CUs to UUs
  interference between co-channel CUs

## Slide 20: Problem formulation
maximizing both CUs and UUs’ throughput
minimum SINR requirement for CUs
maximum interference allowed for UUs
CU capacity
UU capacity
Unlicensed band
{0,1}: indicating the sharing between CU and UU
Interference
SINR
University of Houston

## Slide 21: Solution discussion
Stable marriage game:
  one-to-one matching between CUs and UUs
Preferences of CU over UU
Preferences of UU over CU
Coexistence issue 1 & 2:
  By set up the preference lists of CUs and UUs
Coexistence issue 3:
  By adopting TDMA for multiple co-channel CUs
University of Houston

## Slide 22: Matching externality
CUs’ preferences change due to TDMA
  uneven channel allocation
  unstable matching
Co-channel interfering CUs and UUs
  hidden terminal problem
  invalid (cu, uu) pairs
Inter-channel cooperation (ICC) algorithm
  assistance from eNBs (centralized)

## Slide 23: Dynamic stability
Network dynamics:
  user mobility
  channel fading
Time-independent implementation
  GS repeated over time
  ICC to remove externality
Time-related implementation
  random path to stability (RPTS)
  re-stabilize the previous matching
  divorce and remarry operations
University of Houston

## Slide 24: GS algorithm
Initialize: CU and UU PLs set up
Propose:
Each CU proposes to its most favorite UU;
then delete it from its PL;
Check:
If all CUs’ PLs are empty?
Accept/reject:
Each UU keeps the most favorite CU from the proposals; then reject the rest;
Check:
If all CUs are matched?
Terminate
No
Yes
Yes
No

## Slide 25: RPTS algorithm
Initialize:
CU and UU PLs set up; set A as empty set;
Detection of BPs:
eNBs search for BP(s) in the current matching
ADD or SATISFY:
if both a,b are not in A, call SATISFY; otherwise call ADD
ifs
idd
Terminate
If BP(a,b) detected
If no BP detected
ADD
SATISFY
Convergence of RPTS:
  set A increase by 1 or 2 each iteration
continuous size increase of set A

## Slide 26: ICC algorithm
Remove invalid (cu,uu) pairs
Search all BPs in the current matching
Find the optimal BP with most throughput improvement;
Allow the optimal BP to switch partners;
update the current matching
Terminate
If any BP exists
Check if each BP is allowed to switch partners:
system throughput improve?
If no BP exists
Removes the second type of externality:
hidden terminal problem
Removes the first type of externality:
preference change due to TDMA
Convergence of ICC:
unreversability of each swap

## Slide 27: Time dynamic evaluation
Complexity evaluation in random waypoint (RWP):
RPTS achieves lower complexity than GS
ICC requires 6 or 7 swaps averagely
University of Houston
System throughput in RWP:
RPTS and GS achieve similar system throughput
ICC further improves system throughput
RPTS and GS achieve similar close-optimal system throughput

## Slide 28: Outline
University of Houston
Introduction
  Motivations
  Matching theory basics
Wireless-Oriented Matching Applications:
  Dynamic stability in LTE-Unlicensed
  Device-to-device (D2D) communications
  Facebook content caching
  Fog Computing
  Wireless network virtualization
  Mobile crowd sensing
Future Works
  Dynamic stability in LTE V2X communications
  Stable multiple activity matching in HetNets
Conclusion
  Content sharing in LTE V2X communications

## Slide 29: LTE assisted V2X communications
Connected vehicles
  road safety
  traffic efficiency
  entertainment
LTE assisted vs 802.11p-based V2X:
  Safety critical applications
  Better efficiency and reliability
  Lower latency
University of Houston

## Slide 30: LTE V2X communications system model
University of Houston
eNB
RSU
V2I
V2V
OBU
Vehicles
  carry various data
  information value: type, quantity
  user interest
Infrastructures:
  eNBs, APs, RSUs
Optimize information dissemination
  data information value
  communication link quality

## Slide 31: Problem Formulation
maximizing system information exchange
not self sharing
node (vehicle/infrastructure) capacity
minimum SINR requirement for vehicles
{0,1}: indicating the link connection between nodes
communication period
information value of exchanged data
data rate
University of Houston

## Slide 32: The stable fixture (SF) game
The SF problem stems from chess tournament, where players play against one another.
Definitions:
  A set of players X
  The quota for each player c
  A preference structure PL
LTE assisted V2X modeling:
  many-to-many matching
  connections independent from each other
University of Houston

## Slide 33: The Irving’s stable fixture (ISF) algorithm
degree of player
Preferences:
ISF algorithm:
  reduce preference lists
  construct player set S
    ordered pairs
Phase 1:
  proposing and rejecting
Phase 2:
  finding and removing rotations
A stable matching may not exist in SF
Termination conditions:
  is odd
  player has a short list
University of Houston

## Slide 34: Rotation
First player in the preference not in S
Rotation:
  a sequence of ordered pairs
Search rotation:
  Start by any node with a long list
  Stop when any node is visited twice
Eliminate rotation:
  reconstruct set S
  reduce preference list
University of Houston
last player in the preference list

## Slide 35: Simulation results
Social welfare & average user throughput evaluation:
ISF performs best vs ISF-unweighted, Proximity V2V, ISF-One, Without V2V
Considering data weight further improves performance
Many-to-many matching improves data sharing than one-to-one
University of Houston
ISF achieves close-optimal result

## Slide 36: Outline
University of Houston
Introduction
  Motivations
  Matching theory basics
Wireless-Oriented Matching Applications:
  Dynamic stability in LTE-Unlicensed
  Content sharing in LTE V2X communications
  Fog Computing
  Wireless network virtualization
  Mobile crowd sensing
Future Works
  Dynamic stability in LTE V2X communications
  Stable multiple activity matching in HetNets
Conclusion
  Device-to-device (D2D) communications
  Facebook content caching

## Slide 37: D2D communications
University of Houston
Spectrum sharing:
    Cellular users (CUs) and D2D users (DUs)
  Interference by channel reuse
Optimize the system throughput:
  QoS requirements
Solutions steps:
  Admission control
  Optimal power allocation
  SM matching: GS algorithm
Strategic issue:
  cheating: falsify preference lists
    Coalition strategy (CS)
    improve DU and system performance

## Slide 38: Facebook content caching
University of Houston
Facebook Haystack storage system:
  Lower caching layer has lower latency
  Cache in the same layer has geography diversity
  Cache center has capacity limit
Optimize average service delay
  content popularity
  cache center service delay
College admission (CA) game:
  many-to-one extension of SM

## Slide 39: Outline
University of Houston
Introduction
  Motivations
  Matching theory basics
Wireless-Oriented Matching Applications:
  Device-to-device (D2D) communications
  Facebook content caching
  Dynamic stability in LTE-Unlicensed
  Content sharing in LTE V2X communications
Future Works
  Dynamic stability in LTE V2X communications
  Stable multiple activity matching in HetNets
Conclusion
  Fog Computing
  Wireless network virtualization
  Mobile crowd sensing

## Slide 40: Fog computing
Fog computing:
  bring cloud closer to users
  large scale distribution at edge
  delay sensitive tasks
Joint computational and radio resource allocations
  computational: fog node (CPU)
  radio: spectrum band
Optimize average service delay
Student project allocation (SPA) model
University of Houston

## Slide 41: Wireless network virtualization
University of Houston
Wireless network virtualization:
  Abstraction, isolation and sharing of wireless resources
  Radio resource, physical infrastructure and mobile users
  Great flexibility, higher network efficiency and new services;
Joint service generation and service allocation
Three-dimension stable marriage (3DSM)
  man-woman-dog
  cyclic preferences

## Slide 42: Mobile crowd sensing
Mobile crowd sensing:
  smart phone sensing
  social networking
  environment surveillance, marketing, health monitoring…
A local event sharing:
  Twitter server: only upload Hashtag
  Real-time information exchange
  Hashtag#: location, time, data type&size, keywords
Stable fixture game
  many-to-many matching
University of Houston

## Slide 43: Outline
University of Houston
Introduction
  Motivations
  Matching theory basics
Wireless-Oriented Matching Applications:
  Dynamic stability in LTE-Unlicensed
  Content sharing in LTE V2X communications
  Device-to-device (D2D) communications
  Facebook content caching
  Fog Computing
  Wireless network virtualization
  Mobile crowd sensing
Future Works
Conclusion
  Dynamic stability in LTE V2X communications
  Stable multiple activity matching in HetNets

## Slide 44: Dynamic stability in LTE V2X communications
LTE V2X communications
  safety critical applications
  better efficiency and reliability
  lower latency
Mobility management in vehicular network:
  user mobility
  CSI information change
  real-time support
Dynamic stability in the one-sided matching:
  stable fixture game
  satisfying blocking pairs
University of Houston

## Slide 45: Stable multiple activity matching in HetNets
HetNet communications:
  user device types
  communication contents
  QoS requirements
Diverse partnerships between two players
  video stream sharing
  voice call
  texting
Stable multiple activities (SMA)
Agents participate in multiple partnerships with multiple agents
Improve user satisfaction and resource utilization
University of Houston

## Slide 46: Conclusion
University of Houston
Given a general introduction of matching theory
Provided the bridge between wireless communication and matching theory:
  Select suitable models to capture the problem
  Define preference lists to meet system requirements
  Select/ modify algorithm to guarantee stability
Analyzed the performance:
  Theoretically
  Simulation
Wise choice for future wireless resource allocation problems.

## Slide 47: Publications
University of Houston
Book:
Z. Han, Y. Gu, W. Saad, “Matching Theory for Next-Generation Wireless Networks ”, under editing, Springer, 2016.
Book chapter:
Y. Gu, L. Cai, L. Song, and Z. Han, “LTE-Unlicensed: Overview and Distributed Coexistence Design” In Vincent W.S. Wong, Robert Schober, Derrick Wing Kwan Ng, and Li-Chun Wang, “Emerging Technologies for 5G Wireless Systems”, under editing, Cambridge University Press, 2016.
Journal and Magazine:
Y. Gu, Y. Zhang, M. Pan and Z. Han, "Matching and Cheating in Device to Device Communications Underlying Cellular Networks," in IEEE Journal on Selected Areas in Communications (JSAC), vol. 33, no. 10, pp. 2156-2166, Oct. 2015.
Y. Gu, W. Saad, M. Bennis, M. Debbah and Z. Han, "Matching theory for future wireless networks: fundamentals and applications," in IEEE Communications Magazine, vol. 53, no. 5, pp. 52-59, May 2015.
Y. Gu, Y. Zhang, L. Cai, M. Pan, L. Song, and Z. Han, “LTE-Unlicensed Co-existence Mechanism: A Matching Game Framework, ” to appear in IEEE Wireless Communications Magazine, 2016.
Y. Gu, C. Jiang, L. Cai, M. Pan, L. Song, and Z. Han, “Dynamic Path To Stability in LTE-Unlicensed with User Mobility: A Matching Framework”, under revision of IEEE Transactions on Wireless Communications, 2016.
F. Chiti, R. Fantacci, Y. Gu, and Z. Han, “Content Sharing in Internet of Vehicles: Two Matching-Based User-Association Approaches”, to appear in Vehicular Communications, 2016.
Conference:
Y. Gu, M. Pan and W. Li, "Maximizing the lifetime of delay-sensitive sensor networks via joint routing and sleep scheduling," Computing, Networking and Communications (ICNC), 2014 International Conference on, Honolulu, HI, 2014.
Y. Gu, M. Pan and W. Li, "Joint sleep scheduling and routing for lifetime optimization in delay-sensitive sensor networks," 2013 IEEE International Conference on Sensing, Communications and Networking (SECON), New Orleans, LA, 2013.
Y. Gu, Y. Zhang, M. Pan and Z. Han, "Cheating in matching of device to device pairs in cellular networks," IEEE Global Communications Conference (GLOBECOM), Austin, TX, Dec. 2014.
Y. Zhang, Y. Gu, M. Pan, and Z. Han, “Distributed Matching Based Spectrum Allocation in Cognitive Radio Networks,” IEEE Globe Communication Conference (GLOBECOM), Austin, TX, Dec. 2014.
Y. Pang, Y. Zhang, Y. Gu, M. Pan, and Z. Han, “Efficient Data Collection for Wireless Rechargeable Sensor Clusters in Harsh Terrains Using UAVs,” IEEE Globe Communication Conference (GLOBECOM), Austin, TX, Dec. 2014.
Y. Gu, Y. Zhang, M. Pan and Z. Han, "Student admission matching based content-cache allocation," IEEE Wireless Communications and Networking Conference (WCNC), New Orleans, LA, Mar. 2015.
Y. Zhang, Y. Gu, L. Liu, M. Pan, Z. Dawy and Z. Han, "Incentive mechanism in crowdsourcing with moral hazard," IEEE Wireless Communications and Networking Conference (WCNC), New Orleans, LA, Mar. 2015.
Y. Gu, Y. Zhang, L. Cai, M. Pan, L. Song, and Z. Han, “Exploiting Student-Project Allocation Matching for Spectrum Sharing in LTE-Unlicensed," IEEE Global Communications Conference (GLOBECOM), San Diego, CA, Dec. 2015.
Y. Zhang, Y. Gu, L. Song, M. Pan, Z. Dawy and Z. Han, "Tournament Based Incentive Mechanism Designs for Mobile Crowdsourcing," IEEE Global Communications Conference (GLOBECOM), San Diego, CA, Dec. 2015.
Z. Chang, Y. Gu, Z. Han, X. Chen, and T. Ristaniemi, “Context-Aware Data Caching for 5G Heterogeneous Small Cells Networks”, IEEE International Conference on Communications (ICC), Kuala Lumpur, Malaysia, May 2016.
Y. Gu, L. Wang, M. Pan and Z. Han, “Exploiting the Stable Fixture Matching Game for Mobile Crowd Sensing: A Local Event Sharing Framework”, submitted to the IEEE International Conference on Communications(ICC), May 2017.
Y. Gu, C. Jiang, N. Hoang Tran, M. Pan, L. Song and Z. Han, Cyclic Three-Sided Matching Game Inspired Wireless Network Virtualization, submitted to the IEEE International Conference on Communications(ICC), May 2017.
F. Chiti, M. Fantacci, B. Picano, Y. Gu and Z. Han, “A Low Complexity Matching Game Approach for LTE-Unlicensed,” submitted to the IEEE International Conference on Communications(ICC), May 2017.
Y. Gu, Z. Chang, M. Pan, L. Song and Z. Han, “Joint Radio and Computational Resource Allocation in Fog Computing: A Student Project Allocation Matching”, submitted to 2017 IEEE International Conference on Computer Communications (INFOCOM), Jul. 2017.
Y. Gu, L. Cai, M. Pan, L. Song and Z. Han, “Exploiting the Stable Fixture Matching Game for Content Sharing in D2D-based LTE-V2X Communications”, IEEE Global Communication Conference (GLOBECOM), Washington, D.C., Dec. 2016.

## Slide 49
University of Houston