## Slide 1
Sequential Learning for Passive Monitoring of Multichannel Wireless Networks
Department of Electrical and Computer Engineering
Thanh Le
Department of Electrical and Computer Engineering
University of Houston.
Master thesis defense

## Slide 2: Outline
Problem formulation
Approximate online learning algorithm with multi-agents
Implementation
Future works & Conclusion
Master thesis defense
01

## Slide 3: Propose
We propose an approximate online learning algorithm with multi-agent.
We compare our new approximate approach with the previous proposed three approximation algorithm
We implement our work in a small scale experiment try to sniff data packets from AP and decide which channel has the most information.
Master thesis defense
02

## Slide 4: Outline
Problem formulation
Approximate online learning algorithm with multi-agents
Implementation
Future works & Conclusion
Master thesis defense
03

## Slide 5
User
AP
Range of AP
Sniffers
Range of sniffer
Channel 1
Channel 2
Channel 3
5
User 1
User 3
User 2
04
1. Problem formulation
Sniffer 2
Sniffer 1

## Slide 6: Max-Effort-Cover problem
Passive monitoring is a technique where a dedicated set of hardware devices, called sniffers, are used to monitor activities in wireless networks.
Objective: find the best set of assignments (sniffer to channel) to capture of activity of users with highest probability, where each sniffer can monitor one of a set of channels - MAX-EFFORT-COVER (MEC).
05
1. Problem formulation

## Slide 7: Notation
User with user-activity probabilities .
Sniffer , channel .
We denote as the channel on which user is active.
is the set of sniffers that can monitor the activity of user .
1. Problem formulation
06

## Slide 8: Offline problem[1]
1. Problem formulation
user is monitored or not
weight associated with user
indication of assignment
set of sniffers which can monitor user
07

## Slide 9: Problem approach
1. Problem formulation
In our problem we have no prior information about users and channels.
We need to explore channels that are under-observed to reduce the uncertainty.
We also need to exploit channels where most activities have been observed to gather more information.
08

## Slide 10: Online approach
1. Problem formulation
Our approach: to balance between assigning sniffers to channels known to be the busiest based on current knowledge, and exploring channels that are under-sampled.
09

## Slide 11: Multi-armed Bandit (MAB) Problem
Decide which arm of non-identical slot machines to play in a sequence of trials to maximize his payoff.
If the gambler choose a sub-optimal arm, he will lose some parts of the reward (regret) compares to the case he chooses the optimal arm.
the expected reward of channel , the one of the optimal channel. Then the regret of choosing channel :
Objective: find algorithms with minimum average regret over time.
1. Problem formulation
10

## Slide 12: MAB in wireless monitoring
In our case, we totally have arms (assignments).
The reward of an arm is highly correlated to other arms[2].
The best expected regret of MAB in the stochastic case is in [3]
1. Problem formulation
11
Correlated reward
Uncorrelated reward

## Slide 13: Stochastic versus Adversarial setting
Stochastic channel: channel with an expected user activity probability.
Adversarial channel: no information about the activity probability.
1. Problem formulation
12

## Slide 14: Solution approaches
1. Problem formulation
Offline centralized algo
Exact sequential learning algo
Approximate algo
ε-Greedy
UCB
UCB + Switching cost
Multi agent algo
Single agent algo
Adversarial setting
Hybrid
Online distributed algo
Offline distributed algo
13

## Slide 15: Solution approaches
1. Problem formulation
Offline centralized algo
Exact sequential learning algo
Approximate algo
ε-Greedy
UCB
UCB + Switching cost
Multi agent algo
Single agent algo
Adversarial setting
Hybrid
Online distributed algo
Offline distributed algo
14

## Slide 16: Outline
Problem formulation
Approximate online learning algorithm with multi-agents
Implementation
Future works & Conclusion
Master thesis defense
15

## Slide 17: Idea of the algorithm
2. – Greedy-Agent-approx
16
– Greedy-Agent-approx
Offline Greedy algorithm
Multi-agent idea
Domino effect

## Slide 18: Greedy algorithm
17
2. – Greedy-Agent-approx
Problem
Optimal
Greedy

## Slide 19: Multi-agent idea
2. – Greedy-Agent-approx
Correlation exploiting algorithms:
  Advantage: highly correct information about the channel.
  Drawback: computation complexity .
18

## Slide 20: Multi-agent idea
2. – Greedy-Agent-approx
19

## Slide 21: Domino effect – Reward seen by agents
20
2. – Greedy-Agent-approx
Problem
Agent 1 sees
3
4
5
1
2
Agent 2 sees

## Slide 22: Domino effect – Reward seen by agents
21
2. – Greedy-Agent-approx
Problem
Agent 1 sees
3
4
5
1
2
Agent 2 sees

## Slide 23: Domino effect – Reward seen by agents
22
2. – Greedy-Agent-approx
View 2
View 1
α
β
Total view
When should we start agent 2 so that it can choose its optimal assignment when agent 1 picks his best assignment?

## Slide 24: Our algorithm
  Parameters: with
  Initialization: define with is the time
  Loop: for each
    Let the arm picked by Greedy.
    With probability play , and with probability play a random arm from the spanner set .
  Initialize:
    The stability of each agent as with .
    The sequences by
  For
    Play agent 1 using - Greedy algorithm.
    Whenever , activate agent , play each arm in agent
    at least times, then play it using - Greedy algorithm.
    Observe the feed back and update the average reward matrix.
23
2. – Greedy-Agent-approx

## Slide 25: Parameters in algorithm
2. – Greedy-Agent-approx
24
The stability parameters
Sequences of exploration probability
                is a chosen parameter.
                with

## Slide 26: Properties of the algorithm
2. – Greedy-Agent-approx
Advantage:
  Computation time
  Small regret
Disadvantage: Small probability of linear regret
25

## Slide 27: Simulation results
26
Configuration of 4 APs & 3 Sniffers & 3 Channels 3 Agents.
2. – Greedy-Agent-approx

## Slide 28: Domino effect – Reward seen by agents
27
2. – Greedy-Agent-approx
Problem
Agent 2 sees
Greedy

## Slide 29: Computation time (s)
Run on a Windows desktop PC with Intel core i7-2600 CPU @ 3.4 GHz and 8 GB RAM memory.
28
2. – Greedy-Agent-approx

## Slide 30: Outline
Problem formulation
Approximate online learning algorithm with multi-agents
Implementation
Future works & Conclusion
Master thesis defense
29

## Slide 31: Implementation
Hardware:
  A Dell laptop CPU i5 M520 2.40GHz, RAM 3GB, HDD 200GB.
  802.11a/b/g Wireless Cardbus Adapter, model CB9-GP.
Software:
  OS: Ubuntu 10.04.
  Software: Eclipse Juno for C/C++, library pcap, tcpdump.
Objective: sniff data packets over 3 channels [3, 7, 11]of 802.11 standard to find the best active channel.
3. Implementation
30

## Slide 32: Sniffing process
  Choose the wireless card wlan1, and a frequency in the set of channels [3, 7, 11] of 802.11 standard.
  Tell the library what device we are sniffing on.
  Filter packets we concern.
  Capture the packet and display.
  Close the session.
3. Implementation
31
1. Determine interfaces and frequencies
2. Open a sniff session
5. End session
3. Setup and apply filter
4. Capture packets

## Slide 33: Applying the algorithm
  We use EXP3 and – Greedy, and UCB algorithms to choose the channel to sniff. We also compare it with a simple algorithm choosing a random channel to sniff until the end.
  Access and sniff the channel in a time slot.
  Update the result based on packets observed.
3. Implementation
32
Choose a channel to the sniffer according to the algorithm
Access sniffing process
Update the received result

## Slide 34: Result
3. Implementation
33

## Slide 35: Outline
Problem formulation
Approximate online learning algorithm with multi-agents
Implementation
Future works & Conclusion
Master thesis defense
34

## Slide 36: Future works
Proving our - Greedy-Agent-approx algorithm completely.
Extend our currently small scale experiment into a server-client model.
4. Future works & Conclusion
35

## Slide 37: Server – client model
4. Future works & Conclusion
36

## Slide 38: Conclusions
Passive monitoring of multichannel wireless networks using MAB is a good way to observe the efficiency of wireless channels.
Although optimal algorithm have a well-behaved regret, it suffers the high-computation complexity due to MEC is the NP-hard problem.
The proposed approximate online learning algorithms have faster running time but still guarantee a constant ratio of the optimal reward.
4. Future works & Conclusion
37

## Slide 39: References
[1] A. Chhetry, H. Nguyen, G. Scalosub, and R. Zheng, “On quality of monitoring for multi-channel wireless infrastruture networks,” in The ACM Internaltional Symposium on Mobile Ad Hoc Networking and Computing, pp. 111-120, Chicago IL, Sep. 2010.
[2] P. Arora, C. Szepesvari, and R. Zheng, “Sequential learning for optimal monitoring of multi-channel wireless networks,” in Proceedings of IEEE International Conference on Computer Communications, pp. 1152-1160, Shanghai China, Apr. 2011.
[3] P. Auer, N. C. Bianchi, and P. Fischer, “Finite-time analysis of the multi-armed bandit problem,” in Journal of Machine Learning, vol. 47, no. 2-3, pp. 235-256, Hingham MA, Jun. 2002.
[4] C. Chekuri and A. Kumar, “Maximum coverage problem with group budget constraints and applications,” in APPROX, pp. 72-83, ISBN 978-3-540-27821-4, Springer.
[5] P. Auer, N. C. Bianchi, Y. Freund, and R. E. Schapire, “The non-stochastic multi-armed bandit problem,” in SIAM J. Comput., vol. 32, no. 1, pp. 48-77, Phi PA, Jan. 2003.
[6] M. Tokic, “Adaptive e-Greedy exploration in reinforcement learning based on value differences, in the 33rd annual German conference on advances in artificial intelligence, Heidelberge German, Apr. 2010, pp. 203 – 210.
Master thesis defense
38

## Slide 40: References
[7] R. Zheng, T. Le, and Z. Han, "Approximate online learning algorithms for optimal monitoring in multi-channel wireless networks", IEEE Journal of Selected Topics in Signal Processing (submitted).
[8] R. Zheng, T. Le, and Z. Han, "Approximate online learning algorithms for optimal monitoring in multi-channel wireless Networks", in Proceedings of IEEE International Conference on Computer Communications, Turin Italy, Apr. 2013 (to appear).
[9] T. Le, C. Szepesvari, and R. Zheng, “Sequential learning for optimal monitoring of multichannel
wireless networks with switching costs”, IEEE Transactions on Signal Processing (in
submission).
Master thesis defense
39

## Slide 41
  THANK YOU FOR LISTENNING
Master thesis defense