## Slide 1
Ph.D. Dissertation Defense
December 8th, 2020
Mohamed Ali
Advisor: Prof. Zhu Han
Passive Reflection Techniques for Wireless Communications

## Slide 2: What is Passive Reflection Radio?
First use passive reflection for communication?
Active radio transmission:
Passive reflection transmission:
[] D. M. Dobkin, The RF in RFID: UHF RFID in Practice, 2 edition. Amsterdam: Newnes, 2012.
Signal source
Reflect more
Reflect less

## Slide 3: Motivation
Cisco estimates 500 billion devices connected by 2030
Wireless networks consume as much energy as the airline industry
Energy consumption is becoming a major concern
[1] https://www.cisco.com/c/dam/en/us/products/collateral/se/internet-of-things/at-a-glance-c45-731471.pdf
[2] A. Fehske, G. Fettweis, J. Malmodin and G. Biczok, "The global footprint of mobile communications: The ecological and economic perspective," in IEEE Communications Magazine, vol. 49, no. 8, pp. 55-62, August 2011.

## Slide 4: Motivation
How to keep supporting more devices/capacity while controlling power consumption?
Diverse requirements:
  High-rate broadband devices
  Low-rate massive connectivity devices

## Slide 5: Motivation
Passive reflection radio techniques offer solutions for both use-cases
Passive Tag
For low-rate short-range applications  Ambient Backscatter
  Uses passive reflection as a means of communicating information.
  Piggyback off ambient RF transmissions
High-rate applications  Reconfigurable Intelligent Surfaces
  Uses passive reflection as a means of improving signal propagation.
  Exercise control over signal propagation to increase capacity + simplify transceivers

## Slide 6: Outline
Motivation
Noncoherent Ambient Backscatter Techniques over OFDM:
  Introduction and System Model
  Pseudo-FSK with Energy Detection
  Noncoherent FSK
Reconfigurable Intelligent Surfaces:
  Introduction
  RIS for Orthogonal Spatial Multiplexing
  RIS for Interference Channels
Future work and Conclusion

## Slide 7: Traditional Backscatter Radio
Traditional backscatter is a mature technology.
Reader transmits dedicated constant wave
Tag intentionally changes antenna impedance to communicate
Easy to cancel self-interference.
Chart: 
Clean reader signal
[Figures] V. Liu, et al., “Ambient Backscatter: Wireless Communication out of Thin Air,” New York, NY, USA, 2013, pp. 39–50

## Slide 8: Ambient Backscatter Radio
Backscatter communication without requiring dedicated constant wave carriers?
We have ambient RF transmission everywhere!
Wi-Fi
TV
Cellular
[Figures] V. Liu, et al., “Ambient Backscatter: Wireless Communication out of Thin Air,” New York, NY, USA, 2013, pp. 39–50

## Slide 9: Ambient Backscatter Radio
But, ambient signals are random and uncontrollable
Direct link interference is hard to cancel
Unknown channels  Noncoherent detection.
Cascaded fading  poor performance + hard to analyze
Traditional Backscatter
Ambient Backscatter
Chart: 
Chart: 
[Figures] V. Liu, et al., “Ambient Backscatter: Wireless Communication out of Thin Air,” New York, NY, USA, 2013, pp. 39–50

## Slide 10: System Model
OFDM ambient source
Independent Rayleigh fading channels.
and are frequency selective.
are flat

## Slide 11: System Model
Ambient signal (OFDM  No approximations):
Received at the Tag:
Received at the Reader:
Our Goal:
What looks like?
How to detect?
Error Analysis
useful
interference
noise
Baseband OFDM symbol
Tx Power
Tag Modulation

## Slide 12: Outline
Motivation
Noncoherent Ambient Backscatter Techniques over OFDM:
  Introduction and System Model
  Pseudo-FSK with Energy Detection
  Noncoherent FSK
Reconfigurable Intelligent Surfaces:
  Introduction
  RIS for Orthogonal Spatial Multiplexing
  RIS for Interference Channels
Future work and Conclusion

## Slide 13: Tag Modulation Design
OFDM spectrum structure, :
Around 10% of channel bandwidth is left null (could be used for NB-IoT).
Use guard bands to avoid direct-link interference.
Basic idea:
  ‘1’: shift backscattered signal to guardbands
  ‘0’: do not shift backscattered signal
Upper Guard band
Lower Guard band

## Slide 14: Tag Modulation Design
Deliberately mismatch the antenna at shift frequency.
Backscattered energy will be shifted to both sides of the guardband.
14

## Slide 15: Detector
Noncoherent  energy detector over the null subcarriers:
Detector:
Test statistic distribution:
  Depends on the instantaneous SNR distribution
15
Baseband OFDM symbol after FFT
Set of inband null subcarriers
Test statistic
Noise variance
SNR
Transmitted bit

## Slide 16: Detector
Instantaneous SNR:
Product of two random variables
is an exponential random variable
is a sum of correlated exponential random variables
Distribution can be found to be:
16
Eigenvalues of the covariance matrix of for
Meijer G-function
# of Eigenvalues

## Slide 17: Error Analysis
Error rate function of the detection threshold,
Optimal at the intersection of
Probability of error:
First term independent of SNR
17
Incomplete Gamma function
Gamma function

## Slide 18: Error Analysis
2nd term complicated  condition on the SNR
Then average over the SNR distribution:
Integrate and finally get:
18
Marcum Q-function
Bi-variate Meijer G-function

## Slide 19: Multi-Antenna Rx
No channel info  Noncoherent combining, combined test statistic
Instantaneous SNR at combiner output:
Combiner SNR distribution
19
# of Rx Ant.

## Slide 20: M-ary Modulation
Partial frequency shifts and multi-level energy detection?
Note the subsets are overlapping
20
No shift

## Slide 21: M-ary Modulation
Multi-level energy detection performs very poorly!
Even with 8 antennas @ 25 dB SNR.
Proposed a different technique: Do every subset independently, then combine using an ML rule.
21

## Slide 22: M-ary Modulation
Binary vector of decisions for all subsets
ML detection rule
Assume fading independent between subsets
Construct a decoding table

## Slide 23: Simulation Results: Binary
Baseline: G. Yang, Y. C. Liang, R. Zhang, and Y. Pei, “Modulation in the Air: Backscatter Communication Over Ambient OFDM Carrier,” IEEE Transactions on Communications, vol. 66, no. 3, pp. 1219–1233, Mar. 2018.
Baseline uses repeated part of cyclic prefix to cancel interference
Different delay spreads
OFDM symbol size,
Baseline suffers as delay spread increase
For , outperform baseline by 4 dB @
Simulation verifies analysis
23

## Slide 24: Simulation Results: Multi-Antenna Rx
and
Multi-antenna receiver drastically improves performance
Huge gains with one extra antenna
Improves with more antennas more slowly
Simulation verifies analysis
24

## Slide 25: Simulation Results: 4-ary Scheme
4-ary scheme with multiple antennas
and
Performance more sensitive to bandwidth than binary
Approximate analysis very accurate
25

## Slide 26: Outline
Motivation
Noncoherent Ambient Backscatter Techniques over OFDM:
  Introduction and System Model
  Pseudo-FSK with Energy Detection
  Noncoherent FSK
Reconfigurable Intelligent Surfaces:
  Introduction
  RIS for Orthogonal Spatial Multiplexing
  RIS for Interference Channels
Future work and Conclusion

## Slide 27: Can We Implement FSK?
Improvement over energy detection scheme?
  Asymmetric error probability
  Detection threshold function of SNR
Can we implement FSK?
27

## Slide 28: Can We Implement FSK?
Remember: tag can only change its antenna impedance
A complex sinusoid is just a sequence of phase shifts…
Phase shift keying has been done in backscatter radio:
28
[1] D. Bharadia, K. R. Joshi, M. Kotaru, and S. Katti, “BackFi: High Throughput WiFi Backscatter,” in Proceedings of the 2015 ACM Conference on Special Interest Group on Data Communication, New York, NY, USA, 2015, pp. 283–296.

## Slide 29: Can We Implement FSK?
Cycle through phase shifts at different order
29

## Slide 30: Detector
No knowledge of channels or ambient signal  noncoherent detection
Looks like FSK  think of each subcarrier as a diversity branch
Square-law detection and combining (post-detection EGC) is optimal for noncoherent FSK.
Two test statistics:
Simple detection rule (no SNR dependent threshold):
30
[1] M. K. Simon and M.-S. Alouini, Digital Communication over Fading Channels, 2 edition. Hoboken, N.J: Wiley-IEEE Press, 2004.

## Slide 31: Performance Analysis
Decision statistics distribution is complicated (cascaded correlated fading)
Find conditional distribution first…
Under
Under
31
# of subcarriers

## Slide 32: Performance Analysis
Assuming equiprobable ‘1’s and ‘0’s
Remember the detection rule
Then:

## Slide 33: Performance Analysis
Need to find the distribution of and
Note they are actually equal in distribution
Conditional on SNR  ratio of a noncentral to a central
Known as a singly noncentral F-distribution
PDF:
CDF:
DOF of numerator
DOF of denominator
Noncentrality parameter
of numerator
Beta function
Incomplete Beta function

## Slide 34: Performance Analysis
Substitute in CDF to get conditional probability of error
Average over the SNR distribution
Write the exponential in terms of Meijer’s G-function..
Finally:

## Slide 35: Multi-Antenna Rx
No channel info  Noncoherent combining, combined test statistic
Instantaneous SNR at combiner output: (the same for upper and lower)
Combined SNR distribution
35

## Slide 36: 4-ary Modulation
You can shift energy to disjoint subsets, causes negligible interference
Note no overlap between subsets
36

## Slide 37: 4-ary Modulation Error Analysis
Detector  Four test statistics:
Probability of error:
Exact expression intractable  Use a union bound
Pairwise probability of error:
Error probability bound:
37

## Slide 38: Simulation Results
Baseline: M. A. ElMossallamy, M. Pan, R. Jäntti, K. G. Seddik, G. Y. Li, and Z. Han, “Noncoherent Backscatter Communications Over Ambient OFDM Signals,” IEEE Transactions on Communications, vol. 67, no. 5, pp. 3597–3611, May 2019.
Different OFDM symbol sizes (LTE)
Delay spread =
Outperforms baseline for all sizes.
Gets better for increasing SNR:  ~2 dB @ and ~3 dB @
Simulation verifies analysis

## Slide 39: Simulation Results: Multi-Antenna Rx
Different number of antennas, R
Delay spread
Outperforms baseline for all cases.
Simulation verifies analysis

## Slide 40: Simulation Results: 4-ary modulation
OFDM size = 2048
Delay spread
Single-antenna Receivers
Outperforms baseline by 5 dB at error rate
Delay spread
Two receive antennas
Bound is tight

## Slide 41: Outline
Motivation
Noncoherent Ambient Backscatter Techniques over OFDM:
  Introduction and System Model
  Pseudo-FSK with Energy Detection
  Noncoherent FSK
Reconfigurable Intelligent Surfaces:
  Introduction
  RIS for Orthogonal Spatial Multiplexing
  RIS for Interference Channels
Future work and Conclusion

## Slide 42: Reconfigurable Intelligent Surfaces
Large surfaces comprised of many tightly packed passive scatterers
Capable of backscattering/reflecting incident electromagnetic waves in a controllable manner.
Uses passive reflection to control propagation  enhance channel:
Candidate implementations: antenna reflect-arrays and metasurfaces

## Slide 43: Outline
Motivation
Noncoherent Ambient Backscatter Techniques over OFDM:
  Introduction and System Model
  Pseudo-FSK with Energy Detection
  Noncoherent FSK
Reconfigurable Intelligent Surfaces:
  Introduction
  RIS for Orthogonal Spatial Multiplexing
  RIS for Interference Channels
Future work and Conclusion

## Slide 44: System Model
Uplink: -antenna basestation, and single-antenna users
Assisted by an -element RIS
Received at base-station:
In matrix form:
No amplitude control 
RIS Effects
Fraction of power received through RIS

## Slide 45: RIS for Orthogonal Spatial Multiplexing
You can control channel, what would you change?
Assuming linear practical receivers/precoders, SINRs:
An orthogonal channel matrix is desirable:
  Simple linear receiver can remove cross-user interference
  Power control is decoupled
Benefits of massive MIMO with much less RF chains!
-th precoder/receiver
-th user channel

## Slide 46: RIS for Orthogonal Spatial Multiplexing
Equivalent to solving a system of multi-variate quadratics (NP-complete):
Solutions with higher gains desirable + more fairness
Maximize the minimum singular value of the effective channel:

## Slide 47: RIS Optimization
The RIS amplitude constraint has a geometric interpretation.
Solution must lie of a surface of smooth Riemannian manifold.
The Complex Circle manifold:
Basic concepts:
  Tangent space : space of all tangent vectors at point.
  Riemannian gradient : direction of greatest increase restricted to tangent space.
  Vector transport : transport a vector from tangent space at one point to another point.
  Retraction : A mapping from tangent space to manifold.

## Slide 48: RIS Optimization cont’d
The Riemannian Polak-Ribiere conjugate gradient algorithm converges superlinearly with little added complexity compared to steepest-descent:
  Compute Euclidean gradient
  Project Euclidean gradient into tangent space:
  Find a descent direction:
  Find suitable step size (line search or Armijo backtracking)
  Retract updated point back to manifold surface.
[1] P.-A. Absil, R. Mahony, and R. Sepulchre, Optimization algorithms on matrix manifolds. Princeton, N.J. ; Woodstock: Princeton University Press, 2008.
Hadamard product
Hadamard division

## Slide 49: RIS for Orthogonal Spatial Multiplexing
Cast as unconstrained problem on the complex circle manifold:
We use the Riemannian Polak-Ribiere conjugate gradient algorithm
Euclidean gradient needed: differentiable when minimum singular value is not repeated (happens w.p. )
[1] P.-A. Absil, R. Mahony, and R. Sepulchre, Optimization algorithms on matrix manifolds. Princeton, N.J. ; Woodstock: Princeton University Press, 2008.

## Slide 50: Simulation Results
Baseline scheme (ER-C) uses the effective rank:
,
Outperform un-assisted by ~20 bps/Hz
Outperform baseline by ~8 bps/Hz
MF MMSE  channel is orthogonal
[1] P. d. Hougne, M. Fink, and G. Lerosey, “Optimally diverse communication channels in disordered environments with tuned randomness,” Nature Electronics, vol. 2, no. 1, pp. 36–41, Jan. 2019
Nuclear norm

## Slide 51: Simulation Results
Multiple RIS sizes
Baseline does not take advantage of increased beamforming ability.
Outperforms baseline and non-assisted by large margins

## Slide 52: Simulation Results
Varying amount of power coming through the RIS
Outperforms non-assisted by bps/Hz, even when only of the power come through the RIS
RIS is beneficial even in when a strong line-of-sight path exists

## Slide 53: Outline
Introduction
Noncoherent Ambient Backscatter Techniques over OFDM:
  Introduction and System Model
  Pseudo-FSK with Energy Detection
  Noncoherent FSK
Reconfigurable Intelligent Surfaces:
  Introduction
  RIS for Orthogonal Spatial Multiplexing
  RIS for Interference Channels
Future work and Conclusion

## Slide 54: System Model
-single antenna communicating pairs.
No ability to do any spatial processing at Tx/Rx.
Leverage the RIS to cancel unwanted interference.

## Slide 55: Problem Formulation
Construct a quadratic expression including only interference terms:
and are linear functions of the channels , and .
Non-convex because of the constant modulus constraint.
Baseline: most prevalent technique in literature is to use Semidefinite Relaxation (SDR).
Proposed: cast as a non-constrained manifold optimization problem.

## Slide 56: Problem Formulation
Baseline:
Note that is only rank .
Minimizer will lie in the null space of which has dimensions .
Extract rank-1 solution using EVD.
Proposed:

## Slide 57: Results
Performance metric:
,
Rates approaching no interference case for up to 6 user pairs
SDP baseline fails to obtain good solutions in all considered cases.

## Slide 58: Results
Effect of no. of RIS elements
,
Interference effectively canceled until .
Starts to deteriorate at .
SDP baseline fails to obtain good solutions in all considered cases.

## Slide 59: Results
Effect of power fraction
,
Proposed MO-based effectively cancels interference for power fractions as low as
Large gains in rates for power fractions as low as

## Slide 60: Outline
Introduction
Noncoherent Ambient Backscatter Techniques over OFDM:
  Introduction and System Model
  Pseudo-FSK with Energy Detection
  Noncoherent FSK
Reconfigurable Intelligent Surfaces:
  Introduction
  RIS for Orthogonal Spatial Multiplexing
  RIS for Interference Channels
Future work and Conclusion

## Slide 61: Future work: Location-aided RIS Optimization
Exploits position info to aid RIS optimization without explicit channel info.
Datasets are available linking channel realizations/locations.
Potential for ML techniques.
A. Alkhateeb,"DeepMIMO: A Generic Deep Learning Dataset for Millimeter Wave and Massive MIMO Applications ," in Proc. of Information Theory and Applications Workshop (ITA), San Diego, CA, Feb. 2019.

## Slide 62: Conclusion
Passive reflection techniques can be helpful in a variety of scenarios
  Ambient backscatter for low-rate IoT applications
  Reconfigurable Intelligent Surfaces for high-rate broadband applications
Proposed two noncoherent schemes for ambient backscatter over OFDM:
  Energy-detection based
  Frequency Shift Keying based
  Both outperform state-of-the-art
Proposed two RIS-assisted schemes:
  Allowing Orthogonal Spatial Multiplexing using RIS
  Allowing simultaneous by multiple transceivers pair in an Interference Channel using RIS

## Slide 63: Publications
Journal Publications:
  M. A. ElMossallamy, M. Pan, R. Jantti, K. G. Seddik, G. Y. Li, and Z. Han, “Noncoherent Backscatter Communications Over Ambient OFDM Signals,” IEEE Transactions on Communications, vol. 67, no. 5, pp. 3597–3611, 2019.
  M. A. ElMossallamy, H. Zhang, L. Song, K. Seddik, Z. Han and G. Y. Li “Reconfigurable Intelligent Surfaces for Wireless Communications: Principles, Challenges, and Opportunities,” IEEE Trans. On Cognitive Commun. and Netw., vol. 6, no. 3, pp. 990–1002, Sep. 2020
  M. A. ElMossallamy, H. Zhang, R. Sultan, K. Seddik, L. Song, Z. Han and G. Y. Li “On Spatial Multiplexing Using Reconfigurable Intelligent Surfaces,” to appear in IEEE Wireless Commun. Letters
  M. A. ElMossallamy, R. Sultan, T. Liu, K. Seddik, G. Y. Li, and Z. Han, “Capacity Maximization of RIS-assisted Multi-User MIMO Broadcast Channels,” under review in IEEE Wireless Commun. Letters
  M. A. ElMossallamy, K. Seddik, W. Chen, L. Wang, Z. Han, and G. Y. Li, “RIS Optimization on the Complex Circle Manifold for Interference Mitigation in Interference Channels,” under review in IEEE Transactions On Vehicular Technology (Corres.)
  M. A. ElMossallamy, Z. Han, M. Pan, R. Jantti, K. Seddik, and G. Y. Li, “Noncoherent frequency shift keying for backscatter over ambient OFDM signals,” under preparation for submission to a journal
  X. Cao, Z. Song, B. Yang, M. A. Elmossallamy, L. Qian, and Z. Han, “A Distributed Ambient Backscatter MAC Protocol for Internet-of-Things Networks,” IEEE Internet of Things Journal, vol. 7, no. 2, pp. 1488–1501, Feb. 2020.
Conference Publications:
  M. A. ElMossallamy, Z. Han, M. Pan, R. Jantti, K. Seddik, and G. Y. Li “Backscatter communications over ambient OFDM signals using null subcarriers,” in Proc. IEEE Global Commun. Conf. (GLOBECOM), Abu Dhabi, UAE, Dec. 2018.
  M. ElMossallamy, Z. Han, M. Pan, R. Jantti, K. Seddik, and G. Y. Li, “Noncoherent frequency shift keying for ambient backscatter over OFDM signals,” in Proc. IEEE Int. Conf. on Commun. (ICC), Shanghai, China, May 2019. [IEEE ComSoc TCGCC Best Conference Paper Award]
  M. A. ElMossallamy, Z. Han, M. Pan, R. Jantti, K. Seddik, and G. Y. Li “Noncoherent MIMO Codes Construction using Autoencoders,” in Proc. IEEE Global Commun. Conf. (GLOBECOM), Waikoloa, HI, Dec. 2019.
  R. Duan, R. Jantti, M. A. ElMossallamy, Z. Han, and M. Pan, “Multi-Antenna Receiver for Ambient Backscatter Communication Systems,” in 2018 IEEE 19th International Workshop on Signal Processing Advances in Wireless Communications (SPAWC), Kalamata, Greece, Jun. 2018.
  X. Cao, Z. Song, B. Yang, M. A. ElMossallamy, L. Qian, and Z. Han, “A Distributed MAC Using Wi-Fi to Assist Sporadic Backscatter Communications,” in IEEE Conf. on Computer Commun. (INFOCOM), Apr. 2019, pp. 780–785.

## Slide 64: Thank you!