## Slide 1
Entering the World of GNU Software Radio
Thanh Le and Lanchao Liu

## Slide 2: Outline
Introduction
Hardware
Software
GNU Companion
Communication Demos

## Slide 3: PART I - Introduction

## Slide 4
Software Defined Radio
User App
FPGA
RF/IF conversion circuit
http://www.da.isy.liu.se/research/bp/

## Slide 5
USRP: Universal Radio Peripheral
The hardware solution for GNU SDR
USRP
USRP2

## Slide 6: PART II – Hardware

## Slide 7
Universal Software Radio Peripheral (USRP)
4 ADC 64MS/s (12-bit)
4 DAC 128MS/s (14-bit)
USB 2.0 interface¹
Small FPGA²
MIMO capable
Highest speed 480Mb/s
Capable of processing signals up to 16 MHz wide
$700

## Slide 8
Universal Software Radio
Peripheral (USRP2) ¹
2 ADC 100MS/s (14-bit)
2 DAC 400MS/s (16-bit)
Gigabit Ethernet Interface
Larger FPGA²
On-board SRAM
MIMO capable
2 Gbps high-speed serial interface for expansion
Capable of processing signals up to 100 MHz wide
$1400

## Slide 9
Available daughter-boards
Basic TX/RX: 1MHz – 250MHz
LFTX/LFRX: DC – 30MHz
TVRX: 50MHz-860Mhz
DBSRX: 800MHz – 2.4GHz
WBX0510: 50MHz – 1GHz(20dBm)
RFX400: 400MHz – 500MHz (20dBm)
RFX900: 750MHz – 1050MHz(23dBm)
RFX1200: 1150MHz – 1450MHz(23dBm)
RFX1800: 1.5GHz – 2.1GHz(20dBm)
RFX2400: 2.3GHz – 2.9GHz(17dBm)
XCVR2450: 2.4GHz – 2.5GHz & 4.9GHz -5.9GHz(20dBm)

## Slide 10
Software Defined Radio Block Diagram

## Slide 11
Low Noise Amplifier
Low Pass Filter
Low Pass Filter
Local Oscillator
ADC
Antenna
Mixer
RF Front End

## Slide 12
FPGA – MUX

## Slide 13
FPGA – DDC

## Slide 14
Example 2-1: Simple transmission
A simple sinusoidal wave is transmitted. We can view it at the receiver in spectrum domain.

## Slide 15: PART III – Software

## Slide 16
GNU radio
  GNU radio is an open source, Python-based architecture for building SDR projects
  C++ written signal processing blocks and python written connectors
  Available on Linux, Mac OS and Windows
Signal Generator
FFT
Filter
Modulation
APP1
APP2
Python
C++

## Slide 17
A thumb of rule
For any application, what you need to do at Python level is nothing but drawing a diagram to show the signal flow form the source to the sink using the Python, sometimes with the graphical user interface(GUI) support

## Slide 18
GNU Radio Installation
Step-by-step instruction available on
http://gnuradio.org/redmine/projects/gnuradio/wiki/GettingStarted
  Install the pre-requisites
  Get the GNU Radio source code
  Configure, compile and install GNU Radio
All the following demos are built in: Ubuntu-10.10 + gnuradio-3.32

## Slide 19
Example 3-1:
Src0
(440Hz)
Src1
(640Hz)
FFT
Oscilloscope
Adder

## Slide 20
Data Type
Signal blocks communicate with each other via data stream
GNU Radio requires that input and output data types match exactly
Byte – 1 byte of data(8-bit) Short – 2 bytes integer
Int – 4 bytes integer Float – 4 bytes floating integer
Complex – 8 bytes(a pair of floats)

## Slide 21
Tips: the name of the signal block indicates the input/output data type
  _f : input/output a float
  _fc: input a float and output a complex
  _vff: input and output a vector of floats
  _b: input/output a byte
  _i: input/output a integer
  _s: input/output for short

## Slide 22
USRP Source/Sink
  Initialize variable represents the signal block
  u = usrp2.source_32fc(options.interface, options.mac_addr)
  u = usrp2.sink_32fc(options.interface, options.mac_addr)
  For the USRP source: self.connect(u, other_block)
  For the USRP sink: self.connect(other_block,u)

## Slide 23
Receive: USRP Source Transmit: USRP Sink
Create the USRP source
Set the decimation /Interpolation rate
Connect to another block
Set the gain
Set the center frequency

## Slide 24
Some useful blocks
Sinusoidal Noise
Null Vector
File Audio USRPn
FFT Vector
File Audio USRPn
Adding a constant Adder Subtracter
Multiplying a constant
Multiplier Divier Log
Type Conversion
Low pass/High pass/Band pass/Hilbert/Raised Cosine
Source
Sink
Simple operators
Filters

## Slide 25
Example 3-2: Codes reading - FM Receiver
Explain the codes for FM receiver line by line.

## Slide 26
Useful tools
‘Spectrum analyzer’: usrp2_fft.py
‘Signal generator’: usrp2_siggen_gui.py & usrp2_siggen.py
‘Recorder’: usrp2_rx_cfile.py
Offline analyzer: gr_plot_fft.py & gr_plot_psd.py

## Slide 27
Example 3-3 : ‘Spectrum analyzer’
Example 3-4 : ‘Signal generator’
Example 3-5 : ‘Recorder’

## Slide 28: PART IV GRC

## Slide 29
GNU Radio Companion
A graphical tool that Create signal flow graphs & Generate flow-graph source code

## Slide 30
Adding proper blocks to the diagram and setting it parameters

## Slide 31
Connect proper blocks with each other, saving the file. Generating the flow graph, the system will save your design with a .grc file.

## Slide 32
Executing the flow graph and receive the signal by using USRP2 receiver that we designed before.

## Slide 33
Example 4-1: View signal in time/spectrum domain

## Slide 34
Example 4-2: View the constellation diagram of a signal

## Slide 35: PART IV Communication Demos

## Slide 36
FM Transmitter
gr.wavefile_source()
gr.multiply_const_cc()
Usrp2.sink_32fc()
gr.multiply_const_cc()

## Slide 37
AM transmitter
Gr.interp_fir_filter_fff()
gr.multiply_const_ff
Source
am_mod=gr.float_to_complex()
Usrp2.sink_32fc

## Slide 38
Benchmark_tx.py
source
self.packet_transmitter
Self.amp
Modulator
USRP
usrp_transmit_path

## Slide 39
Benchmark_rx.py
source
usrp_receive_path
Low_pass_filter
source
file
Self.packet_reveiver

## Slide 40
Connection

## Slide 41
Spectrum sensing
source
window
fft
c2mag
log10
threshold

## Slide 42
Reference
http://www.snowymtn.ca/gnuradio/gnuradiodoc-1.pdf
(Totally ten parts, just change the number to get it)
http://gnuradio.org/redmine/projects/gnuradio/wiki
Thanks to Ruolin Zhou @ Wright State University

## Slide 43
Questions/Comments