## Slide 1
Ph.D. Candidate: Kai-Chu Tsai
Committee Chair: Dr. Zhu Han & Dr. Ricardo Lent
Committee Member: Dr. Fan Lei, Dr. Miao Pan, Dr. Hien Van Nguyen, Dr. Li-Chun Wang
Department of Electrical and Computer Engineering
University of Houston
Houston, TX
Satellite-Terrestrial Integration
under Uncertainty Using Machine Learning and
Distributionally Robust Optimization

## Slide 2
Outline
Introduction
Work I: Multi-Commodity Flow Routing for Large-Scale LEO Satellite Networks Using Deep Reinforcement Learning
Work II: Integrated Satellite-Terrestrial Network Routing Using Deep Reinforcement Learning
Work III: Distributionally Robust Optimization for the Integrated Satellite-Terrestrial Routing
Conclusions and Future Works

## Slide 3
Satellite Networks
  Providing global coverage
  Seamless communication
  Enhancing disaster and emergency communication resilience
  Rapid deployment and flexibility
  High-speed data transmission
first artificial satellite, Sputnik 1, in 1957
Importance of satellite networks

## Slide 4
  Seamless coverage: Combine satellite coverage with ground network for uninterrupted and stable communication links
  Low latency and high throughput: Optimize performance for various applications, enabling real-time services through integrated network systems.
Integrated Satellite-Terrestrial Network (ISTN)
Urban
Rural
Remote & Isolated
DELAY
Advantages

## Slide 5
Example of ISTN: 6G
Connectivity
Self-Driving
Mixed Reality
Agriculture
Emergency Management System

## Slide 6
  End-to-end routing
  link management
  user handover control
Challenges for ISTN
  Terrestrial networks
  Satellite networks
high speed
  Construction
  Maintenance
Dynamic network topology
High cost
Complex integration

## Slide 7
Uncertainty in ISTN
handover
Ionosphere perturbation
Propagation delay and signal quality
Weather impact
Coverage and connectivity
Intermittent communication links
Doppler shift

## Slide 8
Introduction of Optimization
Optimization Classification
Optimization
Deterministic Optimization
Optimization under uncertainty
Stochastic Programming (SP)
Distributionally Robust Optimization (DRO)
Robust Optimization (RO)

## Slide 9
Optimization under Uncertainty
Stochastic Programming
  Probability distribution of random parameters is known (inferred from the historical data)
  Obj. function : find a decision 𝑥 that minimizes a functional of the expected cost.
PMF
# of vehicles
Robust Optimization
  Probability distribution of random parameters is unknown,
  but its fluctuation range is known
  Obj. function : find a decision 𝑥 that minimizes the worst-case cost over an uncertainty set
# of vehicles
Uncertainty set

## Slide 10
Optimization under Uncertainty
Distributionally Robust Optimization
  Random parameters
    uncertain
    Its probability distribution is uncertain
    only be estimated by the samples
  Obj. function : find a decision 𝑥 that minimizes the worst-case expected cost over an ambiguity set
PMF
# of vehicles
PMF
# of vehicles
PMF
# of vehicles
PMF
# of vehicles
Ambiguity set
Notes: General picture of the optimization problem
一般來說，optimization問題可以分成我們剛剛提到的確定性optimization problem以及有uncertain parameters的optimization problem,
而不確定性optimization problem，又可在細分為stochastic programming, distributionlly robust optimization 以及 robust optimization。
這3種問題的保守性是愈來愈高的
接下來我們會用一個例子介紹這三種optimization problem
DRO
not only the random parameters are uncertain, but also the probability distribution of the random parameters is uncertain. In most cases, random parameters can only be estimated by the samples. Objective is find a decision 𝑥 that minimizes the worst-case expected cost over an uncertainty set
Although the exact distribution of the random variables may not be known, people usually know certain observed samples or training data and other statistical information.
Due to the uncertain mobility of the vehicles, we consider optimize the model with uncertainty.

## Slide 11
Overview of Work 1, Work 2, and Work 3
Goal: Minimize the total end-to-end latency
Space-terrestrial network data transfer
  DRL [Work 2]
  DRO [Work 3]
Satellite network data delivery
  Deep Reinforcement Learning (DRL) [Work 1]

## Slide 12
Outline
Introduction
Work I: Multi-Commodity Flow Routing for Large-Scale LEO Satellite Networks Using Deep Reinforcement Learning
Work II: Integrated Satellite-Terrestrial Network Routing Using Deep Reinforcement Learning
Work III: Distributionally Robust Optimization for the Integrated Satellite-Terrestrial Routing
Conclusions and Future Works

## Slide 13
Motivation of Work I
  Q-Routing algorithm [1]:
  Find the end-to-end packet delay time by choosing the next-hop
  satellite based on the Q-table
  Delay tolerant reinforcement-based routing [2]:
    Utilize multi-agent reinforcement learning algorithm base on Q-learning to predict the feasibility of data message transmission with high delivery rate and a tolerable average end-to-end delay
[1] R. Dudukovich, A. Hylton and C. Papachristou, "A machine learning concept for DTN routing," 2017 IEEE International Conference on Wireless for Space and Extreme Environments (WiSEE), Montreal, QC, Canada, 2017, pp. 110-115.
[2] Rolla, Vitor G., and Marilia Curado. "A reinforcement learning-based routing for delay tolerant networks." Engineering Applications of Artificial Intelligence 26.10 (2013): 2243-2250.
  Challenges in managing large-scale networks due to expansive state space
  Non-stationarity from multiple agent policies disrupts environment dynamics
Current satellite network routing design
Problems

## Slide 14
Contributions of Work I
  Multiple decision in the single-agent reinforcement learning
Introducing new architectures
  We have developed a binary integer programming formulation to forward the requests from source to destination satellite in the LEO satellite network
  The DRL satellite routing (DRL-SR) algorithm is proposed to deliver the multiple requests within the time slot in the satellite network
  The experimental results corroborate that the proposed method can solve routing problem in the LEO satellite networks
Contributions

## Slide 15
1. Time-slotted structure with duration
  Unchanged topology during each timeslot
2. Variable undirected graph
3. Request
4. Multi-commodity flow routing problem
Route multiple commodities (flow demands) between different sources and sink nodes
Commodities → requests
Sink nodes → destination satellites
LEO Satellite Network Model
user
Source
SAT
Dest.
SAT
size
Three requests generated from three users at timeslot

## Slide 16
Problem Formulation-1
  Network delay for source-destination () pair through satellite to
  Term
    : binary decision for whether use the (𝑢,𝑣) edge to transmit the pair flow
    : binary decision for whether to store the pair flow in satellite 𝑢
    : distance between satellites and satellites at timeslot
    : transmission rate between satellites and satellites
    c : light speed
TX
propagation
Goal: minimize all the delay time for transmitting all the requests from sources to destinations
waiting time
routing delay
Approaching the Dest.
Destination reached
Notes: The routing delay for certain source-destination pair through nodes u to v at timeslot t can be expressed by this formula.
If the flow already arrives at the dest., there is no delay as the first formula shown.
On the other hand, if the flow is on the way to destination, it will have routing delay or waiting delay.
𝛼_(𝑡,𝑢,𝑣)^(𝑠_(𝑖,) 𝑑_(𝑖,) )means the binary decision for whether use the (𝑢,𝑣) edge to transmit the 𝑠_𝑖−𝑑_𝑖 pair flow
𝛽_(𝑡,𝑢,𝑣)^(𝑠_(𝑖,) 𝑑_(𝑖,) ) represents the binary decision for whether to store the 𝑠_𝑖−𝑑_𝑖 pair flow in satellite 𝑢
If alpha = 1, the flow will go from satellite u to satellite v, having routing delay.
Otherwise, if beta=1, the flow will still stay at the current satellite u, causing waiting time.
The routing delay involves propagation delay and transmission delay.
Routing Delay:
After the HAP-UAV completes processing the mobile device’s tasks, it need to find a shortest path to transmit the finished task to LAP-UAVs.
As a result, we have to add up the transmission delays of all the links the tasks passed.
Then, we can obtain total routing delay.

## Slide 17
Link bandwidth limit
Buffer capacity
request occupation limit in the
satellite network
Problem Formulation-2
s.t.
Total network latency
Decision variables
Binary indicator for link utilization
Binary indicator for storing requests
Action limit
Outflow imbalance
Inflow imbalance
Flow imbalance at node

## Slide 18
DRL: State & Action
State
  information of the satellite network
    Satellites:
    Requests:
Action
  Next-hop of the all the requests in the satellite network
Environment
Agent (Satellite operation center)
action
reward
state
location
available storage
remain at current satellite
to the neighbors of current satellite
location
size

## Slide 19
DRL: Reward
  Total reward for all the generated requests in the satellite network within timeslot
  choose to remain at the current satellite
  choose next-hop from neighboring satellites
next hop close to destination
next hop far from destination
no neighbors of the current satellite
next hop reaching destination
next hop closer to dest. / best
next hop closer to dest. / not best
next hop farther from dest. / best
next hop farther from dest. /
not best

## Slide 20
Combined with the multi-step learning, the loss of DRL-SR
With the loss function, we can train the model and let the agent learn how to route the multiple requests simultaneously from the source to destination satellite
Proposed Method: DRL
  Available storage for satellite at next timeslot equals to the current time available storage plus the variation of the flowing requests
Set of flowing out
satellite requests
variation of the flowing requests
Set of flowing in
satellite requests
Transition function for the storage availability
Multi-step learning
Loss function
  Unify the merits of one-step TD learning and Monte Carlo method
  Speed up learning

## Slide 21
Simulation Result-1
  Shortest path
    Local minimum solution
    Effected by the distance between two satellites
  DRL-SR
    Influenced by proximity to the destination satellite, buffer storage, and link availability
  Conclusion:
  More satellites in the network
  → More quickly to forward the
  request to the destination
Latency vs. number of satellites

## Slide 22
Simulation Results-2
  More users on the Earth
  → increase the total latency
  More satellites in the network
  → less time to serve the same
  number of the users
Latency vs. number of users

## Slide 23
Summary of Work I
We have investigated the multi-commodity routing problem in the LEO
satellite network and formulated it as the pure binary integer programming
optimization problem.
To address the NP-hard and multi-commodity problem, we have proposed DRL-SR approach, which is a multiple simultaneous actions under single-agent RL.
Simulation results have shown that the proposed algorithm
  Perform better than the shortest path algorithm
  Require lower latency to complete the same task

## Slide 24
Outline
Introduction
Work I: Multi-Commodity Flow Routing for Large-Scale LEO Satellite Networks Using Deep Reinforcement Learning
Work II: Integrated Satellite-Terrestrial Network Routing Using Deep Reinforcement Learning
Work III: Distributionally Robust Optimization for the Integrated Satellite-Terrestrial Routing
Conclusions and Future Works

## Slide 25
Motivation of Work II
  Hop-count estimation between two ground users [3]
    Find the minimum hop count between two ground users through Mega-constellation networks with inter-satellite links (ISL)
  Q-learning-based routing algorithm [4]
    Optimize the routing path in the satellite network in terms of throughput, delay, and bit error rate
[3] Q. Chen, G. Giambene, L. Yang, C. Fan and X. Chen, "Analysis of Inter-Satellite Link Paths for LEO Mega-Constellation Networks," in IEEE Transactions on Vehicular Technology, vol. 70, no. 3, pp. 2743-2755, March 2021
[4] Y. Yin, C. Huang, D. Wu, S. Huang, M. Wasim Abbas Ashraf, Q. Guo, "Reinforcement Learning-Based Routing Algorithm in Satellite-Terrestrial Integrated Networks", Wireless Communications and Mobile Computing, vol. 2021, Article ID 3759631, 15 pages, 2021.
0
1
2
3
5
Current satellite-terrestrial routing design
Problems
  Lack the actual offloading and downloading latency between ground and space segments
  Connection between terrestrial and satellite networks only through satellite gateway
4
6
7

## Slide 26
Contributions of Work II
  Direct communication between satellites and user equipment (UE)
Introducing new architectures
Contributions
  We have developed a binary integer programming formulation to identify the path with the least delay for transmitting tasks from source to target user equipment within the integrated space-terrestrial network infrastructure
  The multi-step DRL is proposed to address the network routing problem in the integrated space-terrestrial networks.
  The simulation results demonstrate that our proposed method successfully solves the integrated space-terrestrial routing challenge.

## Slide 27
Time-slotted structure with duration
  Unchanged topology during each timeslot
Assumptions
  Set of satellites:
    Number of orbital planes :
    Number of satellite per plane: (evenly distributed)
    altitude:
    Inclination:
  Set of users:
Data size of each user’s task
Space-Terrestrial Network Model - 1
user
Generation timeslot

## Slide 28
Ground-segment
  User equipment
    Source
    Destination
  Assumption:
  maintain one user-to-satellite link (USL) with their
  closest satellite at all times
Space-segment
  Walker-Delta constellation: M/N/F
    53, M=1584,N=72, F=39 (relative spacing between satellites in adjacent planes)
    Altitude: 550km
  Set of feasible links for satellite
Space-Terrestrial Network Model - 2
Integrated part
  Set of feasible ground-space links for satellite
    (dynamic)

## Slide 29
Space-Terrestrial Network Model - 3
TX
propagation
  User equipment  satellite
TX
propagation
  Satellite  User equipment
TX
propagation
  Satellite constellation
One-hop latency: transmit -MB file

## Slide 30
Problem Formulation-1
Objective Function:
  Decision Variables
    : binary decision for whether to forward the pair flow through link
    : binary decision for whether to use the link to route the pair flow
    : binary decision for whether to forward the pair flow through link
    : binary decision for whether to let the pair flow stary at the destination user
    equipment forever
=
Offloading
Within satellite constellation
downloading
Goal: minimize all the latency for forwarding all the tasks from source to destination user equipment
Notes: The routing delay for certain source-destination pair through nodes u to v at timeslot t can be expressed by this formula.
If the flow already arrives at the dest., there is no delay as the first formula shown.
On the other hand, if the flow is on the way to destination, it will have routing delay or waiting delay.
𝛼_(𝑡,𝑢,𝑣)^(𝑠_(𝑖,) 𝑑_(𝑖,) )means the binary decision for whether use the (𝑢,𝑣) edge to transmit the 𝑠_𝑖−𝑑_𝑖 pair flow
𝛽_(𝑡,𝑢,𝑣)^(𝑠_(𝑖,) 𝑑_(𝑖,) ) represents the binary decision for whether to store the 𝑠_𝑖−𝑑_𝑖 pair flow in satellite 𝑢
If alpha = 1, the flow will go from satellite u to satellite v, having routing delay.
Otherwise, if beta=1, the flow will still stay at the current satellite u, causing waiting time.
The routing delay involves propagation delay and transmission delay.
Routing Delay:
After the HAP-UAV completes processing the mobile device’s tasks, it need to find a shortest path to transmit the finished task to LAP-UAVs.
As a result, we have to add up the transmission delays of all the links the tasks passed.
Then, we can obtain total routing delay.

## Slide 31
Problem Formulation-2
s.t.
Total latency
Action
limit
Outflow imbalance
Inflow imbalance
Continuous
routing
Remain at the target UE permanently
Decision variables
Flow conversion

## Slide 32
Multi-step DRL: State
State
  information of the integrated space-terrestrial network
    Satellites:
    User equipment:
    Tasks:
Environment
Agent (Satellite operation center)
action
reward
state
longitude
latitude
source
dest.
current
location
dest.
user
equipment
size

## Slide 33
Reward
  Reward for the task in the integrated
  space-terrestrial network at timeslot 𝑡
Action
  Next-hop of the task in the integrated space-terrestrial network
    Current location of the task
Multi-step DRL: Action & Reward
satellite
orbit
Offload the task when
Route and download the task
when
Route the task when
Exponential-decay reward
  Differentiate the reward across
  different time slots
  Transmit the tasks in fewer time steps

## Slide 34
Simulation Results-1
  Random
    Unpredictable manner
    Increase randomness as the number of user equipment
  Multi-step DRL
    Influenced by proximity to the target user equipment, next-hop latency
  More user equipment in the integrated network
  → More latency to deliver the
  task to the matching target user
  equipment
Latency vs. number of user equipment

## Slide 35
Simulation Results-2
  Larger data size in the network
  → increase the total latency
  Random
    Affected heavily by the traffic load
  Multi-step DRL
    Well-trained model
    Less affected by the traffic load
Data size
Latency vs. Traffic load
1~5 MB
2~6 MB
3~7 MB

## Slide 36
Summary of Work II
We have studied delivering the tasks from the source to the target user equipment with the minimum overall latency in the integrated space-terrestrial networks and formulated it as the pure binary integer programming optimization problem.
To tackle the NP-hard problem, we have proposed multi-step DRL method, which is a varied of conventional Deep Q-networks approach.
Simulation results have shown that the proposed algorithm
  Transmit tasks more efficiently than the random selection algorithm
  Demand a shorter latency to execute the equivalent mission

## Slide 37
Outline
Introduction
Work I: Multi-Commodity Flow Routing for Large-Scale LEO Satellite Networks Using Deep Reinforcement Learning
Work II: Integrated Satellite-Terrestrial Network Routing Using Deep Reinforcement Learning
Work III: Distributionally Robust Optimization for the Integrated Satellite-Terrestrial Routing
Conclusions and Future Works

## Slide 38
Motivation of Work III
  Terrestrial-Satellite Hybrid Routing (TSHR) algorithm [5]
    Find the minimum end-to-end delay by selecting the transmission path among ISL, terrestrial-satellite routing equipment-Satellite Link (TSL) and Inter Terrestrial Link (ITL)
  Joint satellite gateway and routing strategy [6]
    Minimize the overall cost of gateway deployment and traffic routing while satisfying average delay requirement for traffic demands
[5] H. Xu, D. Li, M. Liu, G. Han, W. Huang and C. Xu, "A Hybrid Routing Algorithm in Terrestrial-Satellite Integrated Network," 2020 IEEE/CIC International Conference on Communications in China (ICCC), Chongqing, China, 2020, pp. 90-95
[6] N. Torkzaban, A. Gholami, J. S. Baras and C. Papagianni, "Joint Satellite Gateway Placement and Routing for Integrated Satellite-Terrestrial Networks," ICC 2020 - 2020 IEEE International Conference on Communications (ICC), Dublin, Ireland, 2020, pp. 1-6
Current ISTN routing design
Problems
  Merely through terrestrial-satellite terminals (TSTs), i.e. terrestrial-satellite gateway and base stations, to connect terrestrial and satellite network
  Less coverage area due to fixed terrestrial-satellite terminals (TSTs)

## Slide 39
Contributions of Work III
  We formulate the distributionally robust optimization (DRO) problem to find an optimal minimum delay path to deliver the tasks generated by the source mobile devices to the destination mobile devices under the integrated space-terrestrial networks.
  The uncertain latency involving vehicles due to the unpredictable movement is formed as the Wasserstein ambiguity set.
  The numerical results show that the proposed method can address the integrated space-terrestrial routing problem.
Introducing new architectures
Contributions
  Installation of TSTs on automobiles
  Direct communication between satellites and mobile devices

## Slide 40
Integrated Satellite-Terrestrial Networks
Task (e.g. text message, photos, videos) generated by user equipment (UP)
Aim to transmit the information with minimum latency
Possible resulting data delivery path
Final routing path
Source city
Destination city

## Slide 41
Data Delivery Path Division
Part 1: uplink paths
Path 2:
routing paths in the satellite network
Path 3: downlink paths
Divide the total routing path into three parts

## Slide 42
Delay for Direct Uplink Paths
Propagation
TX
Direct uplink path one
  Path: MD  TST embedded on building
   satellite
  Latency
distance between MD and satellite
light speed
data size generated by MD
at time slot
transmission rate between MD
and satellite at time slot
Direct uplink path two
  Path: MD  satellite
  Latency

## Slide 43
Delay for Undetermined Uplink Paths
Perfect path
partial transmitted data
Undetermined uplink path one
  Perfect path: MD  TST embedded on
  vehicle  satellite
  Reroute path: MD  TST embedded on
  vehicle  (moving vehicle + horizontal
  hand-off cost)  MD  TST embedded
  on building  satellite
  Latency within the range
partial transmitted data
Undetermined uplink path two
  Perfect path: MD  TST embedded on
  vehicle  satellite
  Reroute path: MD  TST embedded on
  vehicle  (moving vehicle + vertical
  hand-off cost)  MD  satellite
  Latency within the range

## Slide 44
Delay for Direct Downlink Paths
Propagation
TX
Direct downlink path one
  Path: satellite  TST embedded on building
   MD
  Latency
distance between satellite and
target MD
light speed
data size generated by MD
at time slot
transmission rate between
satellite and target MD at time slot
Direct downlink path two
  Path: satellite  MD
  Latency

## Slide 45
Delay for Undetermined Downlink Paths
Perfect path
partial transmitted data
Undetermined uplink path one
  Perfect path: satellite  TST embedded on
  vehicle  target MD
  Reroute path: satellite  TST embedded on
  vehicle  (moving vehicle + horizontal hand-
  off cost)  satellite  TST embedded on
  building  target MD
  Latency within the range
partial transmitted data
Undetermined uplink path two
  Perfect path: satellite  TST embedded on
  vehicle  target MD
  Reroute path: satellite  TST embedded on
  vehicle  (moving vehicle + vertical hand-off
  cost)  satellite  target MD
  Latency within the range
animation

## Slide 46
Latency Ambiguity Set
Wasserstein distance
  Used to measure the distance between two distributions.
Uploading latency ambiguity set
Downloading latency ambiguity set
: the set of all possible joint distributions of and .
samples under joint distribution
: sample distance
: expectation of distance for sample and under joint distribution
Notes: Measure the difference between two probability distributions
Wasserstein distance is used to measure the distance between two distributions,where ∏(𝑃_1,𝑃_2)is the set of all possible joint distribution of 𝑃_1 and 𝑃_2. (𝑥, 𝑦)~𝛾 𝑑𝑒𝑛𝑜𝑡𝑒𝑠 samples under joint distribution 𝛾 ‖𝑥−𝑦‖ is sample distance 𝔼_((𝑥,𝑦)~𝛾) [‖𝑥−𝑦‖]shows expectation of distance for sample 𝑥 and 𝑦 under joint distribution 𝛾

## Slide 47
Problem Formulation-1
Binary decision variable set
  Routing:
  Waiting:
Routing time for information generated at timeslot from mobile device
Offloading delay from mobile users to satellites
Routing delay in SAT network
Returning delay from satellites to mobile users

## Slide 48
Problem Formulation-2
s.t.
Total latency
Outflow imbalance
Binary indicator for direct downlink path
Binary indicator for date delivery next-hop in the satellite network
Binary indicator for direct uplink path
Binary indicator for undetermined uplink path
Binary indicator for undetermined downlink path
Binary indicator for staying in the satellite network
Binary indicator for staying in the target UE
Action limit

## Slide 49
Problem Formulation-3
Limited number of offloaded tasks via building
Outflow imbalance
s.t.
Total latency
Inflow imbalance
Continuous routing
Flow conversion
Remain at the dest. permanently

## Slide 50
Proposed Method
Inner maximization optimization w.r.t. two ambiguity sets ,
After substituting into the original problem, the tractable reformulated problem is obtained
Duality theorem

## Slide 51
Numerical Results and Analysis-1
  Robust optimization [RO]
    More conservative: worst-case solution
    Require more time to complete the same task
  Stochastic programming [SP]
    Complete knowledge of the uncertainty
    Need less time to finish the same mission
  Distributionally robust optimization [DRO]
    Expected worst-case solution
    Latency between RO and SP
  More tasks in the network
  → Require more time to forward the
  tasks from the source to the destination
Number of requests vs. latency

## Slide 52
Numerical Results and Analysis-2
  The same amount of tasks of each device
  More users on the source city
  → Increase the total latency
  Proposed DRO model
    Require less total latency than the RO mechanism
    Require more delay than the SP method
    Ambiguity set size increases, latency closer to RO
Size amplification factor controls the ambiguity set size ( >
Number of user equipment vs. latency

## Slide 53
Summary of Work III
We have developed the distributionally robust optimization model to route tasks from source mobile devices to target mobile devices in integrated satellite-terrestrial networks with the minimum expected worse-case latency.
To address the unpredictable vehicle mobility, the delay of uploading and downloading paths is built up as the Wasserstein ambiguity sets.
The original distributionally robust optimization model is then reduced into a formulation that is manageable.
Simulation results have shown that the proposed model
  Perform better than the robust optimization scheme
  Require more latency than stochastic optimization mechanism

## Slide 54
Future Works-1
Distributionally robust reinforcement learning (DRRL)
  Choose an efficient policy to explore the unknown environment
    Ambiguity set for policies:
    Select the worse policy for taking actions
  Training
    Small ambiguity set  optimistic policies
    Large ambiguity set  conservative policies
  Testing
    Beat the unseen environment and conditions
Training
  Small ambiguity set  optimistic policies
  Large ambiguity set  conservative policies
worse case
Best policy
Considered
possible
policies
State space
: Set of probability
distribution mapping
from state to action

## Slide 55
Future Works-2
Graph Neural Networks (GNNs)
  ISTNs: dynamic and complex network topology
  Make decisions based on topologies
Quantum computing
  Formulated problem – pure binary integer programming problem
  Quantum solvers: D-wave, Qiskit, Rigetti

## Slide 56
Conclusions
Introduce the importance and challenge in the integrated space-terrestrial network
Work I: satellite network + end-to-end latency + DRL
  We introduced a multi-step DRL strategy to deliver the tasks from the source to the target user equipment via the Walker Delta constellation, achieving the least possible cumulative delay.
  We devised the deep reinforcement learning satellite routing (DRL-SR) algorithm to transmit the requests from the source to destination satellite with multiple action selection under the single-agent RL.
Work II: ISTN + end-to-end latency + DRL
  We designed the Wasserstein ambiguity set to model the offloading and downloading delay and used DRO method to find the worse-case expectation latency to transmit the tasks.
Work III: ISTN + end-to-end latency + uncertainty + DRO

## Slide 57
Publications
Journal
  Kai-Chu Tsai, Zirui Zhuang, Ricardo Lent, Jingyu Wang, Qi Qi, Li-Chun Wang, and Zhu Han, "Tensor-Based Reinforcement Learning for Network Routing," in IEEE Journal of Selected Topics in Signal Processing, vol. 15, no. 3, pp. 617-629, April 2021
  Kai-Chu Tsai, Lei Fan, Ricardo Lent, Li-Chun Wang, and Zhu Han, Decision-Making Under Uncertainty in the Integrated Satellite-Terrestrial Networks Using Distributionally Robust Optimization, under review at IEEE Transactions on Communications
  Kai-Chu Tsai, Lei Fan, Ricardo Lent, Li-Chun Wang, and Zhu Han, Distributionally Robust Reinforcement Learning for Integrated Satellite-Terrestrial Network Routing, in preparation
Conferences
  Kai-Chu Tsai, Lei Fan, Li-Chun Wang, Ricardo Lent and Zhu Han, "Multi-Commodity Flow Routing for Large-Scale LEO Satellite Networks Using Deep Reinforcement Learning," IEEE Wireless Communications and Networking Conference (WCNC), Austin, TX, USA, 2022, pp. 626-631
  Kai-Chu Tsai, Ting-Jui Yao, Pin-Hao Huang, Cheng-Sen Huang, Zhu Han, and Li-Chun Wang, "Deep Reinforcement Learning-Based Routing for Space-Terrestrial Networks," IEEE 96th Vehicular Technology Conference (VTC2022-Fall), London, United Kingdom, 2022, pp. 1-5
  Kai-Chu Tsai, Lei Fan, Ricardo Lent, Li-Chun Wang, and Zhu Han, " Integrated Satellite-Terrestrial Routing Using Distributionally Robust Optimization" ICC 2023 - IEEE International Conference on Communications, Rome, Italy, 2023, pp. 277-282
  Kai-Chu Tsai, Angeles Vazquez-Castro, Lei Fan, Ricardo Lent, Li-Chun Wang, and Zhu Han, " Integrated Satellite-Terrestrial Network Routing Using Deep Reinforcement Learning“, submitted to ICC 2024 - IEEE International Conference on Communications

## Slide 58
Thank you for your attention.