## Slide 1
Qubit Allocation, Entanglement Routing, and Topology Optimization for Quantum Networks and Computing
Zhu Han, John and Rebecca Moores Professor IEEE Fellow, AAAS Fellow, ACM Fellow Electrical and Computer Engineering Department University of Houston, TX USA
Thanks to Groups of Profs. Lei Fan, Yu Wang, Yuanxiong Guo and NSF

## Slide 2
Outline
2
Background
  Quantum Communication and Networking
  Limitations of ground-based quantum entanglement distribution
  Ariel Access Networks
  Quantum Computing
Joint Optimization of Qubit Allocation, Entanglement Routing, and Quantum Computing
  Optimizing Satellite-based Entanglement Distribution in Quantum Networks via Quantum-Assisted Approaches
  Efficient Entanglement Routing for Satellite-Aerial-Terrestrial Quantum Networks
  Co-Design of Network Topology and Qubit Allocation for Distributed Quantum Computing
Conclusions

## Slide 3
Quantum Communication and Networking
3
Transmit quantum information between nodes,
using quantum phenomena superposition and entanglement
No bits, but qubits
Bits
Qubits
Quantum teleportation
Bit. [Online]. Available: https://www.computerhope.com/jargon/b/bit.htm
What is a qubit. [Online]. Available: https://www.quantum-inspire.com/kbase/what-is-a-qubit/
Teleportation is real, thanks to quantum entanglement. [Online]. Available: https://www.popularmechanics.com/science/a25699/how-quantum-teleportation-works/

## Slide 4
Quantum Communication and Networking
4
Entanglement Generation and Swapping
Stage 1: Alice and Bob generate an Einstein-Podolsky-Rosen (EPR) pair and send one qubit from their respective pairs to Carol
(a) Entanglement generation
(b) Entanglement swapping
(c) Entanglement established
Stage 2: Carol performs a Bell-state measurement (BSM) and transmits the result to Bob, i.e., entanglement swapping
Stage 3: Alice and Bob are entangled

## Slide 5
Quantum Communication and Networking
5
Terrestrial Quantum Network (TQN)
  Utilize optical fiber links
  Exponential increase in photon loss with distance
  Terrestrial repeaters perform entanglement swapping and purification to ensuring high fidelity
Limited Coverage
Constrained scalability
Inefficient communication

## Slide 6
Limitation and Challenges
6
Limitations of ground-based quantum entanglement distribution
Signal attenuation and decoherence: Entanglement is fragile and easily disrupted by loss and noise during transmission.
Distance constraints: Reliable entanglement maintenance is limited over long ground-based distances.
Environmental interference: Electromagnetic noise, temperature shifts, and vibrations degrade quantum stability.
Device imperfections: Hardware errors and component flaws reduce entanglement fidelity.
Security risks: Protecting entanglement channels from eavesdropping and attacks remains difficult.
Cost and scalability: High implementation costs and complex maintenance hinder large-scale deployment.

## Slide 7
Ariel Access Networks
7
Space-Aerial-Terrestrial Quantum Networks (SATQNs)
SATQN has three layers
  Space quantum network enables long-distance entanglement distribution via free space optical links
  Aerial quantum network supports flexible and rapid deployment using free space optical links
  Terrestrial quantum network offers stable quantum connections via optical fiber links

## Slide 8
Aeriel Access Networks
8
An alternative way: satellite-based entanglement distribution
Overcoming distance limits: Satellites enable global-scale entanglement distribution beyond ground-based range.
Reduced signal loss: Space offers minimal attenuation and interference for more reliable quantum transmission.
Broad coverage: Satellites connect remote and inaccessible regions lacking ground infrastructure.
Freedom from obstacles: Signals are unaffected by terrain, buildings, or other terrestrial barriers.
Global quantum networking: Satellite links are essential for secure, worldwide quantum communication.
Complementary integration: Satellite systems enhance and extend ground-based quantum networks

## Slide 9
Ariel Access Networks
9
SATQN Applications
Time-sensitive applications
  Complete tasks as quickly as possible
  Avoid information decoherence due to noise or delay
  E.g., Distributed quantum computing (DQC)
Time-insensitive applications
  Support long-term stream of entanglements
  Require secure communications
  Steady stream of entanglement over time
  E.g., Quantum key distribution (QKD)
Distributed quantum phase estimation with entangled photons. [Online]. Available: https://www.nature.com/articles/s41566-020-00718-2
Quantum Key Distribution Technology. [Online]. Available: https://www.drishtiias.com/daily-updates/daily-news-analysis/quantum-key-distribution-technology/print_manually

## Slide 10
Ariel Access Networks
10
Challenges in SATQNs
Complex Integration
free space optical links and optical fiber links
Decoherence and Errors
noise in quantum channels and imperfections in quantum operations

## Slide 11
Outline
11
Background
  Quantum Communication and Networking
  Limitations of ground-based quantum entanglement distribution
  Ariel Access Networks
  Quantum Computing
Joint Optimization of Qubit Allocation, Entanglement Routing, and Quantum Computing
  Optimizing Satellite-based Entanglement Distribution in Quantum Networks via Quantum-Assisted Approaches
  Efficient Entanglement Routing for Satellite-Aerial-Terrestrial Quantum Networks
  Co-Design of Network Topology and Qubit Allocation for Distributed Quantum Computing
Conclusions

## Slide 12
Quantum Computing
12
NP-hard Optimization Problems
?
e. g. Maximum Likelihood MIMO Detection Using Quantum Computing
Quantum Computing: use quantum mechanics to solve problems too complex for classical computers.
MIMO Detection
Resource Allocation
. . .
Network Slicing
[2] M. Kim, D. Venturelli, and K. Jamieson, “Leveraging quantum annealing for large MIMO processing in centralized radio access networks,” in Proceedings of the ACM Special Interest Group on Data Communication, Beijing, China, Aug. 2019.
[2]
Network Slicing
Network
Function Virtualization
. . .
Quantum Computing:

## Slide 13
Quantum Computing
13
Quantum Computer
Gate Model
Analog Quantum Model
Quantum Annealing
More Qubits
Faster than classical solvers
Fit some optimization problems
Maybe we need to use quantum mechanics in our computers.

## Slide 14
Heat the metal to a temperature;
Lower the temperature;
Annealing a Metal
Simulated Annealing
Heuristic algorithm;
Random search method;
The temperature variable;
Quantum tunneling
Quantum Annealing
Enables jumping from one classical state to another
– Decreases likelihood of getting stuck in a local minimum
Width of energy barrier is important, but height is not
Different Annealing
14

## Slide 15
Superposition
Tensor Product
Qubits and Quantum Operation
15

## Slide 16
Before studying quantum
after studying quantum
Schrödinger Equation
16

## Slide 17
Problem of Hamiltonian:
Goal (what the hardware does)
  Minimize σi ∈ {-1, +1} subject to provided Ji,j ∈ R and hi ∈ R coefficients
  In other words, a quantum optimization program is merely a list of Ji,j and hi
Classical
  Much easier to reason than a quantum Hamiltonian
  Quantum effects are used internally to work towards the goal
Sparsely connected
  Possible to map fully connected problems onto the D-Wave’s Chimera graph
Dwave Hamiltonian
17
Notes: dwave 所实现的coupling 中的configuration是右上角奇美拉或者天马座circuit(Notably, D-Wave Systems' nearest-neighbor coupling achieves a highly connected unit cell of 8 qubits in the Chimera graph configuration. Generally, quantum algorithms require coupling between arbitrary qubits, therefore the connectivity limitation is likely to require multiple swap operations, limiting the length of the possible quantum computation before the processor decoherence.)

## Slide 18
QUBO (Quadratic Unconstrained Binary Optimization)
These important optimization problems can be transformed into QUBO model:
Quantum Computing:
provide an alternative method to solve some NP-hard problems
Knapsack Problems
Assignment Problems
Task Allocation Problems
Capital Budgeting Problems
… (NP-hard problem)
Ising Model
: upper-diagonal matrix
Spins interact with applied field
Neighboring spins interact with each other
Core idea: Encoding the objective function as the eigenvalue of the final ground state of
Schrodinger equation, based on Adiabatic Quantum Computing Model
Chimera
Pegasus
Link Schrodinger with QUBO Model
18

## Slide 19
Considering only the external field:
We arbitrarily call σz = +1 “TRUE” and σz = —1 “FALSE”
Here are the optimal values of σz for different values of h
Observations
– A negative hi means, “I want σz to be TRUE”
– A zero hi means, “I don’t care if σz is TRUE or FALSE”
– A positive hi means, “I want σz to be FALSE”
QUBO Equation
19

## Slide 20
Consider only the coupler strengths:
Here are the optimal values of σz and σz for different values of Ji,j:
Observations
  A negative Ji,j means, “I want σz and σz to be equal”
i j
  A zero Ji,j means, “I don’t care how σz and σz are related”
i j
  A positive Ji,j means, “I want σz and σz to be different”
i j
Best answer appear with high probability
but not 100%, which is Achilles’ heel for
many quantum algorithms but not ours
QUBO Equation
20
Notes: animation
margin word

## Slide 21
Inputs’ energy are set.
Lowest energy is at or closes to the optima.
Energy → possibility
Initial Qubits
Superposition at |s and |s.
Not yet coupled.
Qubits are entangled.
At state of many possible answers.
Couplers & biases applied
A matter of microseconds.
Energy diagram in Quantum Annealing
QUBO Quantum Annealing
21
Notes: The signal processing’s final goal is to inverse the data acquisition process:
Figure out the physical properties of the undersurface model based on the signal acquired.
Unfortunately, many problems block our way from observed signals to our interested velocity model.
这张图是定性地在说dwave如何进行退火的，
第一个状态是先初始化qubit(s)并使其处于叠加态，量子之间并未被circuit或者gate耦合.(如何具体耦合见于这个link https://en.m.wikipedia.org/wiki/Superconducting_quantum_computing的coupling qubit第一段)
第二个是通过增添耦合couple和偏置bias模拟问题(类似于构造山峰地形图，但是还没有让小球滚落)，此时qubits已经开始纠缠了，所以此时读取是state of many possible answers。
最后一步是冷却(让所有在不同位置的小球滚落)并读数，state的能量越低越容易被读到(energy变possibility)

## Slide 22
Distributed Quantum Computing
22
What is Distributed Quantum Computing (DQC)?
  Multiple interconnected quantum processors (QPUs) work together to solve large-scale computational problems
Why DQC?
  single QPUs have limited qubits
  monolithic large QPU is very hard to build
  a promising pathway to large-scale quantum computing
Challenges in DQC
  Qubit allocation/Circuit partition: distribution and management of qubits across multiple QPUs to optimize communication and execution time
  Quantum network function: serve high-quality & low-latency connections among quantum nodes to for remote operations
Notes: The signal processing’s final goal is to inverse the data acquisition process:
Figure out the physical properties of the undersurface model based on the signal acquired.
Unfortunately, many problems block our way from observed signals to our interested velocity model.
这张图是定性地在说dwave如何进行退火的，
第一个状态是先初始化qubit(s)并使其处于叠加态，量子之间并未被circuit或者gate耦合.(如何具体耦合见于这个link https://en.m.wikipedia.org/wiki/Superconducting_quantum_computing的coupling qubit第一段)
第二个是通过增添耦合couple和偏置bias模拟问题(类似于构造山峰地形图，但是还没有让小球滚落)，此时qubits已经开始纠缠了，所以此时读取是state of many possible answers。
最后一步是冷却(让所有在不同位置的小球滚落)并读数，state的能量越低越容易被读到(energy变possibility)

## Slide 23
Outline
23
Background
  Quantum Communication and Networking
  Limitations of ground-based quantum entanglement distribution
  Ariel Access Networks
  Quantum Computing
Joint Optimization of Qubit Allocation, Entanglement Routing, and Quantum Computing
  Optimizing Satellite-based Entanglement Distribution in Quantum Networks via Quantum-Assisted Approaches
  Wei, X., Fan, L., Guo, Y., Han, Z. and Wang, Y., 2024, July. Optimizing satellite-based entanglement distribution in quantum networks via quantum-assisted approaches. In 2024 International Conference on Quantum Communications, Networking, and Computing (QCNC) (pp. 280-287). IEEE.
  Efficient Entanglement Routing for Satellite-Aerial-Terrestrial Quantum Networks
  Co-Design of Network Topology and Qubit Allocation for Distributed Quantum Computing
Conclusions

## Slide 24
Motivation
24
Limitations and challenges of previous works
a heuristic greedy algorithm and ignores some resource constraints
only consider some specific settings by converting the problem into either a maximum weight independent set problem or a maximum weight bipartite matching problem.
Fig. 1. The satellite-based entanglement distribution and terrestrial quantum swapping architecture.
This paper investigates a joint satellite assignment, resource allocation, and path selection scenario to build quantum entanglements for ground stations by leveraging satellite-based entanglement distribution and terrestrial quantum swapping.

## Slide 25
System Model
25
Fig. 2. An example of the space-to-ground transmittance between one SAT and two GSs for the entanglement distribution to this GSP.
1. Network Model
satellites (SAT): , : quantum memory of SAT , : number of transmitters of SAT .
ground stations (GS): , g: quantum memory of GS , : number of receivers of GS .
ground station pairs (GSP):
2. Channel Model
spontaneous parametric down-conversion (SPDC)
space-to-ground transmittance:
free-space transmittance:
atmospheric transmittance:
: the circular apertures of diameter of the transmitter and receiver telescopes
: the specific wavelength
: the atmospheric extinction coefficient

## Slide 26
System Model
26
[1] N. K. Panigrahy, P. Dhara, D. Towsley, S. Guha, and L. Tassiulas, “Optimal Entanglement Distribution using Satellite Based Quantum Networks,” in IEEE Conference on Computer Communications (INFOCOM) Workshops, Virtual, May 2022.
[2] A. Zang, X. Chen, A. Kolar, and J. Chung, “Entanglement Distribution in Quantum Repeater with Purification and Optimized Buffer Time,” in IEEE Conference on Computer Communications Workshops, New York, NY, May 2023.
3. Terrestrial Quantum Swapping
The fidelities of the new states after swapping are defined below [2]
and are the fidelities of two entanglement links, respectively.
2. Channel Model
The fidelity of entangled photon pair after transmission can be approximated by
is the initial fidelity of the entangled photon pair.
Assumptions[1]: ,
is the number of background photons received by GS .
Fig. 2. An example of the space-to-ground transmittance between one SAT and two GSs for the entanglement distribution to this GSP.

## Slide 27
Problem Formulation
27
The joint satellite assignment, resource allocation, and path selection problem.
Objective: maximize the overall utility of all traffic GSPs
Satellite assignment or
Terrestrial quantum swapping
each GSP only connects to one satellite or only selects one swapping path if the satellite assignment is not available.
a GS can be part of multiple GSPs and thus is not allowed to be allocated to more than satellites.
SAT does not get allocated to more than GSPs.
the total entangled photon received from different satellites cannot exceed g.
the total entangled photon pair allocation fraction of SAT cannot exceed .
if a swapping path is selected, then two entanglement links along this path must be established based on the satellite assignment.
the fidelity of entanglement links after transmitting or swapping is larger than the fidelity threshold.
NP-hard
: if satellite is assigned to GSP ; : the entangled photon pair allocation;
: if path is selected to GSP ; : the entangled photon pair allocation.

## Slide 28
Hybrid Quantum-Classic Dantzig-Wolfe Decomposition (HQCDW)
28
① Linearization
② general form
③ reformulation
④ linear combination of extreme points
⑤ DW decomposition
Block
structure

## Slide 29
HQCDW Algorithm
29
Proposed HQCDW framework for joint satellite-based quantum entanglement distribution and terrestrial quantum swapping.
Continuous
optimization
Integer
optimization

## Slide 30
Evaluation
30
Network architecture
Comparison methods
Steepest Descent (SD) [3]: SD is a solver for binary quadratic models by D-Wave Systems with the best move determined through a local minimization.
Random Steepest Descent (RASD) [3]: RASD combines random sampling and steepest descent, with the algorithm using random sampling to generate initial states for SD.
Classical Optimizer (COPT): COPT solves the original problem (5) by using a classical optimizer (e.g., Gurobi, Scipy) in a classical CPU computer.
Classical DW Decomposition (CDWD): CDWD decouples the original problem using DW decomposition and solves all problems with a classical optimizer.
[3] D-Wave Systems Inc., “Ocean software documentation: dwave-samplers, steepestdescentsolver, randomsampler,” Oct. 2023. [Online]. Available: https://docs.ocean.dwavesys.com/en/stable/docs samplers/reference.html
Parameters | Value
Number of SATs | 
Satellites altitude | 
Quantum memory of SATs | 
Number of transmitters | 
Number of GSs | 
Quantum memory of GSs | 
Number of transmitters | 
Parameters | Value
Satellites altitude | 

## Slide 31
Evaluation
31
1. This highlights the effectiveness and robustness of using DW decomposition to tackle larger network scales.
2. This analysis highlights the advantage of using the DW decomposition to overcome constraints imposed by the maximum number of qubits in the quantum machine.
3. This result highlights the benefits of DW decomposition for larger-scale problems.

## Slide 32
Outline
32
Background
  Quantum Communication and Networking
  Quantum Computing
  Limitations of ground-based quantum entanglement distribution
  Ariel Access Networks
Joint Optimization of Qubit Allocation, Entanglement Routing, and Quantum Computing
  Optimizing Satellite-based Entanglement Distribution in Quantum Networks via Quantum-Assisted Approaches
  Efficient Entanglement Routing for Satellite-Aerial-Terrestrial Quantum Networks
  Zhang, Y., Gong, Y., Fan, L., Wang, Y., Han, Z. and Guo, Y., 2025, August. Efficient entanglement routing for satellite-aerial-terrestrial quantum networks. In 2025 34th International Conference on Computer Communications and Networks (ICCCN) (pp. 1-9). IEEE.
  Co-Design of Network Topology and Qubit Allocation for Distributed Quantum Computing
Conclusions

## Slide 33
System Model
33
We have source-destination pairs of terrestrial base stations. Each pair is denoted by a tuple
Each pair requests quantum entanglement
  Quantum key distribution
  Distributed quantum computing
Goal: Maximize SATQN throughput, i.e., end-to-end entanglement generation rate (EGR)
Present it by a graph
  nodes
  sets of satellites , aerial platforms , and terrestrial base station
  links between nodes
  Storage node set Each has storage capacity

## Slide 34
Model Details
34
Loss and noise model between node and
Fiber optical transmittance
Free Space Optical Transmittance
distance
turbulence-induced transmittance
receiver’s efficiency
atmospheric loss
ideal density matrix
Fidelity
ideal entangled state

## Slide 35
Model Details
35
Imperfect entanglement swapping
required purification steps
success probability of step
source-destination pair target fidelity
the end-to-end fidelity of pair along path , which consists of links ℰ and nodes
fidelity parameters related with

## Slide 36
Problem Formulation
36
– path selection
– EGR
– average number of EPR pairs storage
the aggregate weighted EGR across all user pairs, all path, and all time intervals
path selection constraints
storage and channel capacity constraints
fidelity and balance constraints

## Slide 37
Problem Reformulation
37
– path selection
: – EGR; – average number of EPR pairs storage
It is a mix-integer linear problem (MILP)!
Quantum network throughput
Path selection, channel, storage, fidelity, and flow constraints

## Slide 38
Benders’ Decomposition
38
Fix the binary variables and construct the linear subproblem
Fix the continuous variables and construct the mix-integer linear master problem
Upper Bound
Lower Bound
Optimality and feasibility cuts
Binary variables
Problem P1

## Slide 39
Experiments
39
Proposed scheme can better utilize the storage capacity
Proposed scheme has larger network throughput
We consider an SATQN consisting of 2 satellites, 2 HAPs, and 12 terrestrial base stations
Baselines
  Satellite-Only Scheme (SOS): All entanglement requests are managed by satellites
  Random Routing Scheme (RRS): EGR is optimized, while the routing path is randomly selected
  No-Storage Scheme (NSS): None of the nodes has storage capacity

## Slide 40
Outline
40
Background
  Quantum Communication and Networking
  Quantum Computing
  Limitations of ground-based quantum entanglement distribution
  Ariel Access Networks
Joint Optimization of Qubit Allocation, Entanglement Routing, and Quantum Computing
  Optimizing Satellite-based Entanglement Distribution in Quantum Networks via Quantum-Assisted Approaches
  Efficient Entanglement Routing for Satellite-Aerial-Terrestrial Quantum Networks
  Co-Design of Network Topology and Qubit Allocation for Distributed Quantum Computing
  Liu, J., Fan, L., Guo, Y., Han, Z. and Wang, Y., 2025, March. Co-Design of Network Topology and Qubit Allocation for Distributed Quantum Computing. In 2025 International Conference on Quantum Communications, Networking, and Computing (QCNC) (pp. 355-362). IEEE.
Conclusions

## Slide 41
Overview
41
Qubit Interaction Graph G’(Q,C)
logical qubit
qubit allocation
q1
q5
number of CNOT gate operation between two logical qubits
q3
q4
q2
Quantum Network G(V,E)
v1
v2
v3
v4
final topology
2
1
1
1
2
Quantum Circuit
q1
q2
q3
q4
q5
Y
H
X
H
  Entangled qubits enables remote quantum gates and teleportation-based communication
  Qubit allocation requires balancing local processing and remote operations.
  Network topology affects entanglement fidelity and cost of served entangled qubits.
Quantum circuits describe quantum algorithms
Single qubit gates + CNOT are universal
Qubit Interaction Graph (QIG) captures all inter-qubit communications
Exactly a graph partition problem, which is NP-hard

## Slide 42
Objective
42
Objective: minimizing the total communication costs among all QPUs (after assignment)
QPU pairs
communication between single QPU pair
single path cost
edge cost (e.g., distance)
whether edge (u, z) is included in the path between QPUs (i, j)
CNOT gate demand between qubits (a, b)
qubits (a, b) are assigned to QPUs (i, j)

## Slide 43
Constraints
43
43
1. Each qubit should be assigned to
exactly one QPU
2. Each QPU holds a limited number of qubits
Edge (u, z) is not used by any path
Qubit Allocation
Edge (u, z) is not used by the path between (i, j)
3. Each QPU connects to a limited number of edges
4. The total number of edges cannot exceed
Topology Sparsity

## Slide 44
Shortest Paths
44
In degree - out degree for the destination node
In degree - out degree for middle nodes
In degree - out degree for the source node
5-7. Modified from the typical flow/path constraints
8. The length of each path should not exceed
Entanglement Path

## Slide 45
Reformulations
45
Edge Existence
Demand Existence
Reduce from to linear
Reduce from cubic to quadratic
All constraints reduced to at most quadratic (as it is unlikely to reduce to linear)
Objective is still cubic
: whether edge (u,z) is used
: there are communications between QPUs (i, j)

## Slide 46
Evaluations
46
In all cases, TACO-L is the most efficient and finds the best objective
TACO-NL performs worse than TACO, which means the latest automatic linearization feature of Gurobi should be used carefully
Larger circuit and quantum network lead to higher communication cost
TACO: original formulation
TACO-NL: original formulation with high order expression by Guoibi
TACO-L: proposed simplified formulation

## Slide 47
Conclusion
47
Quantum Communication Resource Allocation helped by Quantum Computing
Quantum Computing helped by Quantum Communication

## Slide 48
48
Thank you and visit our lab
48
48
http://wireless.egr.uh.edu/
http://www2.egr.uh.edu/~zhan2
Videos, slides and codes can be found