## Slide 1
Hybrid Satellite-Ground Quantum Networks and Computing
Yu Wang · Temple University Lei Fan, Zhu Han · University of Houston Yuanxiong Guo · University of Texas at San Antonio

## Slide 2
Schedule of This Tutorial
1
Introduction to Hybrid Satellite-Ground Quantum Networks
Motivation, background, and overall system of satellite-ground QN
2
Hybrid Quantum-Classical Computing Framework
Key concepts and techniques used by hybrid QC computing to solve optimization problems
3
Entanglement Distribution in Hybrid Satellite-Ground Quantum Networks
How to use satellite to provide entanglement for ground quantum networks
4
Entanglement Routing in Hybrid Satellite-Ground Quantum Networks
How to routing entanglement in satellite-ground quantum networks
5
Distributed Quantum Computing via Hybrid Satellite-Ground Quantum Networks
How to support distributed quantum computing in hybrid quantum networks
2

## Slide 3
SECTION 1
Introduction
Motivation, background, and overall system of satellite-ground QN
3
Hybrid Satellite-Ground Quantum Networks and Computing

## Slide 4
Outline
1
Quantum Network
2
Quantum Computing and Distributed Quantum Computing
3
Satellite-Ground Communication
4
Satellite-Assisted Quantum Networks
5
Satellite-Ground Quantum Computing
4

## Slide 5
Quantum Network
Quantum Computing
Distributed Quantum Computing
Satellite-Ground Communications
Satellite Assisted Quantum Networks
INTRODUCTION
Quantum Network and Computing
Satellite-Ground Quantum Computing
Transmit quantum information between nodes,
using quantum phenomena superposition and entanglement
No bits, but qubits
Bits
Qubits
Quantum teleportation
Bit. [Online]. Available: https://www.computerhope.com/jargon/b/bit.htm
What is a qubit. [Online]. Available: https://www.quantum-inspire.com/kbase/what-is-a-qubit/
Teleportation is real, thanks to quantum entanglement. [Online]. Available: https://www.popularmechanics.com/science/a25699/how-quantum-teleportation-works/
5

## Slide 6
Quantum Network
Quantum Computing
Distributed Quantum Computing
Satellite-Ground Communications
Satellite Assisted Quantum Networks
INTRODUCTION
3
Satellite-Ground Quantum Computing
Quantum Network
Entanglement Generation and Swapping
Stage 1: Alice and Bob generate an Einstein-Podolsky-Rosen (EPR) pair and send one qubit from their respective pairs to Carol
(a) Entanglement generation
(b) Entanglement swapping
(c) Entanglement established
Stage 2: Carol performs a Bell-state measurement (BSM) and transmits the result to Bob, i.e., entanglement swapping
Stage 3: Alice and Bob are entangled
6

## Slide 7
Quantum Network
Quantum Computing
Distributed Quantum Computing
Satellite-Ground Communications
Satellite Assisted Quantum Networks
INTRODUCTION
3
Satellite-Ground Quantum Computing
Terrestrial Quantum Network (TQN)
  Utilize optical fiber links
  Exponential increase in photon loss with distance
  Terrestrial repeaters perform entanglement swapping and purification to ensuring high fidelity
Limited Coverage
Constrained scalability
Inefficient communication
7

## Slide 8
Quantum Network
Quantum Computing
Distributed Quantum Computing
Satellite-Ground Communications
Satellite Assisted Quantum Networks
INTRODUCTION
3
Satellite-Ground Quantum Computing
Limitations of ground-based quantum entanglement distribution
Signal attenuation and decoherence: Entanglement is fragile and easily disrupted by loss and noise during transmission.
Distance constraints: Reliable entanglement maintenance is limited over long ground-based distances.
Environmental interference: Electromagnetic noise, temperature shifts, and vibrations degrade quantum stability.
Device imperfections: Hardware errors and component flaws reduce entanglement fidelity.
Security risks: Protecting entanglement channels from eavesdropping and attacks remains difficult.
Cost and scalability: High implementation costs and complex maintenance hinder large-scale deployment.
8

## Slide 9
Quantum Network
Quantum Computing
Distributed Quantum Computing
Satellite-Ground Communications
Satellite Assisted Quantum Networks
INTRODUCTION
3
Satellite-Ground Quantum Computing
9

## Slide 10
Quantum Network
Quantum Computing
Distributed Quantum Computing
Satellite-Ground Communications
Satellite Assisted Quantum Networks
INTRODUCTION
3
Satellite-Ground Quantum Computing
NP-hard Optimization Problems
e. g. Maximum Likelihood MIMO Detection Using Quantum Computing
Quantum Computing: use quantum mechanics to solve problems too complex for classical computers.
MIMO Detection
Resource Allocation
. . .
Network Slicing
[2] M. Kim, D. Venturelli, and K. Jamieson, “Leveraging quantum annealing for large MIMO processing in centralized radio access networks,” in Proceedings of the ACM Special Interest Group on Data Communication, Beijing, China, Aug. 2019.
[2]
Network Slicing
Network
Function Virtualization
. . .
Quantum Computing:
10

## Slide 11
Quantum Network
Quantum Computing
Distributed Quantum Computing
Satellite-Ground Communications
Satellite Assisted Quantum Networks
INTRODUCTION
3
Satellite-Ground Quantum Computing
Quantum Computer
Gate Model
Analog Quantum Model
Quantum Annealing
More Qubits
Faster than classical solvers
Fit some optimization problems
Maybe we need to use quantum mechanics in our computers.
11

## Slide 12
Quantum Network
Quantum Computing
Distributed Quantum Computing
Satellite-Ground Communications
Satellite Assisted Quantum Networks
INTRODUCTION
3
Satellite-Ground Quantum Computing
What is wrong in classic computing?
Many Practical NP hard Problems
Total number of combinations exponentially grows
Manufacturing & Logistics
Financial Services
Life science
12

## Slide 13
Quantum Network
Quantum Computing
Distributed Quantum Computing
Satellite-Ground Communications
Satellite Assisted Quantum Networks
INTRODUCTION
3
Satellite-Ground Quantum Computing
Known Types of Quantum Computing and Their Applications and Generality.
Application: | Optimization
Generality : | Restrictive
Application: | Chemistry Sampling Quantum Dynamics
Generality : | Partial
Application: | Cryptography Searching Secure Computing
Generality : | High
13

## Slide 14
Quantum Network
Quantum Computing
Distributed Quantum Computing
Satellite-Ground Communications
Satellite Assisted Quantum Networks
INTRODUCTION
3
Satellite-Ground Quantum Computing
Gate Level Quantum Computing
14

## Slide 15
Quantum Network
Quantum Computing
Distributed Quantum Computing
Satellite-Ground Communications
Satellite Assisted Quantum Networks
INTRODUCTION
3
Satellite-Ground Quantum Computing
Heat the metal to a temperature;
Lower the temperature;
Annealing a Metal
Simulated Annealing
Heuristic algorithm;
Random search method;
The temperature variable;
Quantum tunneling
Quantum Annealing
Enables jumping from one classical state to another
– Decreases likelihood of getting stuck in a local minimum
Width of energy barrier is important, but height is not
Quantum Annealing
15

## Slide 16
Quantum Network
Quantum Computing
Distributed Quantum Computing
Satellite-Ground Communications
Satellite Assisted Quantum Networks
INTRODUCTION
3
Satellite-Ground Quantum Computing
Superposition
Tensor Product
Qubits and Quantum Operation
16

## Slide 17
Quantum Network
Quantum Computing
Distributed Quantum Computing
Satellite-Ground Communications
Satellite Assisted Quantum Networks
INTRODUCTION
3
Satellite-Ground Quantum Computing
Before studying quantum
after studying quantum
Schrödinger Equation
17

## Slide 18
Quantum Network
Quantum Computing
Distributed Quantum Computing
Satellite-Ground Communications
Satellite Assisted Quantum Networks
INTRODUCTION
3
Satellite-Ground Quantum Computing
Problem of Hamiltonian:
Goal (what the hardware does)
  Minimize σi ∈ {-1, +1} subject to provided Ji,j ∈ R and hi ∈ R coefficients
  In other words, a quantum optimization program is merely a list of Ji,j and hi
Classical
  Much easier to reason than a quantum Hamiltonian
  Quantum effects are used internally to work towards the goal
Sparsely connected
  Possible to map fully connected problems onto the D-Wave’s Chimera graph
Dwave Hamiltonian
18

## Slide 19
Quantum Network
Quantum Computing
Distributed Quantum Computing
Satellite-Ground Communications
Satellite Assisted Quantum Networks
INTRODUCTION
3
Satellite-Ground Quantum Computing
QUBO (Quadratic Unconstrained Binary Optimization)
These important optimization problems can be transformed into QUBO model:
Quantum Computing:
provide an alternative method to solve some NP-hard problems
Knapsack Problems
Assignment Problems
Task Allocation Problems
Capital Budgeting Problems
… (NP-hard problem)
Ising Model
: upper-diagonal matrix
Spins interact with applied field
Neighboring spins interact with each other
Core idea: Encoding the objective function as the eigenvalue of the final ground state of Schrodinger equation, based on Adiabatic Quantum Computing Model
Chimera
Pegasus
Link Schrodinger with QUBO Model
19

## Slide 20
Quantum Network
Quantum Computing
Distributed Quantum Computing
Satellite-Ground Communications
Satellite Assisted Quantum Networks
INTRODUCTION
3
Satellite-Ground Quantum Computing
Considering only the external field:
We arbitrarily call σz = +1 “TRUE” and σz = —1 “FALSE”
Here are the optimal values of σz for different values of h
Observations
– A negative hi means, “I want σz to be TRUE”
– A zero hi means, “I don’t care if σz is TRUE or FALSE”
– A positive hi means, “I want σz to be FALSE”
QUBO Equation
20

## Slide 21
Quantum Network
Quantum Computing
Distributed Quantum Computing
Satellite-Ground Communications
Satellite Assisted Quantum Networks
INTRODUCTION
3
Satellite-Ground Quantum Computing
Consider only the coupler strengths:
Here are the optimal values of σz and σz for different values of Ji,j:
Observations
  A negative Ji,j means, “I want σz and σz to be equal”
i j
  A zero Ji,j means, “I don’t care how σz and σz are related”
i j
  A positive Ji,j means, “I want σz and σz to be different”
i j
Best answer appear with high probability
but not 100%, which is Achilles’ heel for
many quantum algorithms but not ours
QUBO Equation
21

## Slide 22
Quantum Network
Quantum Computing
Distributed Quantum Computing
Satellite-Ground Communications
Satellite Assisted Quantum Networks
INTRODUCTION
3
Satellite-Ground Quantum Computing
Inputs’ energy are set.
Lowest energy is at or closes to the optima.
Energy → possibility
Initial Qubits
Superposition at |s and |s.
Not yet coupled.
Qubits are entangled.
At state of many possible answers.
Couplers & biases applied
A matter of microseconds.
Energy diagram in Quantum Annealing
QUBO Quantum Annealing
22

## Slide 23
Quantum Network
Quantum Computing
Distributed Quantum Computing
Satellite-Ground Communications
Satellite Assisted Quantum Networks
INTRODUCTION
3
Satellite-Ground Quantum Computing
or
?
Master Problem
Subproblem
solution
Hybrid GPU and Quantum Computing
using Benders' Decomposition for Mixed Integer Programming
23

## Slide 24
Quantum Network
Quantum Computing
Distributed Quantum Computing
Satellite-Ground Communications
Satellite Assisted Quantum Networks
INTRODUCTION
3
Satellite-Ground Quantum Computing
24

## Slide 25
Quantum Network
Quantum Computing
Distributed Quantum Computing
Satellite-Ground Communications
Satellite Assisted Quantum Networks
INTRODUCTION
Distributed Quantum Computing
3
Satellite-Ground Quantum Computing
What is Distributed Quantum Computing (DQC)?
  Multiple interconnected quantum processors (QPUs) work together to solve large-scale computational problems
Why DQC?
  single QPUs have limited qubits
  monolithic large QPU is very hard to build
  a pathway to large-scale quantum computing
Challenges in DQC
  Qubit allocation/Circuit partition: distribution and management of qubits across multiple QPUs to optimize communication and execution time
  Quantum network function: serve high-quality & low-latency connections among quantum nodes to for remote operations
25

## Slide 26
Quantum Network
Quantum Computing
Distributed Quantum Computing
Satellite-Ground Communications
Satellite Assisted Quantum Networks
INTRODUCTION
Distributed Quantum Computing
3
Satellite-Ground Quantum Computing
Qubit Interaction Graph G’(Q,C)
logical qubit
qubit allocation
q1
q5
number of CNOT gate operation between two logical qubits
q3
q4
q2
Quantum Network G(V,E)
v1
v2
v3
v4
final topology
2
1
1
1
2
Quantum Circuit
q1
q2
q3
q4
q5
Y
H
X
H
  Entangled qubits enables remote quantum gates and teleportation-based communication
  Qubit allocation requires balancing local processing and remote operations.
  Network topology affects entanglement fidelity and cost of served entangled qubits.
Quantum circuits describe quantum algorithms
Single qubit gates + CNOT are universal
Qubit Interaction Graph (QIG) captures all inter-qubit communications
Exactly a graph partition problem, which is NP-hard
26

## Slide 27
Quantum Network
Quantum Computing
Distributed Quantum Computing
Satellite-Ground Communications
Satellite Assisted Quantum Networks
INTRODUCTION
3
Satellite-Ground Quantum Computing
27

## Slide 28
Quantum Network
Quantum Computing
Distributed Quantum Computing
Satellite-Ground Communications
Satellite Assisted Quantum Networks
INTRODUCTION
3
Satellite-Ground Quantum Computing
28

## Slide 29
Quantum Network
Quantum Computing
Distributed Quantum Computing
Satellite-Ground Communications
Satellite Assisted Quantum Networks
INTRODUCTION
3
Satellite-Ground Quantum Computing
29

## Slide 30
Quantum Network
Quantum Computing
Distributed Quantum Computing
Satellite-Ground Communications
Satellite Assisted Quantum Networks
INTRODUCTION
Satellite-Ground Quantum Networking and Computing
3
Satellite-Ground Quantum Computing
Space-Aerial-Terrestrial Quantum Networks (SATQNs)
SATQN has three layers
  Space quantum network enables long-distance entanglement distribution via free space optical links
  Aerial quantum network supports flexible and rapid deployment using free space optical links
  Terrestrial quantum network offers stable quantum connections via optical fiber links
30

## Slide 31
Quantum Network
Quantum Computing
Distributed Quantum Computing
Satellite-Ground Communications
Satellite Assisted Quantum Networks
INTRODUCTION
AI in Space
3
Satellite-Ground Quantum Computing
31

## Slide 32
Quantum Network
Quantum Computing
Distributed Quantum Computing
Satellite-Ground Communications
Satellite Assisted Quantum Networks
INTRODUCTION
AAN Standardization in 3GPP
3
Satellite-Ground Quantum Computing
2017
Release 14
3GPP TR 22.822
Three Use Cases of AAN
Concept of satellite network access
2020
Release 16
Adapting New Radio to support AAN
Necessary features including architecture, higher-layer protocols, and physical layer aspects
3GPP TR 38.821
2019
Release 15
5G enabled AAN
Study on deployment scenarios, key parameters, and channel models
3GPP TR 38.811
2021
Release 17
3GPP TR 38.863
Time, synchronization, and HARQ enhancement; mobility management; switch-over; signaling
New Radio specifications for AAN
2022
Release 18
Coverage enhancement; mobility and service continuity enhancement; deployment in higher bands
Integration with 5G Enhanced
3GPP TR 38.882
2025
Release 19
Regenerative payload for AAN; GNSS-independent access; store-and-forward; RedCap UE support
AAN Deep Integration Enhancement
3GPP TR 21.919
GNSS-resilient AAN operation; IoT AAN Phase 4; 6G AAN architecture study initiated
AAN Native Integration for 6G
2026 Ongoing
Release 20
32

## Slide 33
Quantum Network
Quantum Computing
Distributed Quantum Computing
Satellite-Ground Communications
Satellite Assisted Quantum Networks
INTRODUCTION
Satellite-assisted Quantum Networks (SATQN)
3
Satellite-Ground Quantum Computing
Overcoming distance limits: Satellites enable global-scale entanglement distribution beyond ground-based range.
Reduced signal loss: Space offers minimal attenuation and interference for more reliable quantum transmission.
Broad coverage: Satellites connect remote and inaccessible regions lacking ground infrastructure.
Freedom from obstacles: Signals are unaffected by terrain, buildings, or other terrestrial barriers.
Global quantum networking: Satellite links are essential for secure, worldwide quantum communication.
Complementary integration: Satellite systems enhance and extend ground-based quantum networks
33

## Slide 34
Quantum Network
Quantum Computing
Distributed Quantum Computing
Satellite-Ground Communications
Satellite Assisted Quantum Networks
INTRODUCTION
SATQN Applications
3
Satellite-Ground Quantum Computing
Time-insensitive applications
  Support long-term stream of entanglements
  Require secure communications
  Steady stream of entanglement over time
  E.g., Quantum key distribution (QKD)
Distributed quantum phase estimation with entangled photons. [Online]. Available: https://www.nature.com/articles/s41566-020-00718-2
Quantum Key Distribution Technology. [Online]. Available: https://www.drishtiias.com/daily-updates/daily-news-analysis/quantum-key-distribution-technology/print_manually
Time-sensitive applications
  Complete tasks as quickly as possible
  Avoid information decoherence due to noise or delay
  E.g., Distributed quantum computing (DQC)
34

## Slide 35
Quantum Network
Quantum Computing
Distributed Quantum Computing
Satellite-Ground Communications
Satellite Assisted Quantum Networks
INTRODUCTION
Challenges in SATQNs
3
Satellite-Ground Quantum Computing
Complex Integration
free space optical links and optical fiber links
Decoherence and Errors
noise in quantum channels and imperfections in quantum operations
35

## Slide 36
Quantum Network
Quantum Computing
Distributed Quantum Computing
Satellite-Ground Communications
Satellite Assisted Quantum Networks
INTRODUCTION
Satellite-Assisted Quantum Networks
3
Satellite-Ground Quantum Computing
Simplified example of a satellite-assisted quantum network.
The quantum repeaters are depicted as nodes, connected via fiber links.
Dedicated ground stations (satellite dishes) have both fiber and satellite connections.
Link colors represent entanglement generation probability, with blue indicating higher probability (shorter links) transitioning to red for lower probability (longer links).
Arxiv: SatQNet: Satellite-assisted Quantum Network Entanglement Routing Using Directed Line Graph Neural Networks
36

## Slide 37
Quantum Network
Quantum Computing
Distributed Quantum Computing
Satellite-Ground Communications
Satellite Assisted Quantum Networks
INTRODUCTION
Satellite-Ground Quantum Computing
3
Satellite-Ground Quantum Computing
Quantum Key Distribution (QKD): Satellites send fragile light particles (photons) to ground stations to create unbreakable encryption keys.
Space-Based Advantage: Photons travel through empty space with very little loss or interference, unlike ground fiber-optic cables that degrade over long distances.
Entanglement: Low-Earth-orbit satellites generate and split pairs of linked photons, sending one half to the ground and keeping or sending the other elsewhere to connect remote networks.
https://www.linkedin.com/pulse/how-quantum-computing-could-transform-satellite-ground-kiran-kolipaka-oqpgc
37

## Slide 38
Quantum Network
Quantum Computing
Distributed Quantum Computing
Satellite-Ground Communications
Satellite Assisted Quantum Networks
INTRODUCTION
Satellite-Ground Quantum Computing
3
Satellite-Ground Quantum Computing
Global Security: Creating hack-proof communication networks across continents.
Distributed Computing: Linking separate quantum computers together via space relays.
Quantum Sensing: Improving environmental monitoring and timing precision from space
Boeing’s Q4S Mission
SPOQC Mission (UK)
IonQ & Skyloom
Infrastructure
EAGLE-1 & SAGA (European Space Agency)
Micius (Mozi) Satellite (China)
38

## Slide 39
Schedule of This Tutorial
1
Introduction to Hybrid Satellite-Ground Quantum Networks
Motivation, background, and overall system of satellite-ground QN
2
Hybrid Quantum-Classical Computing Framework
Key concepts and techniques used by hybrid QC computing to solve optimization problems
3
Entanglement Distribution in Hybrid Satellite-Ground Quantum Networks
How to use satellite to provide entanglement for ground quantum networks
4
Entanglement Routing in Hybrid Satellite-Ground Quantum Networks
How to routing entanglement in satellite-ground quantum networks
5
Distributed Quantum Computing via Hybrid Satellite-Ground Quantum Networks
How to support distributed quantum computing in hybrid quantum networks
2
39

## Slide 40
SECTION 2
Hybrid Quantum-Classical Computing Framework
Key concepts and techniques used by hybrid QC computing to solve optimization problems
Hybrid Satellite-Ground Quantum Networks and Computing

## Slide 41
Outline
1
Quantum Optimization Algorithms
Key math foundations and principles
2
Hybrid Quantum Classical Computing
Key concepts and workflow
3
Hybrid Quantum-Classical Application
Simulation Results
4
Conclusion
41

## Slide 42
Q Algorithm
HyQC
Application
Conclusion
Quantum Quantum Optimization Algorithms
Hamiltonian Simulation on Quantum Computer
Evolution from to .
: the actual state of the system
: a time-dependent Hamiltonian (i.e., Kinetic energy + Potential Energy)
: the instantaneous eigenstate
: the instantaneous eigenvalue
Evolution (Path)
Energy
Classical path
Tunnel effect
Solution
42

## Slide 43
Q Algorithm
HyQC
Application
Conclusion
Quantum Optimization Algorithms
*Encode the objective function in the final Hamiltonian of the Quantum System
QUBO (Quadratic Unconstrained Binary Optimization)
Final Hamiltonian
Q: Upper triangular matrix : Binary variable
 | : Pauli matrices operating on qubit .
 | : qubit biases
 | : coupling strengths.
 | : qubit biases
 | : coupling strengths.
43

## Slide 44
Q Algorithm
HyQC
Application
Conclusion
Quantum Optimization Algorithms
*Encode the objective function in the final Hamiltonian of the Quantum System
Time Dependent Hamiltonian
44

## Slide 45
Q Algorithm
HyQC
Application
Conclusion
INTRODUCTION
Quantum Adiabatic Algorithm
45

## Slide 46
Q Algorithm
HyQC
Application
Conclusion
Hybrid Quantum Classical Optimization Algorithms
Hybrid QPU-CPU Algorithm Design
Leverage Classical Optimization Frameworks
  Build on proven decomposition and convex optimization methods to ensure scalability, stability, and interpretability
Identify Quantum-Ready Problem Structures
  Extract discrete, combinatorial, or non-convex components that can be efficiently mapped to quantum processors (QPU) while keeping continuous parts classical.
Accelerate While Preserving Guarantees
  Integrate quantum modules to speed up computation without compromising theoretical properties such as convergence, feasibility, and optimality.
QPU
QPU
QPU
On QPU:
Quantum Adiabatic Algorithm
Quantum Hamiltonian Descent
On CPU:
Linear Programming
Convex optimization
Dual Updates
46

## Slide 47
Q Algorithm
HyQC
Application
Conclusion
Hybrid Quantum Classical Optimization Algorithms
Hybrid Quantum Classical Benders’ Decomposition
Optimality/Feasibility Cuts
Integer Solutions
Master Problem
Sub Problem
Ising Model
Quadratic Penalty
Hamiltonian
Formulation
Zhao, Zhongqi, Lei Fan, and Zhu Han. "Hybrid quantum benders’ decomposition for mixed-integer linear programming." 2022 IEEE Wireless Communications and Networking Conference (WCNC). IEEE, 2022.
47

## Slide 48
Q Algorithm
HyQC
Application
Conclusion
Hybrid Quantum Classical Optimization Algorithms
Hybrid Quantum Multi-Cut Benders’ Decomposition
Quantum algorithm returns multiple solutions after solving the master problem
Each integer solution produce a subproblem, which further returns an optimality/feasibility cut
Reduce the number of iterations and speed up the convergence
Zhao, Zhongqi, Mingze Li, Lei Fan, and Zhu Han. "HQC-Bend: A Python Package of Hybrid Quantum-Classical Multi-cuts Benders’ Decomposition Algorithm." In 2025 International Conference on Quantum Communications, Networking, and Computing (QCNC), pp. 591-597. IEEE, 2025.
48

## Slide 49
Q Algorithm
HyQC
Application
Conclusion
Hybrid Quantum Classical Optimization Algorithms
Dantzig-Wolfe (DW) Decomposition
Wei, Xinliang, Jiyao Liu, Lei Fan, Yuanxiong Guo, Zhu Han, and Yu Wang. "Hybrid quantum-classical computing via Dantzig-Wolfe decomposition for integer linear programming." In 2024 33rd international conference on computer communications and networks (ICCCN), pp. 1-9. IEEE, 2024.
A. Integer Linear Programming
Block structure
…
…
B. Dantzig-Wolfe (DW) Decomposition
Let
if is bounded or unbounded, can also be represented by a linear combination of vertices and polar rays of .
if is bounded, can be expressed as a convex combination of the vertices of .
49

## Slide 50
Q Algorithm
HyQC
Application
Conclusion
Hybrid Quantum Classical Optimization Algorithms
Dantzig-Wolfe (DW) Decomposition
Wei, Xinliang, Jiyao Liu, Lei Fan, Yuanxiong Guo, Zhu Han, and Yu Wang. "Hybrid quantum-classical computing via Dantzig-Wolfe decomposition for integer linear programming." In 2024 33rd international conference on computer communications and networks (ICCCN), pp. 1-9. IEEE, 2024.
Master Problem
if is bounded:
if is bounded or unbounded:
-th Subproblem
Three cases:
The optimal target value is . In this case, and the solution of the subproblem is the extreme ray , and then we add to the master problem for next round calculation.
The optimal target value is bounded and . In this case, and the solution of the subproblem is the extreme point , and then we add to the master problem for next round calculation.
The optimal target value is bounded and . In this case, , and , and therefore we find the optimal solution.
50

## Slide 51
Q Algorithm
HyQC
Application
Conclusion
Hybrid Quantum Classical Optimization Algorithms
Dantzig-Wolfe (DW) Decomposition
Wei, Xinliang, Jiyao Liu, Lei Fan, Yuanxiong Guo, Zhu Han, and Yu Wang. "Hybrid quantum-classical computing via Dantzig-Wolfe decomposition for integer linear programming." In 2024 33rd international conference on computer communications and networks (ICCCN), pp. 1-9. IEEE, 2024.
51

## Slide 52
Q Algorithm
HyQC
Application
Conclusion
APPLICATION · CASE STUDY
One SAGIN snapshot couples four resource decisions
Wei, Xinliang, Jiyao Liu, Lei Fan, Yuanxiong Guo, Yanmin Gong, Zhu Han, and Yu Wang. "Quantum-Assisted Resource Management for Data Access in Space-Air-Ground Integrated Networks." IEEE Transactions on Wireless Communications (2025).
Hybrid Satellite-Ground Quantum Networks and Computing | QCE '26
JOINT DECISION VECTOR
x
User association x, y, z
Connect each Mobile User to at most one terrestrial Base Station (TBS), HAP, or LEO. Binary
η
High-altitude Platform(HAP) cache placement η
Store requested items subject to each HAP's capacity. Binary
ξ
HAP location ξ
Choose one of two feasible locations; both links change. Binary
b
Bandwidth allocation b
Allocate continuous TBS-to-MU and LEO-to-MU bandwidth.
MODELING SCOPE
Centralized, snapshot-based, quasi-static channels
Fixed MU / LEO / TBS positions; perfect CSI
Each HAP selects one of two candidate locations
Direct TBS/LEO service competes with HAP service; an HAP cache miss also consumes LEO-HAP relay capacity.
Key coupling: HAP location changes access and backhaul; caching changes relay demand and user cost.
52
Notes: Open with the optimization snapshot. The controller jointly chooses association, HAP cache placement, one of two HAP locations, and TBS/LEO bandwidth. Emphasize that a location decision changes two paths at once, while an HAP cache miss creates both a relay-flow requirement and an extra utility cost.
[Sources]
- [Claim and asset] Wei et al., Fig. 1 and Sec. II, pp. 2-4, user-provided paper PDF.
- [Style] Session 1 Lei.pdf, user-provided visual reference.

## Slide 53
Q Algorithm
HyQC
Application
Conclusion
APPLICATION · MATHEMATICAL MODEL I
Rates, location, and caching define the utility
Wei et al., Eqs. (2)-(16), pp. 3-5; m(i) denotes the item requested by MU i.
BANDWIDTH-CONTROLLED ACCESS RATES
With channel and power fixed during the snapshot, these rates are linear in the optimized bandwidth b.
h: channel efficiency
HAP LOCATION CONTROLS TWO LINKS
The same ξ_k selects the MU-HAP access rate and the LEO-HAP backhaul rate.
r: achievable rate
RATE MINUS ACCESS AND CACHE-MISS COSTS
utility = delivered rate - association cost - HAP cache-miss cost
NETWORK OBJECTIVE
WHY P1 IS A MINLP
Products x·b and z·b gate bandwidth by association; y·η, y·ξ, and y·η·ξ couple HAP association, caching, and location.
53
Notes: Show why this is not four independent decisions. TBS and satellite rates are bandwidth-linear in the quasi-static snapshot. HAP location changes both access and backhaul rates. User utility subtracts an extra HAP relay cost when the requested item is not cached. The paper leaves the data index implicit in Eq. (14); m(i) is used here to denote the item requested by user i.
[Sources]
- [Claims] Wei et al., Secs. II-B, II-C, and III-A, Eqs. (2)-(16), pp. 3-5.
- [Notation clarification] The slide writes eta_{m(i),k} to make the paper's implicit requested-item index explicit.

## Slide 54
Q Algorithm
HyQC
Application
Conclusion
APPLICATION · MATHEMATICAL MODEL II
Linearization exposes a Benders-ready MILP
Wei et al., Eqs. (16a)-(20)
PHYSICAL FEASIBILITY IN P1
ASSOCIATION + SATELLITE CAPACITY
CACHE + BANDWIDTH BUDGETS
CACHE-MISS BACKHAUL FLOW
EXACT BINARY-PRODUCT LINEARIZATION
Representative exact hull for u = yη
The same 3-constraint pattern enforces v = uξ and w = yξ.
AUXILIARY BINARY GROWTH
Increase Binary Varaibles
Reformulated MILP Model
QPU master: X binary
CPU LP: Y = bandwidth
54
Notes: Group the constraints by physical role instead of reading all ten lines of P1. The nonlinearity is removed with exact auxiliary binaries. This adds 2MQO + MO binary variables, which is also why the QUBO grows quickly. Eq. (20) makes the decomposition boundary explicit: all binary choices are X, while continuous TBS/LEO bandwidth is Y.
[Sources]
- [Claims] Wei et al., Sec. III, Eqs. (16a)-(20), pp. 5-6.
- [Derived count] Auxiliary binary count 2MQO + MO follows directly from u, v, and w index ranges.

## Slide 55
Q Algorithm
HyQC
Application
Conclusion
APPLICATION · ALGORITHM
HyBD sends only the discrete master to the QPU
The classical Benders loop stays intact; quantum annealing acts as the binary master oracle and sample generator.
1 Build QUBO master
binary X + encoded ω + accumulated cuts
2 Sample on QPU
retain top σ feasible candidate solutions X'
3 Solve σ LPs on CPUs
recover bandwidth Y and dual point or ray
4 Add σ cuts
update upper/lower bounds and repeat
55
Notes: Be precise about the quantum role. The QPU does not solve continuous bandwidth allocation and does not replace Benders decomposition. It solves the current penalized binary master. CPUs validate each candidate by solving an LP or dual and generate optimality or feasibility cuts. HyBDM uses the top sigma feasible samples to solve sigma LPs in parallel and add sigma cuts per master iteration. The paper establishes no worst-case complexity reduction.
[Sources]
- [Claims] Wei et al., Sec. IV, Eqs. (22)-(28), Algorithms 1-2, pp. 6-8.
- [Penalty notation] The slide shows penalties with explicit subtraction for positive lambda; the paper's printed sign convention in Eqs. (26)/(28) is ambiguous.

## Slide 56
Q Algorithm
HyQC
Application
Conclusion
APPLICATION · SIMULATION AND HARDWARE RESULTS
Hardware tests match CBD with fewer Benders rounds
Benders rounds to convergence
TEST CASES tuple = {MU, TBS, HAP, LEO, data}
Case 1
{25, 5, 1, 1, 8}
621 reported logical binaries
Case 2
{25, 5, 2, 1, 5}
774 reported logical binaries
Case 3
{25, 3, 2, 2, 5}
749 reported logical binaries
D-Wave Leap + classical LP solver | Same optimal objective as CBD in the tested cases | RAND is lower
Case 3​
56
Notes: Use the exact table values. HyBD reaches the same tested objective as classical Benders with modest single-cut iteration reductions. The largest round reduction comes from HyBDM with five cuts: 14 to 5 in Case 1. The 82.8% timing figure is Case 3's average solver-access time, 167.3 to 28.81 ms. It is not end-to-end wall-clock time because setup, transfer, embedding, queue, and other overhead are excluded.
[Sources]
- [Results] Wei et al., Tables II-IV and Figs. 4-7, pp. 9-10.
- [Caveat] Solver-access-time definition and excluded overhead are stated on p. 10.
- [Consistency choice] The slide uses the reproducible 82.8% from Table III rather than the unexplained 93.0% sentence on p. 12.

## Slide 57
Q Algorithm
HyQC
Application
CONCLUSION
Hybrid Quantum Classical Computing
Conclusion
Select the right role for each processor
  QPU: hard tasks; CPU: convex optimization;
Decomposition provides the bridge
  Benders and Dantzig–Wolfe decomposition create a structured interface between quantum and classical computing
  Multiple QPU samples can generate multiple cuts in one iteration and reduce the number of decomposition rounds
The SAGIN case study demonstrates the workflow
  hybrid method reached the same optimal objective as classical Benders decomposition while requiring fewer Benders rounds
57
Notes: Use the exact table values. HyBD reaches the same tested objective as classical Benders with modest single-cut iteration reductions. The largest round reduction comes from HyBDM with five cuts: 14 to 5 in Case 1. The 82.8% timing figure is Case 3's average solver-access time, 167.3 to 28.81 ms. It is not end-to-end wall-clock time because setup, transfer, embedding, queue, and other overhead are excluded.
[Sources]
- [Results] Wei et al., Tables II-IV and Figs. 4-7, pp. 9-10.
- [Caveat] Solver-access-time definition and excluded overhead are stated on p. 10.
- [Consistency choice] The slide uses the reproducible 82.8% from Table III rather than the unexplained 93.0% sentence on p. 12.

## Slide 58
Schedule of This Tutorial
1
Introduction to Hybrid Satellite-Ground Quantum Networks
Motivation, background, and overall system of satellite-ground QN
2
Hybrid Quantum-Classical Computing Framework
Key concepts and techniques used by hybrid QC computing to solve optimization problems
3
Entanglement Distribution in Hybrid Satellite-Ground Quantum Networks
How to use satellite to provide entanglement for ground quantum networks
4
Entanglement Routing in Hybrid Satellite-Ground Quantum Networks
How to routing entanglement in satellite-ground quantum networks
5
Distributed Quantum Computing via Hybrid Satellite-Ground Quantum Networks
How to support distributed quantum computing in hybrid quantum networks
2
58

## Slide 59
SECTION 3
Entanglement Distribution in Hybrid Satellite-Ground Quantum Networks
How to use satellite to provide entanglement for ground quantum networks
Hybrid Satellite-Ground Quantum Networks and Computing

## Slide 60
Outline
1
Introduction
Motivation, background, and problem setup
2
System Model and Problem Formulation
Key concepts and definitions used throughout
3
Proposed HQCDW Algorithm
Main techniques covered in this tutorial
4
Evaluation
Applying the methods, evaluation highlights
5
Conclusion
Takeaways, open problems, and resources
2
60

## Slide 61
Introduction
Model and Problem
HQCDW Algorithm
Evaluation
Conclusion
INTRODUCTION
Satellite-based Entanglement Distribution
Limitations of ground-based quantum entanglement distribution
  Exponential photon loss in fiber (roughly 0.2 dB/km)
  Decoherence accumulates with distance (more swapping, more noise))
  Geographic and infrastructure constraints
An alternative way: satellite-based entanglement distribution
  Bypass many environmental factors, enable the creation of long-distance entangled links with higher fidelity
  Single “hop” replaces many repeater nodes
  Overcome the geographical constraints of ground-based systems
  Downward atmospheric path is shorter and more favorable
4
61

## Slide 62
Introduction
Model and Problem
HQCDW Algorithm
Evaluation
Conclusion
INTRODUCTION
Satellite-based Entanglement Distribution
  [1] Yin et al., “Satellite-based entanglement distribution over 1200 kilometers,” Science, vol. 356, no. 6343, Jun. 2017
  [2] Hiemstra et al. "The European satellite-based QKD system EAGLE-1." Free-space laser communications XXXVII. Vol. 13355. SPIE, 2025.
  [3] Merolla et al. "High-performance 1560 nm entangled photon source for high secure key rates QKD satellite-based communications." International Conf. on Space Optics—ICSO 2022. Vol. 12777. SPIE, 2023.
  [4] Mazzarella et al., “QUARC: Quantum research CubeSat—A constellation for quantum communication,” Cryptography, vol. 4, no. 1, p. 7, 2020
  [5] Hutterer, et al. "QUBE-II - Quantum Key Distribution with a CubeSat". 73rd International Astronautical Congress, IAC 2022
4
EAGLE-1 & SAGA (European Space Agency) [2&3]
Micius (Mozi) Satellite (China) [1]
QUARC (UK) [4]
QUBE II (Germany) [5]
62

## Slide 63
Introduction
Model and Problem
HQCDW Algorithm
Evaluation
Conclusion
INTRODUCTION
Optimization of Entanglement Distribution from Sky
Selecting an optimal satellite configuration for satellite-based entanglement distribution
  [1] Khatri et al., npj Quantum Inf., 2021
  [2] Panigraphy et al. INFOCOM workshop, 2022
  [3] Wei et al. IEEE Network, 2025
Satellite assignment xi,j to maximize the weighted utility
  Constraints on GS receivers (Rk), satellite transmitters (Ti), fidelity threshold (Fjth)
Solutions: Greedy[1], MIS-based[2] (only for special cases), MaxFlow-based[3] (for more general special cases), LP-based (opt but large time-complexity)
4
63

## Slide 64
Introduction
Model and Problem
HQCDW Algorithm
Evaluation
Conclusion
INTRODUCTION
Motivation & Contribution
Limitations and challenges of previous works
  a heuristic greedy algorithm and ignores some resource constraints
  only consider some specific settings by converting the problem into either a maximum weight independent set problem or a maximum weight bipartite matching problem
  without possible terrestrial swapping (which can improve feasibility of the problem)
Our work investigates a joint satellite assignment, resource allocation, and path selection scenario to build quantum entanglements for ground stations by leveraging satellite-based entanglement distribution and terrestrial quantum swapping.
  X. Wei, L. Fan, Y. Guo, Z. Han, Y. Wang, Entanglement from Sky: Optimizing Satellite-based Entanglement Distribution for Quantum Networks, IEEE/ACM Trans. on Networking (TON), Volume: 32, Issue: 6, Pages: 5295-5309, Dec. 2024.
4
Fig. 1. The satellite-based entanglement distribution and terrestrial quantum swapping architecture.
64

## Slide 65
Introduction
Model and Problem
HQCDW Algorithm
Evaluation
Conclusion
MODEL AND PROBLEM
System Model
Network Model
  satellites (SAT): 𝑀 = {1, · · · , |𝑀|}, 𝑠𝑚𝑖: quantum memory of SAT 𝑖, 𝑡𝑟𝑖: number of transmitters of SAT 𝑖.
  ground stations (GS): 𝑁 = {1, · · · , |𝑁|}, g𝑚𝑘: quantum memory of GS 𝑘, 𝑟𝑟𝑘: number of receivers of GS 𝑘.
  ground station pairs (GSP): 𝑂 = {1, · · · , |𝑂|}
Channel Model spontaneous parametric down-conversion (SPDC)
  space-to-ground transmittance:
  free-space transmittance:
  atmospheric transmittance:
4
Fig. 2. An example of the space-to-ground transmittance between one SAT and two GSs for the entanglement distribution to this GSP.
: the circular apertures of diameter of the transmitter and receiver telescopes
: the specific wavelength
: the atmospheric extinction coefficient
65

## Slide 66
Introduction
Model and Problem
HQCDW Algorithm
Evaluation
Conclusion
MODEL AND PROBLEM
System Model
Entanglement Model
  Either via satellite-based entanglement
  Or via GS swapping (limited to two-hop)
4
Fig. 1. The satellite-based entanglement distribution and terrestrial quantum swapping architecture.
66

## Slide 67
Introduction
Model and Problem
HQCDW Algorithm
Evaluation
Conclusion
MODEL AND PROBLEM
System Model
Satellite-to-Ground Entanglement
  The fidelity of entangled photon pair after transmission can be approximated by
Terrestrial Quantum Swapping
  The fidelities of the new states after swapping are defined below [2]
4
Fig. 2. An example of the space-to-ground transmittance between one SAT and two GSs for the entanglement distribution to this GSP.
is the initial fidelity of the entangled photon pair.
Assumptions[1]: ,
is the number of background photons received by GS .
and are the fidelities of two entanglement links, respectively.
[1] N. K. Panigrahy, P. Dhara, D. Towsley, S. Guha, and L. Tassiulas, “Optimal Entanglement Distribution using Satellite Based Quantum Networks,” in IEEE Conference on Computer Communications (INFOCOM) Workshops, Virtual, May 2022.
[2] A. Zang, X. Chen, A. Kolar, and J. Chung, “Entanglement Distribution in Quantum Repeater with Purification and Optimized Buffer Time,” in IEEE Conference on Computer Communications Workshops, New York, NY, May 2023.
67

## Slide 68
Introduction
Model and Problem
HQCDW Algorithm
Evaluation
Conclusion
MODEL AND PROBLEM
Problem Formulation
The joint satellite assignment, resource allocation, and path selection problem.
4
Objective: maximize the overall utility of all traffic GSPs
Satellite assignment or
Terrestrial quantum swapping
each GSP only connects to one satellite or only selects one swapping path if the satellite assignment is not available.
a GS can be part of multiple GSPs and thus is not allowed to be allocated to more than satellites.
SAT does not get allocated to more than GSPs.
the total entangled photon received from different satellites cannot exceed g.
the total entangled photon pair allocation fraction of SAT cannot exceed .
if a swapping path is selected, then two entanglement links along this path must be established based on the satellite assignment.
the fidelity of entanglement links after transmitting or swapping is larger than the fidelity threshold.
hard problem to solve
: if satellite is assigned to GSP ; : the entangled photon pair allocation;
: if path is selected to GSP ; : the entangled photon pair allocation.
68

## Slide 69
Introduction
Model and Problem
HQCDW Algorithm
Evaluation
Conclusion
HQCDW Algorithm
HQCDW ALGORITHM
4
Fig. 3. Proposed HQCDW framework for joint satellite-based quantum entanglement distribution and terrestrial quantum swapping.
69

## Slide 70
Introduction
Model and Problem
HQCDW Algorithm
Evaluation
Conclusion
HQCDW Algorithm
HQCDW ALGORITHM
4
① Linearization
② general form
③ reformulation
④ linear combination of extreme points
⑤ DW decomposition
Block
structure
70

## Slide 71
Introduction
Model and Problem
HQCDW Algorithm
Evaluation
Conclusion
Partial Linearization & Three DW Subprobelms
HQCDW ALGORITHM
4
71

## Slide 72
Introduction
Model and Problem
HQCDW Algorithm
Evaluation
Conclusion
EVALIATION
Evaluation Setting and Baselines
4
Network architecture
Comparison methods
Steepest Descent (SD) [3]: SD is a solver for binary quadratic models by D-Wave Systems with the best move determined through a local minimization.
Random Steepest Descent (RASD) [3]: RASD combines random sampling and steepest descent, with the algorithm using random sampling to generate initial states for SD.
Classical Optimizer (COPT): COPT solves the original problem (5) by using a classical optimizer (e.g., Gurobi, Scipy) in a classical CPU computer.
Classical DW Decomposition (CDWD): CDWD decouples the original problem using DW decomposition and solves all problems with a classical optimizer.
Parameters | Value
Number of SATs | 
Satellites altitude | 
Quantum memory of SATs | 
Number of transmitters | 
Number of GSs | 
Quantum memory of GSs | 
Number of transmitters | 
Parameters | Value
Satellites altitude | 
72

## Slide 73
Introduction
Model and Problem
HQCDW Algorithm
Evaluation
Conclusion
EVALIATION
Evaluation – Objective Value
4
This highlights the effectiveness and robustness of using DW decomposition to tackle larger network scales.
73

## Slide 74
Introduction
Model and Problem
HQCDW Algorithm
Evaluation
Conclusion
EVALIATION
Evaluation – Solver Accessing Time: QUBO-DW2
4
This analysis highlights the advantage of using the DW decomposition to overcome constraints imposed by the maximum number of qubits in the quantum machine.
74

## Slide 75
Introduction
Model and Problem
HQCDW Algorithm
Evaluation
Conclusion
EVALIATION
Evaluation – Solver Accessing Time: DW3 & PL
4
This analysis highlights the advantage of using the DW3 and PL to overcome constraints imposed by the maximum number of qubits in the quantum machine.
75

## Slide 76
Introduction
Model and Problem
HQCDW Algorithm
Evaluation
Conclusion
EVALIATION
Evaluation – Qubit Usage
4
This result highlights the benefits of DW decomposition (also partial linear) for larger-scale problems.
76

## Slide 77
Introduction
Model and Problem
HQCDW Algorithm
Evaluation
Conclusion
EVALIATION
Evaluation – Qubit Usage
4
The benefits of DW with three subproblems are further
77

## Slide 78
Introduction
Model and Problem
HQCDW Algorithm
Evaluation
Conclusion
CONCLUSION
Conclusion
Satellite-based entanglement distribution provides a great alternative way to support ground-based quantum networks
However, finding optimal satellite assignment is a challenging optimization problem in hybrid satellite-ground networks!
We studied a joint satellite assignment, resource allocation, and path selection for entanglement distribution within a satellite-ground network
We proposed a hybrid quantum-classical Dantzig-Wolfe decomposition technique by leveraging both quantum and classical computing to effectively solve large-scale network optimization challenges and balance qubit usage
Experiments provided compelling evidence of the efficiency and robustness of the proposed methods, with a stable solver accessing time and consistent results compared to classical optimizers
4
78

## Slide 79
Schedule of This Tutorial
1
Introduction to Hybrid Satellite-Ground Quantum Networks
Motivation, background, and overall system of satellite-ground QN
2
Hybrid Quantum-Classical Computing Framework
Key concepts and techniques used by hybrid QC computing to solve optimization problems
3
Entanglement Distribution in Hybrid Satellite-Ground Quantum Networks
How to use satellite to provide entanglement for ground quantum networks
4
Entanglement Routing in Hybrid Satellite-Ground Quantum Networks
How to routing entanglement in satellite-ground quantum networks
5
Distributed Quantum Computing via Hybrid Satellite-Ground Quantum Networks
How to support distributed quantum computing in hybrid quantum networks
2
79

## Slide 80
SECTION 4
Entanglement Routing/Service in Hybrid Satellite-Ground Quantum Networks
How to routing entanglement in satellite-ground quantum networks
Hybrid Satellite-Ground Quantum Networks and Computing

## Slide 81
Outline
1
Introduction
Motivation and background
2
Reliable Bell-Pair Routing
How can Bell entanglement be routed reliably across a heterogeneous satellite-ground QN?
3
Mixed Bell/GHZ Routing
How can one integrated network serve Bell and GHZ demands together?
4
Stochastic Infrastructure Planning
Conclusion
Summary and takeaways
What should be deployed before uncertain Bell/GHZ demand arrives?
5
81

## Slide 82
The core networking primitive is entanglement distribution—not classical packet forwarding.
Introduction
Bell Routing
Bell + GHZ
Planning
Conclusion
INTRODUCTION
Entanglement distribution is the core service
82
Transmit quantum information between nodes using quantum phenomena superposition and entanglement
No bits, but qubits
Bits
Qubits
Quantum entanglement of two qubits
  Reveal both by revealing either
  Even separated by a large distance
Quantum teleportation

## Slide 83
Introduction
Bell Routing
Bell + GHZ
Planning
Conclusion
INTRODUCTION
83
Step 1: Alice and Bob generate an Einstein-Podolsky-Rosen (EPR) pair and send one qubit from their respective pairs to Carol
Step 2: Carol performs a Bell-state measurement (BSM) and transmits the result to Bob
Step 3: Alice and Bob are entangled
Generation and swapping are probabilistic and consume quantum resources.
(a) Entanglement generation
(b) Entanglement swapping
(c) Entanglement established
Swapping extends entanglement across distance

## Slide 84
Introduction
Bell Routing
Bell + GHZ
Planning
Conclusion
INTRODUCTION
84
Fiber-only networks do not scale
Utilize optical fiber links
Exponential increase in photon loss with distance
Terrestrial repeaters perform entanglement swapping and purification to ensuring high fidelity
Limited Coverage
Constrained scalability
Inefficient communication
This motivates free-space satellite and aerial assistance.

## Slide 85
Introduction
Bell Routing
Bell + GHZ
Planning
Conclusion
INTRODUCTION
85
Satellite-Aerial-Terrestrial Quantum Networks (SATQN) has three layers
  Space quantum network enables long-distance entanglement distribution via free space optical links
  Aerial quantum network supports flexible and rapid deployment using free space optical links
  Terrestrial quantum network offers stable quantum connections via optical fiber links
SATQNs add aerial and space relays

## Slide 86
Introduction
Bell Routing
Bell + GHZ
Planning
Conclusion
INTRODUCTION
86
Ground-only candidate path
  Fiber links between ground stations (GS)
  Bell-state swapping at intermediate GSs
  Consumes GS qubits and fiber-channel capacity
  Good for nearby stations
Satellite-assisted candidate path
  GS–SAT uplink, SAT forwarding, SAT–GS downlink
  Consumes satellite lenses and endpoint GS qubits
  Limited by visibility and the number of optical lenses in satellite
  Useful for long-range connectivity
A path choice determines both its success probability and its hardware consumption.
Ground and satellite paths use distinct resources

## Slide 87
Introduction
Bell Routing
Bell + GHZ
Planning
Conclusion
INTRODUCTION
87
Bell-state service: Bipartite entanglement between two nodes
  Two terminals
  One bipartite entangled state
  Source–destination service
  Natural for pairwise communication
GHZ-state service: Multipartite entanglement among a group of nodes
  Three or more terminals
  One shared multipartite entangled state
  Group service
  Natural for group-oriented applications
The requested entanglement state determines the structure of the networking problem.
A
B
one pairwise link
A
B
C
one shared multipartite state
Bell and GHZ services require different structures

## Slide 88
Introduction
Bell Routing
Bell + GHZ
Planning
Conclusion
INTRODUCTION
88
The program progresses from physical-aware Bell routing to mixed Bell/GHZ orchestration and finally to scenario-robust capacity deployment.
1
BELL ROUTING [1]
Route and store reliable EPR pairs.
2
BELL + GHZ [2]
Coordinate admission, fusion, and shared capacity.
3
PLANNING [3]
Deploy qubits and fiber before uncertain demand.
Three studies connect routing to planning
[1] Zhang, et al. "Efficient Entanglement Routing for Satellite-Aerial-Terrestrial Quantum Networks." IEEE ICCCN, 2025.
[2] Guo, et al. "Multipartite Entanglement Routing in Integrated Ground–Satellite Quantum Networks." IEEE ICCCN, 2026.
[3] Guo, et al. "Stochastic Infrastructure Planning for Entanglement Distribution in Integrated Terrestrial–Satellite Quantum Networks." under review.

## Slide 89
Efficient Entanglement Routing for Satellite-Aerial-Terrestrial Quantum Networks
Hybrid Satellite-Ground Quantum Networks and Computing
IEEE ICCCN 25
Yu Zhang, Yanmin Gong, Lei Fan, Yu Wang, Zhu Han, Yuanxiong Guo
Department of Information Systems and Cybersecurity · University of Texas at San Antonio
Department of Electrical and Computer Engineering · University of Houston
Department of Computer and Information Science · Temple University
How can Bell entanglement be routed reliably across a heterogeneous SATQN?

## Slide 90
Introduction
Bell Routing
Bell + GHZ
Planning
Conclusion
BELL ROUTING
90
Routing decisions are coupled across time
We have 𝐾 source-destination pairs of terrestrial base stations. Each pair is denoted by a tuple
Each pair requests quantum entanglement
Goal: Maximize SATQN throughput (i.e., end-to-end entanglement generation rate (EGR))

## Slide 91
Introduction
Bell Routing
Bell + GHZ
Planning
Conclusion
BELL ROUTING
91
Heterogeneity and time shape routing decisions
Heterogeneous network nodes
  Satellites.
  Aerial platforms such as HAPs or UAVs.
  Terrestrial base stations.
Time-indexed links
  The set and quality of feasible links can change over time.
Bell-pair demands
  There are source–destination pairs of terrestrial base stations.
Quantum storage
  A subset of network nodes can store EPR pairs, and each storage node has a finite capacity.
The problem couples route selection across heterogeneous layers with limited storage across time.

## Slide 92
Introduction
Bell Routing
Bell + GHZ
Planning
Conclusion
BELL ROUTING
92
Usable fidelity is determined by time-varying link transmittance, receiver efficiency, channel noise, and how those effects compose along a path.
1
LINK LOSS
Distance and atmosphere set link transmittance.
2
RECEIVER
Receiver efficiency scales the usable signal.
3
FIDELITY
Noise is compared with the ideal Bell state.
Link loss and noise determine path fidelity

## Slide 93
Introduction
Bell Routing
Bell + GHZ
Planning
Conclusion
BELL ROUTING
93
Swapping and purification set usable throughput
Imperfect entanglement swapping
  the end-to-end fidelity of pair 𝑘 along path 𝑝, which consists of links and nodes
  We utilize purification to increase the fidelity
fidelity parameters related with
required purification steps
success probability of step
source-destination pair target fidelity
Usable throughput depends on both how many Bell pairs are generated and whether they meet the target fidelity.
m=1

## Slide 94
Introduction
Bell Routing
Bell + GHZ
Planning
Conclusion
BELL ROUTING
94
Route, rate, and storage decisions are coupled
Decisions
  Decision 1 — Path selection : which path is selected for each demand and time interval
  Decision 2 — EGR allocation : how much entanglement generation rate is allocated
  Decision 3 — Stored EPR pairs : how many EPR pairs are retained at storage-capable nodes
Constrains groups
  Path selection: A valid path must be selected for each served demand.
  Channel capacity: Total EGR on a link cannot exceed its available capacity.
  Storage capacity: Stored EPR pairs cannot exceed node memory.
  Fidelity and purification: Delivered pairs must satisfy the target fidelity after accounting for purification.
  Flow and balance: Entanglement generation, storage, and consumption must remain consistent through the network and over time.
Problem statement
  Choose , , and together so that high-rate paths are also physically usable and supported by available channel and memory resources.

## Slide 95
Introduction
Bell Routing
Bell + GHZ
Planning
Conclusion
BELL ROUTING
95
Bell routing is a constrained mixed-integer model
– path selection
– EGR
– average number of EPR pairs storage
the aggregate weighted EGR across all user pairs, all path, and all time intervals
path selection constraints
storage and channel capacity constraints
fidelity and balance constraints

## Slide 96
Introduction
Bell Routing
Bell + GHZ
Planning
Conclusion
BELL ROUTING
96
A binary master chooses paths; a continuous subproblem allocates EGR and storage; cuts coordinate both layers until upper and lower bounds converge.
Benders decomposes routing and allocation
Fix the binary variables and construct the linear subproblem
Fix the continuous variables and construct the mix-integer linear master problem
Upper Bound
Lower Bound
Optimality and feasibility cuts
Binary variables
Problem P1

## Slide 97
Introduction
Bell Routing
Bell + GHZ
Planning
Conclusion
BELL ROUTING
97
We consider an SATQN consisting of 2 satellites, 2 HAPs, and 12 terrestrial base stations
Baselines
  Satellite-Only Scheme (SOS): All entanglement requests are managed by satellites
  Random Routing Scheme (RRS): EGR is optimized, while the routing path is randomly selected
  No-Storage Scheme (NSS): None of the nodes has storage capacity
Experiment design and benchmark policies

## Slide 98
Introduction
Bell Routing
Bell + GHZ
Planning
Conclusion
BELL ROUTING
98
Proposed scheme can better utilize the storage capacity
Proposed scheme has larger network throughput
Joint routing improves storage and throughput

## Slide 99
Introduction
Bell Routing
Bell + GHZ
Planning
Conclusion
BELL ROUTING
99
Reliable Bell-pair routing requires joint control of path selection, generation rate, fidelity, purification, and quantum memory.
This study serves pairwise Bell demands. Group applications require a shared multipartite state, which introduces coordinated fusion and multi-arm routing.
Bell routing coordinates the service chain

## Slide 100
Multipartite Entanglement Routing in Integrated Ground–Satellite Quantum Networks
Hybrid Satellite-Ground Quantum Networks and Computing
IEEE ICCCN 26
Xiangxing Guo, Yu Zhang, Yanmin Gong, Lei Fan, Yu Wang, Zhu Han, Yuanxiong Guo
Department of Information Systems and Cybersecurity · University of Texas at San Antonio
Department of Electrical and Computer Engineering · University of Houston
Department of Computer and Information Science · Temple University
How can one integrated network serve Bell and GHZ demands together?

## Slide 101
Introduction
Bell Routing
Bell + GHZ
Planning
Conclusion
BELL + GHZ
101
Bell and GHZ demands have different structures
Notations
  Demand sets
}
  Bell demand sets
  GHZ demand sets
Demand examples
  Bell demand : two terminals and
  Greenberger-Horne-Zeilinger (GHZ) demand : terminal set
i
j
one Bell-pair service
i
j
k
one shared multipartite service
The challenge is no longer only finding reliable paths; it is coordinating two entanglement services with different structures over one shared resource pool.

## Slide 102
Introduction
Bell Routing
Bell + GHZ
Planning
Conclusion
BELL + GHZ
102
One ground–satellite graph supports both services
Model
  Graph model with and
    : ground stations
    : satellite
    : fiber links
    : inter-satellite links
    and : uplink/downlink visibility links
We focus on a ground–satellite snapshot to isolate mixed-service routing and infrastructure-planning questions.

## Slide 103
Introduction
Bell Routing
Bell + GHZ
Planning
Conclusion
BELL + GHZ
103
Path choice trades reliability against resource use
Ground-only path
  Simple routing
  Bell swapping at intermediate GSs
  Consumes GS qubits and fiber channel
Satellite-assisted path
  Uses uplink, satellite hops, and downlink
  Visibility-dependent
  Consumes satellite lenses
Each path choice changes both success probability and resource consumption.

## Slide 104
Introduction
Bell Routing
Bell + GHZ
Planning
Conclusion
BELL + GHZ
104
GHZ fusion couples multiple Bell-routing problems
GHZ construction example
GHZ model
  Step 1: select a candidate fusion node
  Step 2: route induced Bell links to every terminal
  Step 3: perform GHZ fusion at the selected node
GHZ routing = fusion-node selection + multiple induced Bell-routing subproblems

## Slide 105
Introduction
Bell Routing
Bell + GHZ
Planning
Conclusion
BELL + GHZ
105
one λ must be feasible for every terminal branch
weakest induced Bell arms limits GHZ rate
fusion-node selection changes which branches are used
This is the main reason GHZ routing is harder than independent Bell routing.
f
v₁
branch 0.8
v₂
branch 0.5
v₃
branch 0.7
fusion node
The weakest branch limits GHZ throughput

## Slide 106
Introduction
Bell Routing
Bell + GHZ
Planning
Conclusion
BELL + GHZ
106
One model jointly serves Bell and GHZ demands
Given an integrated quantum network comprising a ground station network and a satellite network , with Bell demands , GHZ demands , candidate paths , and GS/SAT/fiber capacity limits, find a feasible routing plan to maximize the expected entanglement delivery and enforce GHZ service control.
Decision variables
  : whether to serve Bell demand
  : whether to serve GHZ demand
  : whether to select fusion node f for GHZ demand
  : how many attempts allocated to path

## Slide 107
Introduction
Bell Routing
Bell + GHZ
Planning
Conclusion
BELL + GHZ
107
Attempts, success, and bottlenecks set throughput
The expected throughput of is
  : the number of parallel path attempts on path
  : success probability of candidate path
The expected throughput of is
  : probability of GHZ-state fusion success
  : pre-fusion throughput at fusion node , which is bottlenecked by weakest arm

## Slide 108
Introduction
Bell Routing
Bell + GHZ
Planning
Conclusion
BELL + GHZ
108
Mixed Bell/GHZ routing problem
Objective: Maximize weighted expected entanglement throughput
Constraints
  Bell activation
  GHZ bottleneck
  GHZ activation
  GHZ serving guarantee

## Slide 109
Introduction
Bell Routing
Bell + GHZ
Planning
Conclusion
BELL + GHZ
109
Mixed Bell/GHZ routing problem
Resource Constraints
  GS qubits
  SAT lenses
  Fiber channels
Each includes all GHZ-induced Bell branches and Bell paths, so the two demand types compete for the same resources.

## Slide 110
Introduction
Bell Routing
Bell + GHZ
Planning
Conclusion
BELL + GHZ
110
The joint routing model is a solvable MILP
The final model is a Mixed-Integer Linear Programming (MILP) problem
  Binary variables: demand activation and fusion node selection
  Integer variables: number of path attempts
  Continuous variables: auxiliary variables to bound the throughputs
The routing problem can be solved by off-the-shelf optimizer

## Slide 111
Introduction
Bell Routing
Bell + GHZ
Planning
Conclusion
BELL + GHZ
111
Network
  17 ground stations, 10 orbital planes × 15 satellites=150 LEO satellites
Demands
  Random chosen from ground stations
  20 Bell demands + 20 GHZ demands
Resources
  4 qubits per GS, 4 fiber channel among GSs, 4 lenses per satellite
Baselines[1]
  Two-Step: coverage-first, then throughput
  FER: Greedy admission by expected throughput
  Q-PASS: FER with reliability-aware routing
  B1: Q-PASS with shortest-hop routing
Metric:
  Total expected throughputs
Evaluation setup and baselines
[1] Zeng, Yiming, et al. "Multi-entanglement routing design over quantum networks." Proc. of IEEE INFOCOM, 2022.

## Slide 112
Introduction
Bell Routing
Bell + GHZ
Planning
Conclusion
BELL + GHZ
112
Higher ε admits more GHZ service but consumes more shared resources.
ε controls the service-throughput tradeoff
Throughput–GHZ frontier
  Higher ε → more GHZ, lower throughput.
Admission behavior
  Bell service decreases as GHZ target rises.

## Slide 113
Introduction
Bell Routing
Bell + GHZ
Planning
Conclusion
BELL + GHZ
113
Satellites improve throughput across demand mixes
Different demand combinations
  The throughput–GHZ admission tradeoff persists under different Bell/GHZ demand combinations.
Satellite benefit
  Satellite-assisted paths increase throughput from 4.67 to 6.21.
Setting | Served Bell | Served GHZ | Throughput
Ours with satellite | 6.33 | 5.00 | 6.21
Ours without satellite | 5.67 | 5.00 | 4.67
The tradeoff is stable across different combinations, and satellites improve throughput.

## Slide 114
Introduction
Bell Routing
Bell + GHZ
Planning
Conclusion
BELL + GHZ
114
Mixed Bell/GHZ networking requires fusion-aware routing, balanced three-arm allocation, shared-resource coordination, and explicit GHZ service control.
Next question: what should be installed before that demand is known?
Mixed Bell/GHZ service needs fusion-aware control

## Slide 115
Stochastic Infrastructure Planning for Entanglement Distribution in Integrated Terrestrial–Satellite Quantum Networks
Hybrid Satellite-Ground Quantum Networks and Computing
Under Review
Xiangxing Guo, Yu Zhang, Yanmin Gong, Lei Fan, Yu Wang, Zhu Han, Yuanxiong Guo
Department of Information Systems and Cybersecurity · University of Texas at San Antonio
Department of Electrical and Computer Engineering · University of Houston
Department of Computer and Information Science · Temple University
What should be deployed before uncertain Bell/GHZ demand arrives?

## Slide 116
Introduction
Bell Routing
Bell + GHZ
Planning
Conclusion
PLANNING
116
Routing uses capacity after demand is known; planning decides where that capacity exists before demand arrives.
1
ROUTING
Choose paths and fusion nodes for current demand.
2
PLANNING
Deploy qubits and fiber for uncertain future demand.
3
IMPLICATION
Bad placement cannot be repaired by clever routing.
Routing reacts; planning positions capacity

## Slide 117
Introduction
Bell Routing
Bell + GHZ
Planning
Conclusion
PLANNING
117
1
BEFORE DEMAND
Choose one implementable capacity plan.
2
DEMAND REVEALED
Observe the realized Bell/GHZ scenario.
3
ROUTING RECOURSE
Adapt paths, fusion nodes, and allocations.
Two stages separate deployment and recourse
Deploy terrestrial qubits and fiber now; route Bell and GHZ demand after each scenario is revealed.

## Slide 118
Introduction
Bell Routing
Bell + GHZ
Planning
Conclusion
PLANNING
118
One deployment must serve every demand scenario
Stage 1: before demand
  Here-and-now infrastructure decisions
    Select fiber-edge capacity
    Select GS qubit capacity
    Subject to budget
Stage 2
  Demand uncertainty
  Each scenariowith probability
  Each scenario includes Bell and GHZ commodity sets and
  Each Bell commodity has a requested Bell pari rate
  Each GHZ commodity has requested GHZ state rate

## Slide 119
Introduction
Bell Routing
Bell + GHZ
Planning
Conclusion
PLANNING
119
Objective: Choose terrestrial qubit and link-capacity deployments before demand is known to maximize the expected weighted Bell-pair and GHZ throughput across future demand scenarios
Constraints
  First-stage deployment
    First-stage budget
    At most one configuration
Problem formulation

## Slide 120
Introduction
Bell Routing
Bell + GHZ
Planning
Conclusion
PLANNING
120
Constraints
  Second-stage
    Delivered throughput cannot exceed realized demand
    Path attempts become expected delivery through the path success probability
    All three arms must support the pre-fusion rate
    Bell paths and GHZ arms compete for channels, qubits, and satellite lenses
GHZ
Bell
Problem formulation (cont.)

## Slide 121
Introduction
Bell Routing
Bell + GHZ
Planning
Conclusion
PLANNING
121
Train on six scenarios; test on unseen demand
Network setup
  17 ground stations
  10 orbital planes × 15 satellites
  4 lenses per satellite; 5 candidate paths
Uncertain demand
  6 training scenarios: {Balanced/Bell-heavy/GHZ-heavy} {low intensity, medium intensity}
  Deployment is frozen after training → evaluated on 100 unseen demand scenarios
Baselines
  DET-Mean: Plan for average demand
  TSSP-Bell: Plan using Bell scenarios only
  TSSP-GHZ: Plan using GHZ scenarios only
  TSSP (ours): Plan jointly across Bell + GHZ scenarios
  Wait-and-See (Oracle): knows the test demand before deployment
Metric: Average weighted throughput over unseen scenarios

## Slide 122
Introduction
Bell Routing
Bell + GHZ
Planning
Conclusion
PLANNING
122
Main out-of-sample result
TSSP outperforms mean-demand planning and nearly reaches the oracle.
Stochastic planning nears the wait-and-see oracle

## Slide 123
Introduction
Bell Routing
Bell + GHZ
Planning
Conclusion
PLANNING
123
Deployment budget
Demand uncertainty
Stochastic planning is most valuable under tight budgets and remains robust as demand disperses.
Value rises under tight budgets and uncertainty

## Slide 124
Introduction
Bell Routing
Bell + GHZ
Planning
Conclusion
PLANNING
124
Stochastic planning places scarce terrestrial resources where they remain useful across future Bell/GHZ workloads, while scenario-dependent recourse adapts routing after demand is observed.
Stochastic deployment creates adaptable capacity

## Slide 125
Introduction
Bell Routing
Bell + GHZ
Planning
Conclusion
CONCLUSION
125
Three studies build a quantum control stack
Infrastructure determines feasible services; service decisions determine routing demand; routing reveals physical bottlenecks.
Layer | Main question | Study
Infrastructure planning | Which capacities should exist before uncertain demand? | Planning [3]
Service orchestration | How should Bell and GHZ demands share those capacities? | Bell + GHZ [2]
Physical-aware routing | How should Bell pairs be routed, purified, and stored? | Bell Routing [1]
[1] Y, Zhang, et al. "Efficient Entanglement Routing for Satellite-Aerial-Terrestrial Quantum Networks." IEEE ICCCN, 2025.
[2] X, Guo, et al. "Multipartite Entanglement Routing in Integrated Ground–Satellite Quantum Networks." IEEE ICCCN, 2026.
[3] X Guo, et al. "Stochastic Infrastructure Planning for Entanglement Distribution in Integrated Terrestrial–Satellite Quantum Networks." under review.

## Slide 126
Schedule of This Tutorial
1
Introduction to Hybrid Satellite-Ground Quantum Networks
Motivation, background, and overall system of satellite-ground QN
2
Hybrid Quantum-Classical Computing Framework
Key concepts and techniques used by hybrid QC computing to solve optimization problems
3
Entanglement Distribution in Hybrid Satellite-Ground Quantum Networks
How to use satellite to provide entanglement for ground quantum networks
4
Entanglement Routing in Hybrid Satellite-Ground Quantum Networks
How to routing entanglement in satellite-ground quantum networks
5
Distributed Quantum Computing via Hybrid Satellite-Ground Quantum Networks
How to support distributed quantum computing in hybrid quantum networks
126

## Slide 127
SECTION 5
Distributed Quantum Computing via Hybrid Satellite-Ground Quantum Networks
How to support distributed quantum computing in hybrid quantum networks
Hybrid Satellite-Ground Quantum Networks and Computing

## Slide 128
Outline
1
Introduction
Motivation and background
2
TACO: Topology-Allocation Co-Optimization for Distributed Quantum Computing
Co-design qubit allocation and network topology for entanglement generation, IEEE QCNC 2025 & IEEE TNET (under revision)
3
UNIQ: Communication-Efficient Distributed Quantum Computing
Joint optimization of qubit allocation, entanglement management and network scheduling, arXiv:2512.00401 & IEEE JSAC (under review)
4
Conclusion
Takeaways, open problems, and resources
4
128

## Slide 129
Introduction
TACO
UNIQ
Conclusion
INTRODUCTION
129
Quantum Computing
|0⟩ and |1⟩
0 and 1
Significant Advantage:
High Speed to solve large tasks
Classical Computers | Quantum Computers
Only be in one of two state 0 or 1 | Simultaneously in the superposition state
Classical Computers | Quantum Computers
Only be in one of two state 0 or 1 | 
Reason…
Quantum characteristics parallel computing
One state at a time
Many states at a time

## Slide 130
Introduction
TACO
UNIQ
Conclusion
INTRODUCTION
130
Qubits, Quantum Gates and Circuits
Quantum gates
Quantum States, Circuits, and Measurements
CNOT
(Controlled Not)
Hadamard
Pauli-Z
Pauli-X
Gate
Notation
Matrix
Quantum Circuits
Qubit
Example
X
State Input
Circuit
Classical Output
Measurement
0 or 1
q1
q2
q3
q4
X
H
Z
Expected Result
0: 40 times
1: 60 times
100 shots
Pauli Z
= ,

## Slide 131
Introduction
TACO
UNIQ
Conclusion
INTRODUCTION
131
Current Quantum Computers: The Qubit Limitation
Numbers of qubits for one QPU
Current State: Noise intermediate-scale quantum technology (NISQ)
Future State: Fully error corrected quantum computers with millions of qubits.
Limit qubits per QPU

## Slide 132
Introduction
TACO
UNIQ
Conclusion
INTRODUCTION
132
Why Scaling a Single QPU Is Difficult [1]
Hardware Noise
High error rates in quantum operations
Fabrication Difficulty
Large chips are hard to build
Control Complexity
Requires thousands of control lines
Difficult to build large quantum processors with millions of qubits
Limited Qubit Count
Large quantum circuits cannot be executed on a single device
Distributed Quantum Computing
Multiple QPUs are interconnected to collaboratively execute a large quantum circuit
Single QPU capacity:
5 qubits
DQC capacity (9 QPUs):
45 qubits
Task circuit: 45 qubits
[1] Zhou, R., Gan, Y., Liu, Y., & Qian, C. (2025, July). CloudQC: A network-aware framework for multi-tenant distributed quantum computing. In 2025 IEEE 45th International Conference on Distributed Computing Systems (ICDCS) (pp. 155-165). IEEE.

## Slide 133
Introduction
TACO
UNIQ
Conclusion
INTRODUCTION
133
DQC is a paradigm where multiple interconnected quantum processors (QPUs) work together to solve computational problems
  single QPUs have limited qubits and coherence times
  allowing resource sharing and enabling heterogeneous QC
  enabling large-scale quantum algorithms
Image Source: Caleffi et al., Distributed quantum computing: A survey, Elsevier Computer Networks, 2024
Distributed Quantum Computing (DQC)
https://research.cisco.com/quantum-research/quantum-data-center

## Slide 134
Introduction
TACO
UNIQ
Conclusion
INTRODUCTION
134
Key DQC Challenges
  Qubit allocation: Strategic distribution and management of qubits across multiple quantum nodes to optimize computation, entanglement distribution, and communication
  Entanglement generation and distribution: Reliable and long-distance entanglement with high fidelity is difficult due to decoherence and noise
  Quantum network topology: Optimizing the connections between quantum nodes for efficient computation is still an open problem
data qubit
quantum
link
QPU v1
QPU v2
comm. qubit
Quantum Network
v1
v2
v3
v4

## Slide 135
Introduction
TACO
UNIQ
Conclusion
INTRODUCTION
135
Putting DQC in Space
3
Extreme Cold Environment: reducing the massive cooling infrastructure needed on earth
Reduced Electromagnetic Interference (EMI): far from human-made radio frequency noise and electrical interference. This means lower decoherence rates
Global Coverage & Low Latency: a global quantum internet, distributing entangled particles to ground stations worldwide
Quantum Communication & Cryptography: truly unhackable global communication networks
Scientific Applications On-Site: process astronomical data, navigation, and simulations in real time
Boeing’s Q4S Mission
SPOQC Mission (UK)
IonQ & Skyloom Infrastructure
EAGLE-1 & SAGA (European Space Agency)
Micius (Mozi) Satellite (China)
SpaceX – AI Data Center in Space

## Slide 136
Co-design of Network Topology and Qubit Allocation for Distributed Quantum Computing
Hybrid Satellite-Ground Quantum Networks and Computing
IEEE QCNC· IEEE TNET
Jiyao Liu, Lei Fan, Yuanxiong Guo, Zhu Han, Yu Wang
Department of Computer and Information Science · Temple University
Department of Electrical and Computer Engineering · University of Houston
Department of Information Systems and Cybersecurity · University of Texas at San Antonio

## Slide 137
Introduction
TACO
UNIQ
Conclusion
TACO: Topology-Allocation Co-Optimization for Distributed Quantum Computing
137
Qubit Allocation in DQC
Qubit Interaction Graph G’(Q,C)
logical qubit
qubit allocation
q1
q5
number of CNOT gate operation between two logical qubits
q3
q4
q2
Quantum Network G(V,E)
v1
v2
v3
v4
final topology
2
1
1
1
2
Quantum Circuit
q1
q2
q3
q4
q5
Y
H
X
H
Qubit Allocation: strategic distribution & management of qubits for DQC across multiple quantum nodes to optimize performance
  Entangled qubits serve as a fundamental resource for DQC, enabling distributed quantum gates and teleportation-based communication
  Allocating qubits effectively requires balancing local processing (within a quantum node) and remote operations (across entangled nodes)
  Network topology affects entanglement fidelity—longer-distance entanglement swapping increases decoherence and reduces success rates.

## Slide 138
Introduction
TACO
UNIQ
Conclusion
TACO: Topology-Allocation Co-Optimization for Distributed Quantum Computing
138
Motivation and Contribution
Research Gaps
  Existing works focus on partitioning quantum circuits and minimizing teleportation but often consider simplified network conditions and entanglement availability
  Network-aware qubit allocation considers communication cost but lacks joint optimization with topology design
  Inspired by Mao et al. ICDCS 24
  Topology design in DQC, a meta-heuristic algorithm based on simulated annealing to find the near-optimal topology
  Do not explicitly model the swapping routing into the optimization problem, which makes their optimization problem challenging to solve
  Assumes entanglement paths follow the shortest path, restricting solution space and reducing optimality
Our Contribution
  We propose a co-design of network topology and qubit allocation, explicitly modeling entanglement paths, allowing for direct optimization via classical solvers
  We also develop heuristics from edge contraction in qubit interaction graph () to pre-assign groups of qubits to QPUs, ensuring that our method remains effective at scale

## Slide 139
Introduction
TACO
UNIQ
Conclusion
TACO: Topology-Allocation Co-Optimization for Distributed Quantum Computing
139
Motivation and Contribution
Research Gaps
  Existing works focus on partitioning quantum circuits and minimizing teleportation but often consider simplified network conditions and entanglement availability
  Network-aware qubit allocation considers communication cost but lacks joint optimization with topology design
  Inspired by Mao et al. ICDCS 24
  Topology design in DQC, a meta-heuristic algorithm based on simulated annealing to find the near-optimal topology
  Do not explicitly model the swapping routing into the optimization problem, which makes their optimization problem challenging to solve
  Assumes entanglement paths follow the shortest path, restricting solution space and reducing optimality
Our Contribution
  We propose a co-design of network topology and qubit allocation, explicitly modeling entanglement paths, allowing for direct optimization via classical solvers
  We also develop heuristics from edge contraction in qubit interaction graph to pre-assign groups of qubits to QPUs, ensuring that our method remains effective at scale

## Slide 140
Introduction
TACO
UNIQ
Conclusion
TACO: Topology-Allocation Co-Optimization for Distributed Quantum Computing
140
General Quantum Circuit
Quantum Circuit
q1
q2
q3
q4
q5
Y
H
X
H
Quantum circuits describe quantum algorithms
Single qubit gates + CNOT are universal
q1
q5
q4
q2
2
1
1
1
2
q3
Qubit Interaction Graph (QIG) captures all inter-qubit communications
Qubit Interaction Graph
logical qubit
number of CNOT gate operation between two logical qubits

## Slide 141
Introduction
TACO
UNIQ
Conclusion
TACO: Topology-Allocation Co-Optimization for Distributed Quantum Computing
141
Qubit Allocation – Qubit Mapping
Qubit Interaction Graph G’(Q,C)
qubit allocation
Quantum Network G(V,E)
v1
v2
v3
v4
final topology
q1
q5
q3
q4
q2
2
1
1
1
2
Exactly a graph partition problem, which is NP-hard
data qubit
quantum
link
QPU v1
QPU v2

## Slide 142
Introduction
TACO
UNIQ
Conclusion
TACO: Topology-Allocation Co-Optimization for Distributed Quantum Computing
142
Problem Formulation: Objective
Objective: minimizing the total communication costs among all QPUs (after assignment)
QPU pairs
communication between single QPU pair
single path cost
edge cost (e.g., distance)
whether edge (u, z) is included in the path between QPUs (i, j)
CNOT gate demand between qubits (a, b)
qubits (a, b) are assigned to QPUs (i, j)

## Slide 143
Introduction
TACO
UNIQ
Conclusion
TACO: Topology-Allocation Co-Optimization for Distributed Quantum Computing
143
Problem Formulation: Resource and Topology Constraints
1. Each qubit should be assigned to
exactly one QPU
2. Each QPU holds a limited number of qubits
Edge (u, z) is not used by any path
Qubit Allocation
Edge (u, z) is not used by the path between (i, j)
3. Each QPU connects to a limited number of edges
4. The total number of edges cannot exceed
Topology Sparsity

## Slide 144
Introduction
TACO
UNIQ
Conclusion
TACO: Topology-Allocation Co-Optimization for Distributed Quantum Computing
144
Problem Formulation: Entanglement Constraints
In degree - out degree for the destination node
In degree - out degree for middle nodes
In degree - out degree for the source node
5-7. Modified from the typical flow/path constraints
8. The length of each path should not exceed
Entanglement Path
Non-Linear Binary Programming

## Slide 145
Introduction
TACO
UNIQ
Conclusion
TACO: Topology-Allocation Co-Optimization for Distributed Quantum Computing
145
Formulation 1: Non-Linear Binary Programming

## Slide 146
Introduction
TACO
UNIQ
Conclusion
TACO: Topology-Allocation Co-Optimization for Distributed Quantum Computing
146
Partial Linearization
Edge Existence
Demand Existence
Reduce from to linear
Reduce from cubic to quadratic
All constraints reduced to at most quadratic (as it is unlikely to reduce to linear)
Objective is still cubic
: whether edge (u,z) is used
: there are communications between QPUs (i, j)

## Slide 147
Introduction
TACO
UNIQ
Conclusion
TACO: Topology-Allocation Co-Optimization for Distributed Quantum Computing
147
Formulation 2: Cubic Binary Programming

## Slide 148
Introduction
TACO
UNIQ
Conclusion
TACO: Topology-Allocation Co-Optimization for Distributed Quantum Computing
148
Simulation Results
TACO-L is the most efficient
TACO-NL performs worse than TACO, which means the latest automatic linearization feature of Gurobi should be used carefully
Larger circuit and quantum network lead to higher communication cost
Efficiency (Solving Time)
More computing resource leads to lower cost (more qubits are hold on the same QPU so fewer communications)
More communication resource leads to lower cost (denser graph - shorter paths so smaller communication overheads)
Computing & Communication Resources
Baselines | Description
TACO | Formulation 1, manually reduced to quadratic then solved by Gurobi
TACO-NL | Formulation 1, automatically solved by Gurobi
TACO-L | Formulation 2, automatically solved by Gurobi
Solving Methods
Topology-Allocation Co-Optimization
Circuit | Qubit # | CNOT #
adr4 | 14 | 1,498
clip | 14 | 14,772
co14 | 15 | 7,840
rand24 | 24 | 18,600
rand32 | 32 | 75,600
Quantum Circuits Used

## Slide 149
Introduction
TACO
UNIQ
Conclusion
TACO: Topology-Allocation Co-Optimization for Distributed Quantum Computing
149
Simulation Results
TACO-L is the most efficient
Larger circuit lead to higher communication cost
Can only solve up to 64 or 96 qubits within 300 seconds
Objective/Solving Time for larger circuits
Topology-Allocation Co-Optimization
Objective/Solving Time for more larger circuits
EC: edge contraction on QIG – greedy heuristic
KL: Kernighan-Lin graph partitioning of QIG
PA: Pre-assign via greedy heuristic
Can now solve up to 1024 qubits within seconds

## Slide 150
Introduction
TACO
UNIQ
Conclusion
TACO: Topology-Allocation Co-Optimization for Distributed Quantum Computing
150
Summary
DQC Problem:
  Jointly optimizing qubit allocation and network topology in distributed quantum computing
Problem Formulations:
  be able to explicitly jointly formulate qubit allocation and topology design in an integer nonlinear programming problem
  further partially linearize the original formulation so that it can be solved more efficient
Evaluations via Simulations:
  partially linearized formulation is efficient to solve
  more computing and communication resources lead to less communication cost
  can solve larger size of problem with edge contract and greedy pre-assignment

## Slide 151
UNIQ: Communication-Efficient Distributed Quantum Computing
Hybrid Satellite-Ground Quantum Networks and Computing
arXiv:2512.00401 · Manuscript submitted to IEEE JSAC
Department of Electrical and Computer Engineering · University of Houston
via Unified Nonlinear Integer Programming
Hui Zhong, Jiachen Shen, Lei Fan, Xinyue Zhang, Hao Wang, Miao Pan and Zhu Han

## Slide 152
Introduction
TACO
UNIQ
Conclusion
UNIQ: Communication-Efficient Distributed Quantum Computing
152
DQC Challenge: Long Execution Time [1]
Operation | Latency
Single-qubit gates | ~20 ns
Two-qubit gates | ~200 ns
Measurement | ~1 μs
EPR preparation | ~2 μs
Table 1. EPR generation time [1].
q1
q3
q2
q4
QPU 1
QPU 2
q4
QPU 1
QPU 2
c1
c3
EPR1
q1
q2
q3
q4
Remote gates is Time-consuming!
Each QPU capacity:
2 computing qubits
2 communication qubits
QPU 1
QPU 2
q1
q3
q4
q2
c1
c3
c2
c4
EPR generation process: probabilistic, loss-limited
EPR2
q2
q1
Remote gate: Across QPUs, pre-established communication channel
Local gate: Within one QPU
EPR pairs (Einstein–Podolsky–Rosen pairs):
Entangled qubit pairs shared between QPUs that enable quantum communication.
[1] Zhou, R., Gan, Y., Liu, Y., & Qian, C. (2025, July). CloudQC: A network-aware framework for multi-tenant distributed quantum computing. In 2025 IEEE 45th International Conference on Distributed Computing Systems (ICDCS) (pp. 155-165). IEEE.

## Slide 153
Introduction
TACO
UNIQ
Conclusion
UNIQ: Communication-Efficient Distributed Quantum Computing
153
The DQC Execution Workflow [1]
1. Qubit allocation
Split the circuit and assign logical qubits to QPUs.
2. Entanglement management
Create EPR pairs for remote CNOT gates across QPUs.
3. Network scheduling
Choose when gates and EPR generation happen under dependencies.
→
→
[1] Zhou, R., Gan, Y., Liu, Y., & Qian, C. (2025, July). CloudQC: A network-aware framework for multi-tenant distributed quantum computing. In 2025 IEEE 45th International Conference on Distributed Computing Systems (ICDCS) (pp. 155-165). IEEE.

## Slide 154
Introduction
TACO
UNIQ
Conclusion
UNIQ: Communication-Efficient Distributed Quantum Computing
154
Stage 1 — Qubit Allocation
1. Qubit allocation
2. Entanglement management
3. Network scheduling
→
→
q1
q2
q3
q4
The task circuit
q1
q2
q3
q4
QPU A
QPU B
QPU A
QPU B
Each QPU
Computing qubits: 2 Communication qubits: 1
q1
q3
q2
q4
QPU A
QPU B
Save time!
Qubit allocation: Minimize the number of remote gates
QPU A
QPU B
q1
q2
q3
q4
QPU A
QPU B
q1
q3
q2
q4
5 EPR
2 EPR

## Slide 155
Introduction
TACO
UNIQ
Conclusion
UNIQ: Communication-Efficient Distributed Quantum Computing
155
Stage 2 — Entanglement Management
1. Qubit allocation
2. Entanglement management
3. Network scheduling
→
→
q1
q3
q2
q4
QPU A
QPU B
Entanglement management:
Establish an EPR pair through communication qubits, which serves as a channel for information transmission.
QPU A
QPU B
q1
q3
q2
q4
Each QPU
Computing qubits: 2 Communication qubits: 1
q1
q3
q2
q4
QPU A
QPU B
EPR 1
EPR 2
QPU A
QPU B
q1
q2
q3
q4
c1
c2
c1
c2

## Slide 156
Introduction
TACO
UNIQ
Conclusion
UNIQ: Communication-Efficient Distributed Quantum Computing
156
Stage 3 — Network Scheduling
1. Qubit allocation
2. Entanglement management
3. Network scheduling
→
→
Network Scheduling:
Remote gates without qubit overlap can be parallel execution; otherwise, executed sequentially.
QPU A
QPU B
q1
q3
q2
q4
Each QPU
Computing qubits: 2 Communication qubits: 1
q1
q3
q2
q4
QPU A
QPU B
EPR
EPR
c1
c2
Remote gate 1
Remote gate 2
q1
q3
q2
q4
QPU A
QPU B
EPR
EPR
c1
c2
Remote gate 1
Remote gate 2

## Slide 157
Introduction
TACO
UNIQ
Conclusion
157
State of the Art and Its Limitation [1]
STOA [1]:
Qubit allocation: graph partitioning to minimize remote gates
Network scheduling: priority-based scheduling
QPU A
QPU B
q1
q3
q4
q2
q1
q3
q2
q4
QPU A
QPU B
q1
q2
q4
QPU A
QPU B
c1
c2
c3
c4
EPR1
EPR2
c1
c2
c3
c4
Disadvantage:
Process each step sequentially and independently
Parallel gate execution is not considered.
Operation | Latency
Single-qubit gates | ~20 ns
Two-qubit gates | ~200 ns
Measurement | ~1 μs
EPR preparation | ~2 μs
2μs
200ns
2μs
200ns
Total time 4μs
Table 1. EPR generation time [1].
1. Qubit allocation
3. Network scheduling
→
→
[1] Zhou, R., Gan, Y., Liu, Y., & Qian, C. (2025, July). CloudQC: A network-aware framework for multi-tenant distributed quantum computing. In 2025 IEEE 45th International Conference on Distributed Computing Systems (ICDCS) (pp. 155-165). IEEE.
2. Entanglement management

## Slide 158
Introduction
TACO
UNIQ
Conclusion
158
State of the Art and Its Limitation [2]
1. Qubit allocation
2. Entanglement management
3. Network scheduling
→
→
[2] Wu, A., Zhang, H., Li, G., Shabani, A., Xie, Y., & Ding, Y. (2022, October). Autocomm: A framework for enabling efficient communication in distributed quantum programs. In 2022 55th IEEE/ACM International Symposium on Microarchitecture (MICRO) (pp. 1027-1041). IEEE.
STOA [2]:
Generate EPR pairs in parallel to save execution time
Ours:
Formulate the joint optimization of 3 steps as a Nonlinear Integer Programming (NIP) problem
Generate EPR in parallel; A generalizable framework for arbitrary networks, easy to scale up
q1
q2
q4
QPU A
QPU B
c1
c2
c3
c4
EPR1
EPR2
q1
q2
q4
QPU A
QPU B
c1
c2
c3
c4
EPR 1 EPR 2
Disadvantage:
Process each step independently
The design is highly architecture-dependent, requiring circuit-by-circuit analysis
2μs
200ns
2μs
200ns
2μs
200ns
200ns
Total time 4μs
Total time 2μs
Save Time
QPU A
QPU B
q1
q3
q4
q2
c1
c3
c2
c4
QPU A
QPU B
q1
q3
q4
q2
c1
c3
c2
c4
QPU A
QPU B
q1
q3
q4
q2
c1
c3
c2
c4
Circuit by circuit!

## Slide 159
Introduction
TACO
UNIQ
Conclusion
UNIQ: Communication-Efficient Distributed Quantum Computing
159
State of the Art and Its Limitation [2]
Autocomm: circuit-by-circuit optimization [2]
Circuit 1:
Circuit 2:
Circuit rewriting rules for parallel EPR preparation
Circuit…
Rule-based, Circuit-by-circuit optimization
Limited generalizability and scalability
…
Our work: one generalizable and scalable solution
Circuit 1:
Circuit 2:
Circuit…
One generalizable and scalable solution
A unified mathematical way
Formulate as a unified optimization problem
Design an algorithmic solution
Generate execution plans for arbitrary circuits
Applicable to arbitrary circuits
[2] Wu, A., Zhang, H., Li, G., Shabani, A., Xie, Y., & Ding, Y. (2022, October). Autocomm: A framework for enabling efficient communication in distributed quantum programs. In 2022 55th IEEE/ACM International Symposium on Microarchitecture (MICRO) (pp. 1027-1041). IEEE.

## Slide 160
Introduction
TACO
UNIQ
Conclusion
UNIQ: Communication-Efficient Distributed Quantum Computing
160
Mathematical Formulation (1/3)
Objective Function:
Minimize the total execution time
Minimize the communication cost
QPU A
QPU B
q1
q3
q4
q2
Each QPU
Computing qubits: 2
Communication qubits: 2
q1
q2
q3
q4
q1
q3
q2
q4
QPU A
QPU B
q1
q3
q2
q4
QPU A
QPU B
c1
c3
c2
c4

## Slide 161
Introduction
TACO
UNIQ
Conclusion
UNIQ: Communication-Efficient Distributed Quantum Computing
161
Mathematical Formulation (1/3)
Objective Function:
Minimize the total execution time
Minimize the communication cost
a) Mapping Validity:
Each logical qubit q must be assigned to exactly one QPU u.
QPU A
QPU B
q1
q3
q4
q2
b) QPU Capacity:
The number of allocated qubits q on a QPU u cannot exceed its capacity.
Each QPU
Computing qubits: 2
Communication qubits: 2
q1
q2
q3
q4
q1
q3
q2
q4
QPU A
QPU B
c) Gate Scheduling:
Each gate g must be and can only be assigned an exact time slot t.
q1
q3
q2
q4
QPU A
QPU B
c1
c3
c2
c4

## Slide 162
Introduction
TACO
UNIQ
Conclusion
UNIQ: Communication-Efficient Distributed Quantum Computing
162
Mathematical Formulation (2/3)
Objective Function:
Minimize the total execution time
Minimize the communication cost
d) Same-QPU Indicator:
Whether the two qubits of CNOT gate g = () reside on different QPUs.
If = 0, it means that the gate g is local gate
e) EPR Generation Requirement:
The execution of a remote gate ( = 1) strictly demands the consumption of an EPR entangled pair ( = 1)
f) EPR Before Execution Ordering:
The EPR pair for the remote gate g must be generated before the gate is executed.
q1
q3
q2
q4
QPU A
QPU B
q1
q3
q2
q4
QPU A
QPU B
QPU A
QPU B
q1
q3
q4
q2
c1
c3
c2
c4
EPR
EPR

## Slide 163
Introduction
TACO
UNIQ
Conclusion
UNIQ: Communication-Efficient Distributed Quantum Computing
163
Mathematical Formulation (3/3)
q3
c2
c4
Objective Function:
Minimize the total execution time
Minimize the communication cost
g) Precedence:
h) Undirected Mapping Indicator:
i) Concurrent EPR Generation and Inventory:
If two CNOT gates have qubit overlap, then they have execution order.
A dummy variable indicates whether gate g spans QPUs u and v.
EPR pairs can be stored and used, subject to inventory limits.
q1
q3
q2
q4
q1
q3
q2
q4
QPU A
QPU B
QPU A
QPU B
NP hard problem!

## Slide 164
Introduction
TACO
UNIQ
Conclusion
UNIQ: Communication-Efficient Distributed Quantum Computing
164
Algorithm: A Two-Stage Heuristic
DQC stages
Allocation, EPR management, Scheduling are interdependent
Unified NIP
Jointly optimize runtime and communication cost
Hard to solve
Greedy Mapping + JIT Scheduling
Decompose into mapping and scheduling decisions
Exact solving is computationally prohibitive
What is Mapping?
Placement determines whether a CNOT gate is local or remote.
Mapping is the spatial decision that reduces communication cost.
Map qubits with strong interaction weights in same QPU
Fewer remote gates ----- Less EPR demand
q1
q2
q3
q4
QPU 1
QPU 2
q1
q3
q2
q4
Strong interaction
What is Just in Time (JIT) Scheduling?
Gates and EPR pairs must satisfy precedence and communication qubit budgets over time.
Scheduling determines when to execute each gate to finish the circuit as early as possible.
Schedule each gate in earliest feasible slot
Generate EPR pairs in slot or earlier when beneficial
q1
q2
q4
QPU A
QPU B
c1
c2
c3
c4
EPR 1 EPR 2
Input: circuit + QPU topology + capacities
Stage 1: greedily map qubits using interaction weights
Stage 2: schedule gates in earliest feasible slots; pre-build EPR pairs
Output: a feasible execution plan with lower runtime and communication cost

## Slide 165
Introduction
TACO
UNIQ
Conclusion
UNIQ: Communication-Efficient Distributed Quantum Computing
165
Evaluation Setting
1) Implementation
A lightweight discrete–event simulator in Python
Quantum circuits: Qiskit package
Table 2. Characteristics of user-defined circuits.
3) Evaluation Metrics
circuit runtime, algorithm execution time, the objective value defined in Eq. (1), and EPR pairs utilization
minimize the first three metrics
maximize EPR pairs utilization
Table 3. Characteristics of real-world quantum circuits.
2) Circuits Settings
Circuits with four different scales
Real-world quantum circuits
4) Baseline Methods
Simulated annealing: heuristic global optimization
Random: random mapping
Average: average over random trials
CloudQC [1]
[1] Zhou, R., Gan, Y., Liu, Y., & Qian, C. (2025, July). CloudQC: A network-aware framework for multi-tenant distributed quantum computing. In 2025 IEEE 45th International Conference on Distributed Computing Systems (ICDCS) (pp. 155-165). IEEE.

## Slide 166
Introduction
TACO
UNIQ
Conclusion
UNIQ: Communication-Efficient Distributed Quantum Computing
166
Representative Example
Fig 2. Comparison with our method and Random Scheduling.
At time slot 1, most gates are executed.
(15 local gates, 14 remote gates)
It only takes 5 time slots to complete the entire circuit.
In the preceding periods, the available resources were being fully utilized.
At time slot 1, a small number of gates are executed.
(4 remote gates)
It takes 13 time slots to complete the entire circuit.
Fig 3. Communication qubit utilization in our method.
Overall, our method significantly reduces circuit execution time and achieves high communication resource utilization.

## Slide 167
Introduction
TACO
UNIQ
Conclusion
UNIQ: Communication-Efficient Distributed Quantum Computing
167
Different User-Defined Circuits
Table 2. Characteristics of user-defined circuits.
Fig 4. Comparison of our method with existing methods
Achieves the lowest objective value, indicating the shortest circuit runtime.
The algorithm execution time of our method is acceptable.

## Slide 168
Introduction
TACO
UNIQ
Conclusion
UNIQ: Communication-Efficient Distributed Quantum Computing
168
Hybrid Satellite-Ground Quantum Networks and Computing | QCE ’26
Framework Comparison with CloudQC
Fig 5. Comparison with CloudQC [1].
UNIQ can further reduce communication cost and execution time.
The shorter circuit runtime than CloudQC [1].
Achieves the lowest objective value, indicating the shorter circuit runtime.
The algorithm execution time of our method is shorter.
[1] Zhou, R., Gan, Y., Liu, Y., & Qian, C. (2025, July). CloudQC: A network-aware framework for multi-tenant distributed quantum computing. In 2025 IEEE 45th International Conference on Distributed Computing Systems (ICDCS) (pp. 155-165). IEEE.

## Slide 169
Introduction
TACO
UNIQ
Conclusion
UNIQ: Communication-Efficient Distributed Quantum Computing
169
Summary and Next Steps
Summary:
Jointly optimize DQC execution workflows
Formulate DQC optimization as a unified nonlinear integer programming problem
Reduce circuit execution time through parallel EPR generation
Next Step:
Probabilistic EPR generation and fidelity-aware scheduling
Resource-constrained quantum data-center topology design
Learning-based scheduling policies warm-started by UNIQ
UNIQ: Unified optimization
Allocation
Entanglement
Scheduling

## Slide 170
Introduction
TACO
UNIQ
Conclusion
CONCLUSION
170
Conclusion
DQC is a new paradigm where multiple interconnected quantum processors (QPUs) work together to solve computational problems beyond the current QPU limitation
Hybrid satellite-ground quantum networks provide an infrastructure to support DQC in the space
  Global coverage, low latency
  High security, easier cooling, reduced EM interference
Such space DQC can support many new applications
However, there are many challenging DQC optimizations
  Joint qubit allocation and network topology (focusing on entanglement distribution cost for remote gate over quantum networks)
  Jointly optimize DQC execution workflows (qubit allocation, entanglement management and gate scheduling)
  More to be studied and hybrid quantum-classical framework may be helpful.

## Slide 171
References
[1] Z. Zhao, L. Fan and Z. Han. "Hybrid quantum benders’ decomposition for mixed-integer linear programming." in Proc. Of WCNC, 2022
[2] Z. Zhao, M. Li, L. Fan and Z. Han, "HQC-Bend: A Python Package of Hybrid Quantum-Classical Multi-cuts Benders’ Decomposition Algorithm,” in Proc. of QCNC, 2025
[3] X. Wei, , J. Liu, L. Fan, Y. Guo, Z. Han, and Y. Wang, "Hybrid quantum-classical computing via Dantzig-Wolfe decomposition for integer linear programming." In ICCCN, 2024.
[4] X. Wei, J. Liu, L. Fan, Y. Guo, Y. Gong, Z. Han, and Y. Wang, “Quantum-Assisted Resource Management for Data Access in Space-Air-Terrestrial Integrated Networks”, IEEE TWC, Volume: 25, Pages: 5127-5140, 2026
[5] X. Wei, J. Liu, L. Fan, Y. Guo, Z. Han, and Y. Wang, “Optimal entanglement distribution problem in satellite-based quantum networks,” IEEE Network, vol. 39, no. 1, pp. 97–103, 2025.
[6] X. Wei, L. Fan, Y. Guo, Z. Han, and Y. Wang, “Entanglement from sky: Optimizing satellite-based entanglement distribution for quantum networks,” IEEE/ACM TON, vol. 32, no. 6, pp. 5295–5309, 2024.
[7] Y. Zhang, Y. Gong, L. Fan, Y. Wang, Z. Han, and Y. Guo, “Efficient entanglement routing for satellite-aerial-terrestrial quantum networks,” in Proc. of ICCCN, 2025.
[8] X Guo, Y. Zhang, L. Fan, Y. Wang, Z. Han, Y. Gong, and Y. Guo, Multipartite Entanglement Routing in the Integrated Ground-Satellite Quantum Networks, in Proc. of ICCCN, 2026
[9] X Guo, Y. Zhang, L. Fan, Y. Wang, Z. Han, Y. Gong, and Y. Guo "Stochastic Infrastructure Planning for Entanglement Distribution in Integrated Terrestrial–Satellite Quantum Networks." under review.
[10] J. Liu, L. Fan, Y. Guo, Z. Han, and Y. Wang, “Co-design of network topology and qubit allocation for distributed quantum computing,” in Proc. of QCNC, 2025. Extended version to appear TNET.
[11] H. Zhong, J. Shen, L. Fan, X. Zhang, H. Wang, M. Pan, and Z. Han, “Uniq: Communication-efficient distributed quantum computing via unified nonlinear integer programming,” 2025. [Online]. Available: https://arxiv.org/abs/2512.00401
Sec 2
Sec 3
Sec 4
Sec 5

## Slide 172
Thank You & Questions
Lei Fan, Yuanxiong Guo, Yu Wang and Zhu Han
lfan8,zhan2@uh.edu, · yuanxiong.guo@utsa.edu, wangyu@temple.edu Lab / Group Website · https://sites.google.com/view/lorelab/home, https://guoyuanxiong.github.io/, https://cis.temple.edu/~yu/wanglab/ and https://wireless.egr.uh.edu/
Quantum